## SIU GLAT2524  NCR Report

| Request ID | Item Description | Serial # | Description of NonConformance | Disposition | Work Performed | Status |
| --- | --- | --- | --- | --- | --- | --- |
| 00636 | Back plane assy EPU/SIU | GLAT 2418, 2419, 2420 | Reject No. 1 found at the vendors: 1. S/N GLAT 2419 (1-5); GLAT 2418 (2-1) ; GLAT 2420 (1-4) ; Vendor has applied red arrows to multiple areas though out the back side / solder side of the PWB?s that exhibited excessive solder. 2. Is: SLAC personnel gave verbal direction to the vendor not to perform the rework and route pwbs to SLAC. S/B: NCR should have been generated prior to release of product to SLAC. 3. S/N GLAT 2419 Connector center key damaged. Loc= row 1 conn #4 (view attachments) 4. S/N GLAT 2418 Connector pins slightly bent. Loc = Row 2 Conn # 1, Row 3 Conn # 1. | 1. Rework 2. Doc. Change 3. UAI 4. Rework | #1 Excess solder removed from surface. #2 This NCR was created. #3 UAI #4 Bent pins straighten with tweezers. | CLOSED |
| 00660 | EPU/SIU Back Plane PWB | SEE BELOW | Flight PWBS S/N's 1-1, 1-2, 1-3, 1-5, 1-6, 2-1, 2-2, 2-3, 2-4, 2-6, 3-1, 3-2, 3-3, 3-6, 4-1, 5-1, 5-4, 5-6 Total Qty 18 During the coupon evaluation Goddard made an observation that after thermal stress was performed on the coupon sample, not every hole was filled with solder, which might indicate solderability problems. Ref: EC50503 also View attachments | Scrap | Boards segregated and stored in MRB cabinet | CLOSED |
| 00664 | Back Plane SIU-EPU | GLAT 2418 | 1. SN GLAT2418, X-Rays exhibited plated through holes partially filled with solder causing voids on one side of the barrel. L= X2J1-23B and X2-J5-5A. (View attachments) | Rework | Touch up complete Per WO #1580. SLAC/GSFC MRB accepted x-rays of reworked pins | CLOSED |
| 00701 | SIB CCA | GLAT2210 | Problem # 1: Solder in the bend radius of U8 and U7. Problem # 2: U27 and U28 not installed flush against the board. Problem # 3: Excessive solder at U61. Problem # 4: Poor wetting of solder at J3 pins. (10/25/05 yc liew) After X-rays Problem # 5. Insufficient solder at pin J4.D9 | Probs 1,2,3,5: Rework Prob 4: UAI | #1 Removed Solder. #2 UAI #3 Removed excessive solder. #4UAI #5 Touched up per WO #1728 | CLOSED |
| 00715 | Back Plane CCA | GLAT 2418, GLAT 2416 | 1. B/plane CCA's were Re Xayed and found GLAT 2418, X3-P1-E7, X1-P2-B6; GLAT 2416 , X3-P4- D20, X3-P5-A19, X4-P4-C23; barrel fillet less than 75 %. | Rework | SLAC/GSFC MRB accepted x-rays of reworked pins on GLAT 2418 (this board is used in SIU GLAT2524); review still pending for GLAT2416 | CLOSED CLOSED |
| 00721 | EPU/SIU Back Plane Assy | GLAT 2431 | 1. Flux residue at the base of the connectors L= Rows 1 and 4 2. Flux residue along the edges of the CCA 3. J2 Connector epoxy on the face of the matting connector 4. J5 Foreign Material through out the entire connector, base of the connector (blue grommet) 5. Some type of yellow substance is either embedded or has seeped under the conformal coat. L= Back side of CCA along the sides of where the harness assembly is installed. View Picture. | Rework | #1, #2 returned CCA to vendor to rework to print. #3 remove excess epoxy per WO #1752. #4, #5 rework to print. (#5 with vendors proposal). | CLOSED |
| 00722 | GLAT2242 and All CPS CCA | CPS GLAT2242 | Redline change to LAT-TD-01673-03, page 55, step 5.4.1-22 Ripple voltage: Measured 122 mV req IS: < 100 mV req SB: redline to < 150 mV Error was never changed during Engineering model testing, and will only require a redline change to the doc per Dave N. instructions. | Documentation Change | LAT-DOC revised from -03 to -04 | CLOSED |
| 00725 | LCB CCA | GLAT 2230 | 1. Shock monitors tripped during transportation 1ea 100G X-Axes, 2ea 50 G, and 2ea 25 G. (11-10-05 er) 2. SN GLAT 2230, X-Rays exhibited plated through holes partially filled less then 75% barrel filled. L= J1-D9, J1-B20, J4-C17, J4-B18, J4-C21, 5plcs 3. (11-17-05 er) The x-rays that were taken on Nov 10 found that two plated throuh holes were partially filled less then 75% barrel filled L= J1-B20 and J4-C17. | Prob 1: UAI Prob 2,3: Rework | #1 Inspection: no damages to packing and CCA #2, #3 Touched up solder joints per WO #1764. SLAC/GSFC MRB accepted x-rays of reworked pins | CLOSED |
| 00733 | EEPROM used for SIB boards |  | 1) Life test of parts is in progress Part is at risk for application as EEPROM is not fully qualified. 2) QTY = 2 EEPROMs from DLC 0532 showed failure at low temperature during qualification life testing of EEPROM lot by vendor (Austin). SIB CCAs GLAT2210, GLAT221, GLAT2212 use EEPROMs from DLC 0532. | Use As Is | Regular and further life tests completed. GSFC accepted parts for use. | CLOSED |
| 00737 | RAD 750 CCA | F013 | 1. J2 side of connector melted. 2. Silver material mix in and on top of the conformal coat, L= Top and Bottom side of the CCA, view area?s of U12, U10, U8 View attachments 3. White contamination on top of conformal coat L=U12 4. Flux residue under the conformal coat Back side of CCA L= C55, 2ea connector joints, C4, C58, View attachments for locations | Rework | Removed white particulates with alcohol. The particulates were on top on conformal coat. All rework documented on WO #1790. QA re-inspected and accepted. | CLOSED |
| 00738 | CPS EPI/SIU Power Supply | GLAT 2243, GLAT 2234 | 1. X-Rays exhibited plated through holes partially filled less then 75% barrel filled. GLAT 2243, L= J5-D20; GLAT 2234 L= J4-B2, J4-B22. | Rework | Touched up solder joints per WO #1724. SLAC/GSFC MRB accepted x-rays of reworked pins | CLOSED |
| 00739 | LCB CCA | GLAT 2232 | 1. SN GLAT 2232 X-Rays exhibited plated through holes partially filled less then 75% barrel filled. L= J4-C3, J4-C7, J4-C10, J4-B24, J5-A5, J5-A7, J5-A19, J5-A20, J5-A21, J5-A22, 10plcs 2. (11-17-05 er) The x-rays that were taken on Nov 10 found that two plated throuh holes were partially filled less then 75% barrel filled L=J4-C7 and J4-C1 | Rework | #1 and #2 Touched up solder joints per WO #1766. . SLAC/GSFC MRB accepted x-rays of reworked pins | CLOSED |
| 00746 | SIB EEPROMs | GLAT 2210, 2211, 2212, 2213 | During SIB board testing at Silver Engineering, anomaly with data write to EEPROMs was observed on GLAT2210, 2211, 2212, 2213 SIBs. See Silver Engineering report summary, attachment 1. | None | Silver engineering duplicated anomaly on EM board | CLOSED |
| 00771 | SIU GLAT 2524, T/V test | GLAT 2524 | During T/V testing of SIU GLAT 2524, the following event error was reported: 'EventTest' evtTest error: ERROR (t=4442.280046): 1 Missed Events detected. |  |  | CLOSED |

12/7/05