## TEM/TPS NCR Report

| NCR | Item Description | Serial # | Description of NonConformance | Disposition | Work Performed | Status |
| --- | --- | --- | --- | --- | --- | --- |
| 00299 | TEM Box Assy | All | IS: TEM Box have incorrect connector reference designators. S.B.: TEM box base drawing LAT-DS-00554 should show correct reference designators. | Rework | Used Brady labels with kapton tape overlay to remark ref. designators to revised drawing | CLOSED |
| 00348 | TEM/TPS GLAT 1753 | All | IS: During T/V test of GLAT 1753, Tracker bias 1 and 0 voltage and Tracker Bias current are out of tolerance during hot thermal cycle performance testing per LAT-TD-03631-04. Measured Bias 1 voltage ranged from 133.2 to 135.58 V, measured Bias 0 voltage ranged from 117.4 - 119.49 V, measured Bias current was 0.0029A during 4 hot soak temperature testing. Ambient and cold temperature soak testing was OK. S.B.: Within ranges specified in performance test procedure LAT-TD-04085 rev. 3. Bias 1 voltage range is 145 - 165 V, Bias 0 voltage range is 130 - 150 V, Bias current range is 0.0030 - 0.0045 A | Documentation Change | MRB concurred to change range of TKR Bias voltages and current in LAT-TD-03631. | CLOSED |
| 00367 | TEM/TPS Qual model GLAT 1754 | GLAT 1754 | IS: TEM power supply current value that is read back via the sensors are out of tolerance as measured during performance testing per LAT-TD-04085 rev 3 following EMI testing and prior to T/V testing. Problem is not with the TPS current but with the on-board monitoring of current. S.B.: Within tolerance | Rework |  | CLOSED |
| 00370 | TEM/TPS Qual model GLAT 1754 | GLAT 1754 | IS: Comprehensive Performance Test (CPT) per LAT-TD-04085 was not performed during first cold cycle of qual level T/V test S.B.: First cold soak of T/V cycle should include CPT following an additional 4 hour soak at -40 C per LAT-TD-03631 sec. 5.3.3.9 | Use-as-is | MRB concurred to proceed with T/V test. | CLOSED |
| 00384 | Pressure sensor for T/V chamber, TEM/TPS Qual model GLAT 1754 | GLAT 1754 | IS: Erratic readings for T/V chamber pressure observed. Chamber pressure sensor or sensor controller suspect S.B.: Steady pressure readings | Rework | MRB concurred to repress chamber and replace faulty sensor with new one; proceeded with T/V test | CLOSED |
| 00397 | TEM/TPS Package | GLAT1752,1753, 1754 | Issue: Oscillation of CAL-3.3V Digital when TEM/TPS tester board is connected. Amplitude around 100mV, 1-2KHz frequency. Oscillation is triggered at power-on of calorimeter and sustained. No oscillation is present when turning the power on at cold tempeartures (-40C). At room-temperature oscillation might or might not be triggered by power-on. At hot temperatures (+50C) oscillation was always triggered at power-on. | Rework | MRB concurred with TPS board design changes. Design change was verified on TPS from GLAT 1754 (Qual). All TPS boards to be reworked per revised CCA drawing. TPS units on GLAT 1752 and GLAT 1753 installed in GRID t obe removed and reworked per NCR | OPEN Pending Systems Engineeringapproval of technical memo from ELX defining TEM/TPS power on conditions to avoid initiating oscillations |

7/19/05