## TEM/TPS NCR Report

| NCR | Item Description | Serial # | Description of NonConformance | Disposition | Work Performed | Status |
| --- | --- | --- | --- | --- | --- | --- |
| 00299 | TEM Box Assy | All | IS: TEM Box have incorrect connector reference designators. S.B.: TEM box base drawing LAT-DS-00554 should show correct reference designators. | Rework | Used Brady labels with kapton tape overlay to remark ref. designators to revised drawing | CLOSED |
| 00348 | TEM/TPS GLAT 1753 | All | IS: During T/V test of GLAT 1753, Tracker bias 1 and 0 voltage and Tracker Bias current are out of tolerance during hot thermal cycle performance testing per LAT-TD-03631-04. Measured Bias 1 voltage ranged from 133.2 to 135.58 V, measured Bias 0 voltage ranged from 117.4 - 119.49 V, measured Bias current was 0.0029A during 4 hot soak temperature testing. Ambient and cold temperature soak testing was OK. S.B.: Within ranges specified in performance test procedure LAT-TD-04085 rev. 3. Bias 1 voltage range is 145 - 165 V, Bias 0 voltage range is 130 - 150 V, Bias current range is 0.0030 - 0.0045 A | Documentation Change | MRB concurred to change range of TKR Bias voltages and current in LAT-TD-03631. | CLOSED |
| 00436 | TEM and TPS CCAs | GT104 thru GT122 | IS: Arathane 5750 A/B used by vendor (General Technologies) to conformal coat TEM and TPS CCAs has shelf life that expired on 3 April 2005 S.B.: Shelf life not expired | Documentation Change | MUA #003 approved by GSFC to extend shelf life three months; GT received new material in June 2005 | CLOSED |
| 00488 | TPS, CCA | GLAT1785 GLAT1786 | Discrepancy occurred during rework at SLAC. Ref W/O 872 1. S/Ns GT116, GT115 both units wire staking was applied inside the radius of the bends. 2. S/N GT115, R103, R140 capacitors are not flush to PWB due to excessive amount of staking compound. 3. No hardness test coupon for epoxy staking | 1. Use-as-is 2. Use-as-is 3. Use-as-is | Rework would risk board damage. Visual inspection of reworked TPS showed full cure of epoxy staking | CLOSED |
| 00511 | TPS, CCA | GLAT 1779, 1781, 1782, 1785, 1790, 1792, | IS: Procedure LAT-TD-01652-05, external power supply current is 0.158 amp SB: 0.16 - 0.21 amp | Document Change | Observed and dispositioned previously on NCR 469 | OPEN Pending revision of TD-01652 to change tolerance |
| 00525 | TPS SVT | GLAT 1785 (GT 115) | IS: Per LAT-TD-04098-02, External power supply current readout is 23 m Amps SB: +26.5 - +29.5 m Amps | Documentation Change | Dispositioned by Dave Nelson to increase allowable power supply current range | OPEN Pending revision of TD-04098 to change tolerance |
| 00526 | TPS CCA | GLAT 1785 (GT 115) | IS: Operations 120 & 130 in AIDS to update Mate/Demate Log is missing. SB: Not this condition. | Document change | Mate/demate logs updated | CLOSED |
| 00545 | TEM/TPS assy | see below | IS: TEM/TPS assemblies were tested for less than the 150 hours of failure free power on time prior to delivery to LAT integration per LAT-MD-00408 para. 7.1.2.9. S.B.: TEM/TPS assemblies tested for at least 150 failure free powered on hours prior to delivery for LAT integration | Document change | Mate/demate logs updated | CLOSED |
| 00546 | TEM/TPS assy | GLAT 1838, 1839 | During GLAT1838/GLAT1839 testing in TV chamber TV chamber DAQ reported old value of test unit temperature. It caused LAT-DS-04085 temp. testing procedure to fail. S.B.: Chamber should be reporting updated values of test unit temp. | Use-as-is | Proceeded with T/V test. Problem has not been observed again. No performance failure of hardware; problem was caused by chamber DAQ software | CLOSED |
| 00551 | TEM/TPS | GLAT 1838, 1839, 1840, 1841 | IS: No shock monitors were included with the units during transport to/from vibration testing at Wyle labs SB: Shock monitors installed per AIDS #669 | Use-as-is | Units are hand carried to/from Wyle labs in shipping containers. Have not observed excessive shock on any units transported for vibe test. | CLOSED |

7/19/05