## TEM/TPS NCR Report

| NCR | Item Description | Serial # | Description of NonConformance | Disposition | Work Performed | Status |
| --- | --- | --- | --- | --- | --- | --- |
| 00299 | TEM Box Assy | All | IS: TEM Box have incorrect connector reference designators. S.B.: TEM box base drawing LAT-DS-00554 should show correct reference designators. | Rework | Used Brady labels with kapton tape overlay to remark ref. designators to revised drawing | CLOSED |
| 00348 | TEM/TPS GLAT 1753 | All | IS: During T/V test of GLAT 1753, Tracker bias 1 and 0 voltage and Tracker Bias current are out of tolerance during hot thermal cycle performance testing per LAT-TD-03631-04. Measured Bias 1 voltage ranged from 133.2 to 135.58 V, measured Bias 0 voltage ranged from 117.4 - 119.49 V, measured Bias current was 0.0029A during 4 hot soak temperature testing. Ambient and cold temperature soak testing was OK. S.B.: Within ranges specified in performance test procedure LAT-TD-04085 rev. 3. Bias 1 voltage range is 145 - 165 V, Bias 0 voltage range is 130 - 150 V, Bias current range is 0.0030 - 0.0045 A | Documentation Change | MRB concurred to change range of TKR Bias voltages and current in LAT-TD-03631. | CLOSED |
| 00436 | TEM and TPS CCAs | GT104 thru GT122 | IS: Arathane 5750 A/B used by vendor (General Technologies) to conformal coat TEM and TPS CCAs has shelf life that expired on 3 April 2005 S.B.: Shelf life not expired | Documentation Change | MUA #003 approved by GSFC to extend shelf life three months; GT received new material in June 2005 | CLOSED |
| 00489 | TEM CCA | GLAT1762, 1763, 1765 | 1. GLAT1762, 1763, 1765 mounting screws for the CCA are too long causing threads to protrude slightly from the bottom of the housing. 2. No dust covers installed on connectors of boards as delivered from vendor for test. | Use-as-is | 1. Board temporarily installed in box for test. Conformal coat and thermal adhesive will increase thickness of board to eliminate screw protrusion. | CLOSED |
| 00491 | TPS CCA | GLAT17841788, 1783 | 1) All three CCA boxes with incorrect 78 pin connector jack screws installed. 2) All three CCA boxes have jack post screws installed backwards. 3) The lid screws used are of incorrect length (3/8 ''). SB 1/4". | 1. Use-as-is 2. Rework 3. Rework | Boards are not in flight configuration; supporting hardware is temporarily installed and was reconfigured to complete board testing | CLOSED |
| 00545 | TEM/TPS assy | see below | IS: TEM/TPS assemblies were tested for less than the 150 hours of failure free power on time prior to delivery to LAT integration per LAT-MD-00408 para. 7.1.2.9. S.B.: TEM/TPS assemblies tested for at least 150 failure free powered on hours prior to delivery for LAT integration | Use-as-is | Updating data packages with actual powered on hours | OPEN Pending Systems Engineering approval to use-as-is |
| 00551 | TEM/TPS | GLAT 1838, 1839, 1840, 1841 | IS: No shock monitors were included with the units during transport to/from vibration testing at Wyle labs SB: Shock monitors installed per AIDS #669 | Use-as-is | Units are hand carried to/from Wyle labs in shipping containers. Have not observed excessive shock on any units transported for vibe test. | CLOSED |

7/19/05