## TEM/TPS NCR Report  -  9/19/05

## GLAT 1840, 1846, 1847, 1848, 1849

| NCR | Item Description | Serial # | Description of NonConformance | Disposition | Work Performed | Status |
| --- | --- | --- | --- | --- | --- | --- |
| 00397 | TEM/TPS Package | All | Issue: Oscillation of CAL-3.3V Digital when TEM/TPS tester board is connected. Amplitude around 100mV, 1-2KHz frequency. Oscillation is triggered at power-on of calorimeter and sustained. No oscillation is present when turning the power on at cold tempeartures (-40C). At room-temperature oscillation might or might not be triggered by power-on. At hot temperatures (+50C) oscillation was always triggered at power-on. | Rework | MRB concurred with TPS board design changes. Design change was verified on TPS from GLAT 1754 (Qual). All TPS boards to be reworked per revised CCA drawing. TPS units on GLAT 1752 and GLAT 1753 installed in GRID to be removed and reworked per NCR | OPEN Pending Systems Engineeringapproval of technical memo from ELX defining TEM/TPS power on conditions to avoid initiating oscillations |
| 00513 | TPS, CCA | GLAT 1781, 1790, 1792, 1777 (TEM/TPS GLAT1840) | IS: Per LAT-TD-01652 performance test, RMS noise on TEM 2.5V was 820 microvolt S.B.: less than 500 microvolt | Documentation Change | Previously observed and dispositioned in NCR #469 | OPEN Pending revision of TD-01652 to change range |
| 00545 | TEM/TPS assy | ALL | IS: TEM/TPS assemblies were tested for less than the 150 hours of failure free power on time prior to delivery to LAT integration per LAT-MD-00408 para. 7.1.2.9. S.B.: TEM/TPS assemblies tested for at least 150 failure free powered on hours prior to delivery for LAT integration | Use-as-is | Updating data packages with actual powered on hours | OPEN Pending Systems Engineering approval to use-as-is |
| 00614 | TPS SVT | TEM/TPS GLAT1847 | Marginal limit for CAL high voltage bias current. | Documentation Change | Concluded that acceptance limit selected for CAL high voltage current should be changed | OPEN Pending revision of TD-04085-04 with new CAL high voltage current |
| 00615 | TEM/TPS | GLAT 1847 | IS: Error in temperature test during T/V resulted from Broken thermocouple #12. This disabled temperature test S.B. No failure | Use As Is | Temperatures were verified using redundant TCs | CLOSED |

9/16/05