|  | Document # | Date |
| --- | --- | --- |
|  | LAT-TD-02834 | November 13, 2003 |
|  | Author(s) | Supersedes |
|  | Richard Claus |  |
| LAT Requirements Document |  |  |
|  | Subsystem/Office |
|  | I&T |
| Document Title |
| GLAST LAT I&T Testing Requirements Document |

This copy dated: 5/7/2004 1:38 PM

Gamma-ray Large Area Space Telescope (GLAST)

Large Area Telescope (LAT)

Integration and Test Subsystem (I&T)

Testing Requirements Document

CHANGE HISTORY LOG

| Revision | Effective Date | Description of Changes |
| --- | --- | --- |
| 01 | January 13, 2004 | Initial draft distributed to subsystems for their input |
| 02 | March 11, 2004 | Added CAL contributions received thus far |
| 03 | May 5, 2004 | Added ACD and TKR contributions received thus far |

TABLE OF CONTENTS

1.	Purpose	7

2.	Scope	7

3.	Definitions	7

3.1.	Acronyms	7

3.2.	Definitions	8

4.	Applicable Documents	8

5.	Description	9

6.	Necessary infrastructure	9

7.	Test Scripts	9

7.1.	TKR (WBS 4.1.4)	11

7.1.1.	Tracker Power Consumption	11

7.1.2.	Tracker Temperature	12

7.1.3.	Tracker Leakage Current	13

7.1.4.	GTRC configuration	14

7.1.5.	GTFE registers load and read-back	15

7.1.6.	GTFE split configuration	16

7.1.7.	Tracker Gain and Noise	17

7.1.8.	Tracker Threshold Scan	18

7.1.9.	Tracker ToT Test with charge injection	19

7.1.10.	Tracker single strip noise occupancy	20

7.1.11.	Tracker layer noise occupancy	21

7.1.12.	Efficiency, resolution and alignment	22

7.1.13.	Tracker Muon Scan	23

7.2.	CAL (WBS 4.1.5)	24

7.2.1.	CAL Power Consumption	24

7.2.2.	CAL Temperature	27

7.2.3.	GCRC configuration	29

7.2.4.	GCFE configuration	30

7.2.5.	AFEE configuration	31

7.2.6.	CAL reset	33

7.2.7.	CAL Pedestals	34

7.2.8.	CAL Electronic Gain	36

7.2.8.1.	CAL Electronic Gain 1	36

7.2.8.2.	CAL Electronic Gain 2	39

7.2.9.	CAL Integral non-linearity	41

7.2.9.1.	CAL Integral non-linearity 1	41

7.2.9.2.	CAL Integral non-linearity 2	43

7.2.10.	Evaluate channel droop	46

7.2.11.	CAL Noisy Channels	48

7.2.12.	CAL Dead Channels	49

7.2.13.	CAL LO Discriminator	50

7.2.13.1.	CAL LO Discriminator 1	50

7.2.13.2.	CAL LO Discriminator 2	52

7.2.13.3.	CAL LO Discriminator 3	54

7.2.13.4.	CAL LO Discriminator 4	56

7.2.13.5.	CAL LO Discriminator 5	58

7.2.14.	CAL HI Discriminator	60

7.2.14.1.	CAL HI Discriminator 1	60

7.2.14.2.	CAL HI Discriminator 2	62

7.2.14.3.	CAL HI Discriminator 3	64

7.2.14.4.	CAL HI Discriminator 4	66

7.2.14.5.	CAL HI Discriminator 5	68

7.2.15.	CAL Zero-Suppress Thresh.	70

7.2.15.1.	CAL Zero-Suppress Thresh. 1	70

7.2.15.2.	CAL Zero-Suppress Thresh. 2	72

7.2.15.3.	CAL Zero-Suppress Thresh. 3	74

CAL High Rate Trigger	76

7.3.	ACD (WBS 4.1.6)	77

7.3.1.	ACD Test Script Outline (This section from D. Thompson)	77

7.3.2.	Power-on AEM electronics	78

7.3.3.	Power-on FREE cards	79

7.3.4.	GAFE and GARC configure & readback	80

7.3.5.	ACD pedestal readback	81

7.3.6.	ACD Strobe	82

7.3.7.	ACD Veto Threshold	83

7.3.8.	ACD HLD Threshold	84

7.3.9.	ACD Trigger	85

7.3.10.	ACD Low Range PHA	86

7.3.11.	ACD High Range PHA	87

7.3.12.	ACD Zero-Suppress	88

7.3.13.	ACD Non-linearity	89

7.3.14.	ACD light tightness	90

7.3.15.	ACD Power-On High Voltage	91

7.3.16.	ACD Raise/Lower High Voltage	92

7.3.17.	ACD pedestal calculation	93

7.3.18.	ACD MIP threshold	94

7.3.19.	ACD pedestal measurement	95

7.3.20.	ACD False VETO	96

7.3.21.	ACD discriminator mask	97

7.3.22.	ACD Limit Check	98

7.3.23.	ACD Gain Calibration	99

7.3.24.	ACD SAA Mode	100

7.3.25.	ACD Operating Power Consumption	101

7.3.26.	ACD Efficiency	102

7.3.27.	ACD Timing	103

7.3.28.	ACD High Rate Trigger	104

7.4.	ELX (WBS 4.1.7)	105

7.4.1.	Power Supply Assembly voltage measurement test	105

7.4.2.	Power Supply Assembly current limit test	106

7.4.3.	Power Distribution Unit voltage measurement test	107

7.4.4.	Power Distribution Unit current limit test	108

7.4.5.	Power Distribution Unit voltage sequencing test	109

7.4.6.	Voltage margin test	110

7.4.7.	SysClk margin test	111

7.4.8.	Environmental monitoring test	112

7.4.9.	Writeable register test	113

7.4.10.	Read-only register test	114

7.4.11.	Dataless command tests	115

7.4.12.	Event path tests	116

7.4.13.	Trigger path tests	117

7.4.14.	Detector (sensor?) tests	118

7.5.	FSW (WBS 4.1.7)	119

7.5.1.	1553 Interface Test	119

7.5.2.	Command Functional	120

7.5.3.	Memory Upload and Dump	121

7.5.4.	Narrowband Telemetry	122

7.5.5.	Wideband Telemetry	123

7.5.6.	Vehicle Signals Interface	124

7.5.7.	CPU-CPU Communications	125

7.5.8.	EPU Internal Configuration	126

7.5.9.	T&DF Internal Configuration	127

7.5.10.	TKR Internal Configuration	128

7.5.11.	CAL Internal Configuration	129

7.5.12.	ACD Internal Configuration	130

7.5.13.	Event Filtering	131

7.5.14.	Electronic Calibration	132

7.5.15.	FSW and LAT Initialization	133

7.5.16.	FSW and LAT recovery	134

7.5.17.	LAT Pointing Calculations	135

7.5.18.	GRB Handling	136

7.5.19.	GRB Detection	137

7.5.20.	Repointing Logic	138

7.5.21.	Safe Modes	139

7.5.22.	Science Modes	140

7.5.23.	Diagnostic and Calibration Modes	141

7.5.24.	Thermal Control System	142

7.5.25.	LAT On-Orbit Initialization	143

7.5.26.	Sky Survey Mode	144

7.5.27.	Pointed Observation Mode	145

7.5.28.	LAT Performance Verification	146

7.5.29.	LAT Airborne End-to-End Test	147

7.6.	I&T (WBS 4.1.9) System level tests	148

7.6.1.	Inter-subsystem timing-in script	148

7.6.2.	Inter-subsystem cross talk test	149

7.6.3.	Data taking	150

7.6.4.	Comprehensive test	151

7.6.5.	Limited performance test	152

7.6.6.	Aliveness test	153

7.6.7.	Single contributor trigger	154

7.6.8.	Single contributor synchronization	155

7.6.9.	Single contributor muon survey	156

7.6.10.	Multi-contributor synchronization	157

7.6.11.	Multi-contributor high rate trigger	158

8.	File formats	159

8.1.	Schema and configuration files	159

8.2.	Calibration files	159

8.2.1.	XML	159

8.2.2.	FITS binary tables	159

8.3.	Event data files	159

Purpose

This document outlines the testing requirements to be carried out by the GLAST LAT I&T subsystem.

Scope

The scope of this document covers EM-2 and LAT integration.  The goal is to have a comprehensive set of scripts ready for LAT integration after the end of EM-2.  This document covers both functional tests and calibration procedures that are run on-line using LATTE.  Offline calibration procedures are covered under a separate document (LAT-TD-???).  Both individual subsystem tests as well as system level tests are covered.

Definitions

Acronyms

ACD	Anti-coincidence subsystem

AEM      	ACD Electronics Module

API      	Application Program Interface

CAL	Calorimeter subsystem

COMM     	Communications Module

cPCI     	Compact PCI

EEPROM   	Electrically Erasable Programmable Read Only Memory

EGSE	Electronic Ground Support Equipment

ELX	Electronics subsystem

EM      	Engineering Model

EPU      	Event Processor Unit

FITS     	Flexible Image Transport System

FSW	Flight software

FU       	Flight Unit

GUI      	Graphical User Interface

I&T	Integration and Test

IDL      	Interactive Data Language

ISOC	Instrument Science Operations Center

LAN      	Local Area Network

LAT 	Large Area Telescope

LATTE	LAT Test Executive

LCB	LAT Communications Board

MB       	Mega bytes

NFS     	Network File System

ODBC	Open DataBase Connectivity

PCI      	Peripheral Communications Interface

PPC      	Power PC

PSA	Power Supply Assembly

QU       	Qualification Unit

RAM      	Random Access Memory

ROOT     	Rene's (?) Object Oriented Tool

RTE      	Real Time Engine

SBC      	Single Board Computer

SCL      	Spacecraft Control Language

TBR      	To Be Reviewed

TKR	Tracker subystem

TCP/IP   	Transmission Control Protocol/Internet Protocol

TEM      	Tower Electronics Module

VME      	Versa Module Eurocard

Definitions

Flash Memory   	A type of memory that retains its contents when powered off.  It is normally read only but can be written by a special software procedure.

Functional test	A test that produces a go/no-go result.

Calibration procedure	A procedure whose product is a set of constants.

Subsystem	One of ACD, CAL, TKR, ELX or FSW

System	Something that crosses subsystem boundaries

Test-stand     	The combination of a workstation, embedded system, electronics and sensor under test, with corresponding software

Single Contributor	A single contributor system, includes integrated TKR, CAL, TEM, PSA

Multi-contributor	Can include any subset of entire LAT system

Applicable Documents

- LAT-MD-00408	LAT Program Instrument Performance Verification Plan

- LAT-TD-00191	Tracker Tower Electrical Tests

- LAT-SS-00231	Calorimeter Performance Acceptance Standard and Tests

- LAT-TD-01112	ACD Functional Test Plans

- LAT-TD-00786	LAT Flight Software Test Plan

- LAT-MD-00676	LAT Assembly Sequence

- LAT-MD-00466	LAT I&T SVAC  Plan

- LAT-MD-00440	LAT Beam Test Plan

- LAT-MD-01055	LAT Electrical Performance Test Plan

- LAT-SS-00XXX-XX 	LAT Electrical Ground Support Equipment Level 3 Specification

- LAT-SS-00586	Online Software Validation and Verification

Description

This document describes testing to be carried out as LAT components are received by I&T from the subsystems.  In many cases, corresponding test software will also be received.  This software is used by the subsystem to carry out the pre-ship testing and by a combination of the subsystem and I&T to determine the acceptance of the component by I&T.

The delivered software will undergo scrutiny by I&T before being accepted, version controlled and released into the I&T repertoire of tests to be carried out during integration.  If it follows I&T requirements, the test is to be listed in this document.  If it doesn’t, and I&T and the subsystem cannot agree on making a common test, I&T will develop its own version of the test.  The project should strive to avoid the latter situation to prevent having to resolve discrepancies between the results of the subsystem’s version and I&T’s version of the test.  As well, handling the divergence of the independent development and maintenance paths is potentially difficult.

I&T will be the main source of the system level tests, in collaboration with the System Engineering department.

Necessary infrastructure

- Certified Test Stand (LAT-TD-00861).  
I&T will certify, validate and establish a pedigree of the test stand hardware and the associated flight software.  These will be maintained under configuration control.

- Certified version of LATTE (LAT-SS-00586).  
I&T will certify LATTE using the LAT Test Bed.  LATTE core software is version controlled and released.

Test Scripts

Each test listed in this section is described on an integer number of pages (usually one).  The test descriptions are formatted in the form of a table.  The table contains:

- The test script’s name

- The test’s TEST ID

- The test’s SVAC ID, if applicable

- Any aliases the test script goes by

- Test script(s) this script supercedes, if any

- Category, from:

  - Electronics - Component name (e.g., Power supplies, TEM, PSA, etc.)

  - ACD

  - Calorimeter

  - Tracker

  - I&T

- Short description (synopsis)

- Author.  May be useful if a question occurs and contact with the original author is desired to find the intention of something.

- Owner/maintainer.  Likely to change with time or involve multiple people and won’t be updated in this document.

- Test description version number.

- Motivation (e.g. answers a requirement in some LAT document)

- Prerequisites: Script(s) that must be run before this one can be expected to succeed (e.g., to generate some input file for this script

- Required EGSE

- Required input data/files

  - Type, e.g., calibration, configuration…

  - Format, e.g., XML, FITS…

- Generated output data/files

  - Type, e.g., event data, calibration…

  - Format, e.g., XML, FITS…

- Possible completion statuses, e.g., PASSED, FAILED, other

- Long description of the test

- Additional comments, perhaps to list quirks or observations?

A subsection is devoted to each test script table.

TKR (WBS 4.1.4)

Tracker Power Consumption

| NAME TkrPowerConsumptionTest | TEST ID TKR101 | SVAC ID |
| --- | --- | --- |
| ALIASES TE101 | SUPERCEDES None | CATEGORY TKR |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION Measure the Tracker readout-electronics power consumption |
| PREREQUISITES Testing of TEM and power supplies before mating to flight hardware. Individual trays tested by TKR subsytem before tower assembly. |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test report |
| COMPLETION STATUSES |
| DESCRIPTION The digital power (2.5 V), analog high (2.5 V), and analog low (1.5 V) supplies are successively turned on, and a clock is supplied to the Tower by the TEM. The resulting current draw and power-supply voltages are checked to be within specifications and are recorded. The current and voltage measurements are made using the monitoring built into the TEM and supplies. Following the measurement with clock only (no commands) the data mask is loaded such that all channels are disabled. Trigger-acknowledge signals, followed by readout, are sent at a rate of 1 kHz, and the power measurement is repeated. |
| COMMENTS TO BE REVIEWED – TEM V and I monitors functionalities need to be assessed |

Tracker Temperature

| NAME | TEST ID TKR102 | SVAC ID |
| --- | --- | --- |
| ALIASES TE102 | SUPERCEDES None | CATEGORY TKR |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION Verify that the Tracker built-in temperature sensors work. |
| PREREQUISITES TKR101 |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION All supplies, except the SSD bias voltage, are turned on and delivered to the tower module. The temperature from each of the 16 sensors is recorded at 5-minute intervals for an hour. A plot of temperature versus time is made for each sensor. |
| COMMENTS Tower-level test |

Tracker Leakage Current

| NAME | TEST ID TKR103 | SVAC ID |
| --- | --- | --- |
| ALIASES TE103 | SUPERCEDES None | CATEGORY TKR |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION Measure the Tracker SSD bias current and monitor the Tracker internal temperature with SSD biased. |
| PREREQUISITES TKR102 |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION With the Tracker module powered and clocked, the SSD bias supply is turned on and ramped step by step (5 V steps) to a voltage sufficient to deplete all SSDs in the tower module (according to information from the tower module assembly database) and within the specified maximum range. The Tracker temperature is monitored and recorded (from the internal sensors), as is the room temperature. The supply current is recorded at each step, and a plot of current versus voltage is made. The measurement is made with room lights on and off, to verify the light shielding. The results are compared with the sum of leakage current measurements of the trays from which the tower module was assembled. |
| COMMENTS TO BE REVIEWED – TEM V and I monitors functionalities need to be assessed |

GTRC configuration

| NAME TkrGTRCConfiguration | TEST ID TKR201 | SVAC ID |
| --- | --- | --- |
| ALIASES TE201 | SUPERCEDES None | CATEGORY TKR |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION Test loading and readback of the controller-chip configuration register, including broadcast mode |
| PREREQUISITES TKR101 |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES Pass/fail |
| DESCRIPTION The GTRC chips are sequentially addressed and their configuration registers loaded with a bit pattern. Each time the register is read back and checked for errors. The test is repeated with the complement of the bit pattern. The test then is repeated with a broadcast address for writing the register, followed by sequential readback. |
| COMMENTS Functional test applied to each single layer |

GTFE registers load and read-back

| NAME TkrGTFECheck | TEST ID TKR202 | SVAC ID |
| --- | --- | --- |
| ALIASES TE202 | SUPERCEDES None | CATEGORY TKR |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION Test loading and readback of the 5 readout-chip configuration registers, including broadcast mode |
| PREREQUISITES TKR201 |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES Pass/fail |
| DESCRIPTION The GTFE chips are sequentially addressed via the low-side GTRC and their mask (TRIGGER, DATA, CALIB) and DAC registers are sequentially loaded with a bit pattern. In each case the register then is read back and checked for errors. The MODE register then is loaded to switch the chips to the high-side controller and the MODE register is read back via the right GTRC. The MASK and DAC registers then are loaded with the complement bit pattern and read back via the right GTRC and checked. The GTFE MODE registers are set to split them equally between the two sides in each layer. GTFE MASK and DAC registers are simultaneously loaded with bit patterns via a broadcast command, and then sequentially read back and checked. |
| COMMENTS Functional test applied to each single layer |

GTFE split configuration

| NAME TkrReadingConfigurationTest | TEST ID TKR203 | SVAC ID |
| --- | --- | --- |
| ALIASES TE203 | SUPERCEDES None | CATEGORY TKR |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION Test redundancy of layer readout configurations, test charge injection system and data path |
| PREREQUISITES TKR202 |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES Pass/fail |
| DESCRIPTION The redundancy of the readout configuration is tested by running the same test of the charge injection system for three layer configurations, i.e. i) all GTFEs readout on the low-side GTRC, ii) all GTFEs readout on the high-side GTRC, iii) default configuration with 12 GTFEs on each side. In each configuration all the channels in the layer are enabled for data taking and triggering, and the signal threshold is set high enough to cut out noise; two random channels per GTFE are pulsed with enough charge to cross the threshold. The layer is readout and the channels above threshold are compared with the pulsed one. In case the default configuration is not working, all possible configurations with any number of GTFE on each side are scanned in order to define the optimal split point, which is the one that minimizes the number of GTFEs isolated from the readout. |
| COMMENTS Functional test applied to each single layer |

Tracker Gain and Noise

| NAME TkrNoiseAndGain | TEST ID TKR301 | SVAC ID |
| --- | --- | --- |
| ALIASES TE301 | SUPERCEDES None | CATEGORY TKR |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION Secondary calibration of the noise performance and threshold stability. |
| PREREQUISITES TKR203 |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report. Data files with gain and noise for each channel and list of dead channels (both amplifiers and disconnected strips) |
| COMPLETION STATUSES |
| DESCRIPTION The GTFEs mode registers and the GTRCs control register are set according to the optimal split point from test TKR203 (see 7.1.6). The calibration DAC is set in each chip to about 1 fC injection, and the calibration and data masks are set to select in each layer a set of non-adjacent channels smaller in number than the GTRC buffer size. The threshold is scanned over a range about 1 fC, with about 100 events per setting taken. For each setting the occupancy is calculated, and the data are used to fit for each channel the gain and noise. Channels having too low a gain are listed as dead amplifiers, and channels with a noise comparable with the average noise level from a bare MCM are listed as disconnected strips. The procedure is repeated for different mask settings until all live channels are analyzed. The results are stored in a database. A list of gain and noise for each channel is generated, as well as a list of dead channels. |
| COMMENTS Functional and performance test applied to each single layer |

Tracker Threshold Scan

| NAME TkrTriggerRate | TEST ID TKR302 | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY TKR |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION Test layer self trigger and GTFEs trigger lines |
| PREREQUISITES TE301 |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES Pass/fail |
| DESCRIPTION The GTFEs mode registers and the GTRCs control register are set according to the optimal split point from test TKR203 (see 7.1.6). The calibration masks are all disabled. The trigger in the TEM is set to the standard 3-in-a-row self trigger, enabling the combination of layers that includes the tray under test; the other five missing silicon layers are faked by forcing the corresponding trigger lines in the combination to be always on. One GTFE at a time is enabled for triggering and data. The threshold DAC is set at a low value, the TEM LRS counters are monitored and each single FE must provide high rate trigger primitives at sufficiently low threshold. The threshold is increased in steps until while the trigger rate decreases to cosmic rays levels at a reasonably high threshold. |
| COMMENTS Functional and performance test applied to each single layer |

Tracker ToT Test with charge injection

| NAME TkrTotTest | TEST ID TKR303 | SVAC ID C11, C12 |
| --- | --- | --- |
| ALIASES TE303 | SUPERCEDES TKR206 | CATEGORY TKR |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION Calibration of the TOT gain. Explore full range of calibration DAC |
| PREREQUISITES TE302 |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES Pass/fail, TOT time_vs_charge calibration factor |
| DESCRIPTION The GTFEs mode registers and the GTRCs control register are set according to the optimal split point from test TKR203 (see 7.1.6). The calibration and data masks in each layer are set to enable a maximum of 30 channels randomly chosen for each GTRC to be strobed and readout. The threshold is fixed at a low value, and the calibration DAC is scanned over its whole range, with about 100 events per setting taken. The TOT value at both GTRC is read for each setting and the data are used to calibrate the TOT. The results are stored in the calibration database. |
| COMMENTS Functional and performance test applied to each single layer |

Tracker single strip noise occupancy

| NAME TkrNoiseOccupancy | TEST ID TKR304 | SVAC ID C10 |
| --- | --- | --- |
| ALIASES TE304 | SUPERCEDES TKR501 | CATEGORY TKR |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION Noisy channel search |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report plus list of noisy channels |
| COMPLETION STATUSES |
| DESCRIPTION The GTFEs mode registers and the GTRCs control register are set according to the optimal splitting point from test TKR203 (see 7.1.6). The data and trigger masks in the layer are set to enable all channels to be readout. The threshold is fixed around a working point value (about ¼ MIP, THR_DAC = 35). 100,000 random triggers are issued and the single strip noise occupancy (hits/triggers) is recorded. Any channel with a noise occupancy larger than 10-3 is considered as noisy and recorded in a database. |
| COMMENTS Functional and performance test applied to each single layer |

Tracker layer noise occupancy

| NAME TkrLayerNoiseOccupancy | TEST ID TKR501 | SVAC ID C10 |
| --- | --- | --- |
| ALIASES TE501 | SUPERCEDES TKR502 | CATEGORY TKR |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION Check the noise performance and determine working point for data taking |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION The GTFEs mode registers and the GTRCs control register for all layers are set to the standard configuration for data taking (i.e. 12 FEs on each GTRC), unless otherwise specified as a result of test TKR203 (see 7.1.6). The data and trigger masks in the layer are set to enable all channels to be readout except the noisy channels, as from test TKR304 (see 7.1.10). Random triggers are issued at various threshold values, scanning the full range 0 of the threshold DAC register, and the strips above threshold are readout. At each data point the layer noise occupancy is calculated as the ratio of the number of strips above threshold divided by the number of strips enabled. The threshold gets incremented until a plateau is reached, which is the result of cosmic rays crossing the tower in accidental coincidence with random triggers. The average values expected are a few 10-4 for the occupancy plateau, occuring at a threshold DAC larger than ~30 (range 0). The threshold DAC corresponding to the requirements layer noise occupancy of 10-4 is extrapolated from the plot and is defined as the working point for that layer for subsequent tests. The efficiency at that threshold or higher will be evaluated in the efficiency scan. |
| COMMENTS Functional and performance test applied to each single layer |

Efficiency, resolution and alignment

| NAME TkrDetectionEfficiency | TEST ID TKR503 | SVAC ID ? |
| --- | --- | --- |
| ALIASES TE503 | SUPERCEDES None | CATEGORY TKR |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION Verification of the single layer detection and trigger efficiency, spatial resolution, and tower alignment requirements. |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report. Efficiency scans for all layers, alignment constants, single-hit resolution for all layers |
| COMPLETION STATUSES |
| DESCRIPTION The mode-registers, masks, and threshold DACs are set as determined by test TKR501 (see 7.1.11). The trigger is set to the standard 3-in-a-row and all combinations are enabled. Detection efficiency is studied for each layer independently: the trigger line from the layer under study is forced to 1 and cosmic ray data are taken for at least 12 hours. The data are analyzed as follows. Tracks are found and fit to straight lines with the layer under study omitted from the pattern recognition. Events are selected with a single, good-quality track that passes through all the other tracker layers. The projection of the track onto the selected layer is calculated, and a search is made for a hit cluster close to the track, if the extrapolation shows that the particle, to high confidence, passed through a live detector region. The efficiency for finding a hit cluster is calculated from the full data set and recorded for each of the 16 SSDs in the layer. The threshold DAC is then varied and the efficiency measurement is repeated until the threshold range 0 has been explored. The same measurement is then repeated for all the layers in the tracker tower. For each trigger in the above procedure, the status of all Layer-ORs is recorded, and the efficiency of each Layer-OR is calculated in the same manner as for the data readout. During the same procedure, when a cluster is found close to the track in the selected layer, its distance from the track intersection is calculated and a histogram of that residual is made on a layer-by-layer basis. The width of the distribution is a measure of the resolution (with some bias from the track fit), and the mean of the distribution gives an indication of the alignment quality. The number of triggers registered in every combination of 3 x-y- layers is recorded as to check that every combination works with good efficiency. |
| COMMENTS Performance test applied to tower only |

Tracker Muon Scan

| NAME | TEST ID TKR504 | SVAC ID C9 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES TKR503 | CATEGORY TKR |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION Exercise the system in working conditions for medium-long term periods |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

CAL (WBS 4.1.5)

CAL Power Consumption

Below is a draft of the CAL power consumption procedures.  It relies heavily upon LATTE's rule capability and RunControl's Environemental Monitor and Housekeeping capabilities.  Please review it and let me know if it's the way to go or if there is a better way.  I not very familiar with rules so please correct any mistakes or misconceptions.  I plan to implement temperature monitoring in a similar manner.

| NAME | TEST ID CAL | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Monitor CAL Power Consumption |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION TBD |
| PREREQUISITES Environmental Monitoring “enabled” HouseKeeping enabled |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES Schema describing Calorimeter voltage/current monitor rules and limit settings which could vary by TEM (see description) : $CAL_ROOT\FMx\Configurations\calvcMonConfig.xml | GENERATED OUTPUT FILES Housekeeping File: Session Log: Alarms Display: (Not an output file but don’t know where else to put it) |
| COMPLETION STATUSES Red/Yellow ALARMS |
| DESCRIPTION <?xml version='1.0' encoding='UTF-8'?> <configuration name='CAL current/voltage Monitoring Rules' version='1.0'> <rules> <rule name='voltageMonitor'> <class>gRule.GruleAlarms</class> <parameters> <name>voltageMonitor</name> <subsystem>CAL</subsystem> <category>voltage</category> <enabled>1</enabled> <continuous>1</continuous> <yellowLowerLimit>TBD</yellowLowerLimit> <yellowUpperLimit>TBD</yellowUpperLimit> <yellowAction>None</yellowAction> <redLowerLimit>TBD</redLowerLimit> <redUpperLimit>TBD</redUpperLimit> <redAction>disablePower</redAction> </parameters> </rule> <rule name='currentMonitor'> <class>gRule.GruleAlarms</class> <parameters> <name>currentMonitor</name> <subsystem>CAL</subsystem> <category>current</category> <enabled>1</enabled> <continuous>1</continuous> <yellowLowerLimit>TBD</yellowLowerLimit> <yellowUpperLimit>TBD</yellowUpperLimit> <yellowAction>None</yellowAction> <redLowerLimit>TBD</redLowerLimit> <redUpperLimit>TBD</redUpperLimit> <redAction>disablePower</redAction> </parameters> </rule> <rule name='biasVoltageMonitor'> <class>gRule.GruleAlarms</class> <parameters> <name>voltageMonitor</name> <subsystem>CAL</subsystem> <category>voltage</category> <enabled>1</enabled> <continuous>1</continuous> <yellowLowerLimit>TBD</yellowLowerLimit> <yellowUpperLimit>TBD</yellowUpperLimit> <yellowAction>None</yellowAction> <redLowerLimit>TBD</redLowerLimit> <redUpperLimit>TBD</redUpperLimit> <redAction>disableHV</redAction> </parameters> </rule> <rule name='biasCurrentMonitor'> <class>gRule.GruleAlarms</class> <parameters> <name>currentMonitor</name> <subsystem>CAL</subsystem> <category>current</category> <enabled>1</enabled> <continuous>1</continuous> <yellowLowerLimit>TBD</yellowLowerLimit> <yellowUpperLimit>TBD</yellowUpperLimit> <yellowAction>None</yellowAction> <redLowerLimit>TBD</redLowerLimit> <redUpperLimit>TBD</redUpperLimit> <redAction>disablePower</redAction> </parameters> </rule> </rules> <GLAT> <GTEM ID='0-15'> <GTIC> <adc_cal_digital_3_3v egu="CAL Digital 3.3 Voltage",rule="voltageMonitor"/> <adc_cal_digital_3_3i egu="CAL Digital 3.3 Current",rule="currentMonitor"/> <adc_cal_analog_3_3v egu="CAL Analog 3.3 Voltage",rule="voltageMonitor"/> <adc_cal_analog_3_3i egu="CAL Analog 3.3 Current",rule="currentMonitor"/> <adc_cal_bias_v egu="CAL Bias Voltage",rule="biasVoltageMonitor"/> <adc_cal_bias_i egu="CAL Bias Current",rule="biasCurrentMonitor"/> <adc_tkr_c7_t1 egu="Temperature"/> </GTIC> </GTEM> </GLAT> </configuration> |
| COMMENTS The objective is to use RunControl provided capabilities to monitor power consumption and take appropriate action. The RunControl capabilities to be used are: Rule definition and assignment to telemetry items Environmental monitoring Housekeeping It would be convenient if uniform limits could be applied across all TEMs, however, this is dependent upon the capabilities of the TEM current/voltage monitoring circuitry and will require some analysis before actual limits can be determined. |

CAL Temperature

Below is a draft of the CAL temperatures procedure.  Same comments are with CAL power comsumption description.

| NAME | TEST ID CAL | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Monitor CAL Temperatures |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION TBD |
| PREREQUISITES Environmental Monitoring “enabled” HouseKeeping enabled |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES Schema describing Calorimeter temperature monitor rules and limit settings which could vary by TEM (see description) : $CAL_ROOT\FMx\Configurations\calvcMonConfig.xml | GENERATED OUTPUT FILES Housekeeping File: Session Log: Alarms Display: (Not an output file but don’t know where else to put it) |
| COMPLETION STATUSES Red/Yellow ALARMS |
| DESCRIPTION <?xml version='1.0' encoding='UTF-8'?> <configuration name='CAL Temperature Monitoring Rules' version='1.0'> <rules> <rule name='temperatureMonitor'> <class>gRule.GruleAlarms</class> <parameters> <name>temperatureMonitor</name> <subsystem>CAL</subsystem> <category>temperature</category> <enabled>1</enabled> <continuous>1</continuous> <yellowLowerLimit>TBD</yellowLowerLimit> <yellowUpperLimit>TBD</yellowUpperLimit> <yellowAction>None</yellowAction> <redLowerLimit>TBD</redLowerLimit> <redUpperLimit>TBD</redUpperLimit> <redAction>disablePower</redAction> </parameters> </rules> <GLAT> <GTEM ID='0-15'> <GTIC> <adc_afee0_t0 egu="Temperature",rule=”temperatureMonitor”/> <adc_afee0_t1 egu="Temperature"",rule=”temperatureMonitor”/> <adc_afee1_t0 egu="Temperature"",rule=”temperatureMonitor”/> <adc_afee1_t1 egu="Temperature"",rule=”temperatureMonitor”/> <adc_afee2_t0 egu="Temperature"",rule=”temperatureMonitor”/> <adc_afee2_t1 egu="Temperature"",rule=”temperatureMonitor”/> <adc_afee3_t0 egu="Temperature"",rule=”temperatureMonitor”/> <adc_afee3_t1 egu="Temperature"",rule=”temperatureMonitor”/> </GTIC> </GTEM> </GLAT> </configuration> |
| COMMENTS The objective is to use RunControl provided capabilities to monitor CAL temperatures and take appropriate action. The RunControl capabilities to be used are: Rule definition and assignment to telemetry items Environmental monitoring Housekeeping It would be convenient if uniform limits could be applied across all TEMs, however, this is dependent upon the capabilities of the TEM current/voltage monitoring circuitry and will require some analysis before actual limits can be determined. |

GCRC configuration

See AFEE Configuration, Section 7.2.5

GCFE configuration

See AFEE Configuration, Section 7.2.5

AFEE configuration

| NAME Calu_init | TEST ID CAL | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION TBD |
| PREREQUISITES TEMPowerUp |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calu_init.html Register Snapshot: yymmddhhmmss_FMx_calu_init.xml |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Procedure Init: Read CAL parameters configuration file Obtain Calorimeter unit identifier: try configuration file first else use runControl preferences instrumenttype value. Update default runControl Preferences paths with calorimeter unit identifier (assumes subdirectories already exist) Turn of Schema reuse flag (can be overridden from a test suite) Setup: (runControl.rcSetup does schema processing) Turn on schema reuse flag (all following application runs use this schema) Set power up flag based on whether “all” calorimeters defined in schema are powered up Set current configuration parameter values which include: TBD If interactive mode: Display current configuration parameter values Prompt operator for configuration parameters Else if batch Update CAL configuration parameters with batch values startRun: Initialize report structure Disable triggers Set trigger mask to no triggers Running: Set PDU registers based on configuration values Set HV bias DAC value Power Calorimeters Wait for HV to settle Initialize GCCCs Initialize GCRCs with configuration values Initialize GCFEs with configuration values Initialize FLE,FHE,LAC,ULD DACs from tables contained in files if available Take register configuration snapshot and save filename to be used by all following application runs as the initial instrument state. Report: TBD |
| COMMENTS |

CAL reset

See AFEE Configuration, Section 7.2.5

CAL Pedestals

| NAME CALU_PEDESTALS_CI | TEST ID CAL | SVAC ID C18 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Determine CAL Noise Pedestals |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION Level IV: 9.1.14.1 The equivalent noise (RMS) on the low energy slow shaped signal paths (LEX8, LEX1) shall be less than 2000 e-. Level IV: 9.1.14.2 The equivalent noise (RMS) on the high energy slow shaped signal paths (HEX8, HEX1) shall be less than 2000 e-. |
| PREREQUISITES Estimate of electrons per ADC bin for LEX and HEX slow shaping circuits (see TBD). Note: Tests can be run without the above mentioned information, but requirements for absolute noise cannot be tested. |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES Schema describing Calorimeter: $CAL_ROOT\FMx\Configurations\FMx_schema.xml CAL Configuration file: $CAL_ROOT\FMx\Configurations\calParams.cfg | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calu_collect_ci.html Register Snapshot: yymmddhhmmss_FMx_calu_collect_ci.xml Noise Pedestals Table: yymmddhhmmss_FMx_pedestals.fits Noise Pedestal Statistics: yymmddhhmmss_FMx_pedestal_stats.csv |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Algorithm Setup: Nominal with the following changes: Tack Delay setting = CI_TIMED_PEAK Disable calibration injection to all FEs (config_1 = 0x80) Collect noise data For each operational gain setting plus the muon gain setting, gainidx = 0 to 8 (9 settings) For N samples (default = 1000) Use GLT self trigger to inject charge (FEs accept no charge however), delay, and read 4 range event data Compute Mode for each component and energy range, mode[gainidx, 4,8,2,12] Compute Mean for each component and energy range, mean[gainidx, 4,8,2,12] Compute standard deviation for each component and energy range, std[gainidx,4,8,2,12] Save Pedestals table, mode[9,4,8,2,12], in FITS format to file Histogram noise samples and fit gaussian For each gain, gainidx = 0 to 8 For LEX8 and HEX8 ranges, rangeidx = 1,3 (LEX1 and HEX1 range data does not have enough points to fit curve) For each layer, layeridx = 0 to 7 (SLAC numbering 0-3=X layers, 4-7=Y layers) For each logend, eidx = 0 to 1 For each log, logidx=0 to 11 Histogram noise ADC settings using mode[gainidx,rangeidx,layerid,eidx,logidx] +/- offset (default = 30) as histogram lower/upper boundaries. Fit gaussian to histogram Find Peak[gainidx,rangeidx,layeridx,eidx,logidx] Compute Centroid[gainidx,rangeidx,layeridx,eidx,logidx] Compute FWHM[gainidx,rangeidx,layeridx,eidx,logidx] Compute Area[gainidx,rangeidx,layeridx,eidx,logidx] Save pedestals statistics, mode, peak, centroid, fwhm, area in FITS file format (to support utilities needing noise threshold data, low and high trigger DAC settings, data suppresion DAC settings). Save pedestals statistics, mode, peak, centroid, fwhm, area in CSV file format suitable for database entry (trend analysis support) Requirements checks/sanity checks If Area[…] does not equal 80 to 100% of N samples then PASS[…]= FALSE (failed check) |
| COMMENTS |

CAL Electronic Gain

Attached is a draft of the CAL Electronic Gain procedures.  It consists of 2 procedures;

calf_gain_p01 to characterize  evaluate the selectable Low and High Energy gain settings.

calf_gain_p02 to characterize and evaluate the "times 8" and "times 1"  gain ratios for both low and high energy.

CAL Electronic Gain 1

| NAME Calf_gain_p01 | TEST ID CAL | SVAC ID C19 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Characterize and evaluate CAL charge amplifier gain capabilities |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION Level IV: 9.1.1.6 The gain of the low energy channels shall be adjustable by a) at least a factor of 2 b) in steps of approximately 10%-25%. Level IV: 9.1.2.5 The gain of the high energy channels shall be adjustable by a) at least a factor of 2 b) in steps of approximately 10%-25%. c) An additional gain setting shall be used for ground liveness testing. Level IV: 9.1.11.4 The high energy charge amplifier shall provide a test gain to be used in ground aliveness test with cosmic muons. The test gain shall increase the nominal gain by a factor of approximately 10. The test gain configuration is pre-selected by command input to the ASIC. |
| PREREQUISITES Calu_init |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES Schema describing Calorimeter: $CAL_ROOT\FMx\Configurations\FMx_schema.xml CAL Configuration file: $CAL_ROOT\FMx\Configurations\calParams.cfg | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calf_gain_p01.html Register Snapshot: yymmddhhmmss_FMx_calf_gain_p01.xml Events File: yymmddhhmmss_FMx_calf_gain_p01.fits relative gain Table: yymmddhhmmss_FMx_relgain.fits |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Algorithm Setup: Nominal with the following changes: Tack Delay setting = CI_TIMED_PEAK Collect gain data For each energy range, rangeidx = 0 to 3 Find minimum globally useable DAC setting Find maximum globally useable DAC setting Using mid DAC setting For each operational gain setting plus the muon gain setting, gainidx = 0 to 8 (9 settings) For N samples, default = 1000 Use GLT self trigger to inject charge, delay, and read 4 range event data Compute Mean for each component and energy range, mean[gainidx, 4,8,2,12] Compute standard deviation for each component and energy range, std[gainidx,4,8,2,12] Calculate relative gains wrt nominal gain setting For each gain setting, gainidx = 0 to 8 Compute relative gain at gain setting gainidx as ratio of value at gain setting gainidx over value at nominal, relGain = mean[gainidx…]/mean[5,…] Save relative gain table, relgain[9,4,8,2,12], in FITS format to file For relative gains 7 to 1 If ratio between previous relative gain and current relative gain is not between 10 to 25% then fail component If relative gain 0 is not 2 times greater than relative gain 7 then fail component If relative gain 8 is not 10 time greater than relative gain 7 for the HEX1 range then fail component |
| COMMENTS While this test supports subsets of the LAT hardware, it expects the existent TEMs to have identical configurations. In LAT systems where the existing TEMs are not identical, groups of identical TEMs should be identified and individual tests run on each identical TEM subgroup(see Test Preparation) It is sufficient to use for each ranges, one Charge Injection value for relative gain testing if chosen appropriately. For each range, this test will find the minimum and maximum Charge Injection value that produces ADC results above pedestal and below saturation respectively and choose the middle value from this interval as the Charge Injection value for relative gain testing. Nominal gain setting for the LEX8/LEX1 ranges is gain setting 5. Nominal gain setting for the HEX8/HEX1 ranges is gain setting 13. “steps of approximately 10%-25%.” referred to in requirements Level IV 9.1.1.6 and 9.1.2.5 will be interpreted for testing purposes to be 9% to 27.5% i.e. 10% tolerance assigned to approximately. |

CAL Electronic Gain 2

| NAME Calf_gain_p02 | TEST ID CAL | SVAC ID C19 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Characterize and evaluate the “times 8” to “times 1” gain ratios for both the Low and High Energy Paths |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION Level IV: 9.1.3.6 The LEX1 amplifier of the low energy channel shall process the entire low energy charge amplifier range, i.e. nominally 1.6 GeV maximum energy. Level IV: 9.1.3.7 The LEX8 amplifier of the low energy channel shall process the lowest eighth of the low energy charge amplifier range, i.e. nominally 200 MeV maximum energy. Level IV: 9.1.3.8 The HEX1 amplifier of the high energy channel shall process the entire high energy charge amplifier range, i.e. nominally 100 GeV maximum energy. Level IV: 9.1.3.9 The HEX8 amplifier of the high energy channel shall process the lowest eighth of the high energy charge amplifier range, i.e. nominally 12.5 GeV maximum energy. |
| PREREQUISITES Calu_collect_ci |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES Schema describing Calorimeter: $CAL_ROOT\FMx\Configurations\FMx_schema.xml CAL Configuration file: $CAL_ROOT\FMx\Configurations\calParams.cfg | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calf_gain_p02.html |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Algorithm TBD |
| COMMENTS |

CAL Integral non-linearity

Below is a draft of the CAL Integral non-linearity test procedures.  It consists of 3 procedures;

Calu_collect_singlex16 to collect charge injected event data by column.

calf_adc_p02 to evaluate integral non-linearity, noise, and range coverage by channel.

calf_adc_p05 to evaluate droop

CAL Integral non-linearity 1

| NAME calu_collect_ci_singlex16 | TEST ID CAL | SVAC ID C20 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Collect event data generated using |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION Prerequisite for calf_adc procedures |
| PREREQUISITES calu_init |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calu_collect_ci_singlex16.html Register Snapshot: yymmddhhmmss_FMx_calu_collect_ci_singlex16.xml Events File: yymmddhhmmss_FMx_calu_collect_ci_singlex16.fits |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Algorithm Setup Obtain collection parameters (range order, channel columns, charge Injection DAC sequence, number of samples, gains) Collect data For each range order, (default ridx = 0) For each column, (default colIdx = 0,11) For each Charge Injection (CI) setting; cidx = bDAC, eDAC,iDAC (default cidx = 0,4096,16) For N samples, sidx=0,199 (default = 200) Use GLT self trigger to inject charge, delay, and read 4 range event data Archive event |
| COMMENTS Charge Injection is done one column at a time to better simulate the operational environment. Events from simultaneous charge injection to multiple channels in a layer shows some dependency on number of channels injected. |

CAL Integral non-linearity 2

| NAME calf_adc_p02 | TEST ID CAL | SVAC ID C20 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Evaluate channel integral non-linearity, noise, and energy range. |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION Level IV: 9.1 a)The GCFE shall perform spectroscopic measurements over a range from 0.4 MeV to 100 GeV…c)The dynamic range shall be divided into two independent signal chains, one for low energy range, one for the high energy range. Level IV: 9.1.1.1 The low energy charge amplifier shall process energy depositions in the 2 MeV to 1.6 GeV range. The characteristics of the inputs to the low energy range are summarized in Table 9.3. Level IV: 9.1.2.1 The high energy charge amplifier shall process energy depositions in the 100 MeV to 100 GeV range. The characteristics of the inputs to the low energy range are summarized in Table 9.3. Level IV: 9.1.11 The GCFE ASIC shall accept a precision calibration voltage from an external DAC as a reference voltage for a calibration charge injection system. Level IV: 9.1.11.1 The test charge injection system shall be capable of testing the entire dynamic range of the GCFE ASIC. Level IV: 9.1.3.6 The LEX1 amplifier of the low energy channel shall process the entire low energy charge amplifier range, i.e. nominally 1.6 GeV maximum energy. Level IV: 9.1.3.7 The LEX8 amplifier of the low energy channel shall process the lowest eighth of the low energy charge amplifier range, i.e. nominally 200 MeV maximum energy. Level IV: 9.1.3.8 The HEX1 amplifier of the high energy channel shall process the entire high energy charge amplifier range, i.e. nominally 100 GeV maximum energy. Level IV: 9.1.3.9 The HEX8 amplifier of the high energy channel shall process the lowest eighth of the high energy charge amplifier range, i.e. nominally 12.5 GeV maximum energy. Level IV: 9.1.5 The maximum non-linearity in each of the four ranges: LEX8, LEX1, HEX8, and HEX1 shall be 1% of full range. Level IV: 9.1.14.3 a)The output of the buffer amplifier for each of the four amplifier ranges shall be monotonically increasing with charge input over the top 99.9% of the energy range. b)The integral non-linearity shall be less than +/- 0.5% of full scale. This is the deviation of the best fit straight line from the measured amplitudes over the top 99% of the energy range. Level IV: 9.2.1.3 The maximum non-linearity of the ADC shall be 0.5% of full range. |
| PREREQUISITES calu_collect_ci_singlex16 with full four range readout |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES Events File: yymmddhhmmss_FMx_calu_collect_ci_singlex16.fits Note: Tests can be run without the following information, but characterization in energy terms cannot be performed ADC to Energy Conversion Table. Pedestals Table Relative Gain Table | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calf_adc_p02.html Noise Pedestals Table: yymmddhhmmss_FMx_pedestals.fits Noise Pedestal Statistics: yymmddhhmmss_FMx_pedestals_stats.csv |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Algorithm Setup Collect data For each Charge Injection (CI) setting; cidx = bDAC, eDAC,iDAC (default cidx = 0,4096,16) For N samples, sidx=0,199 (default = 200) read 4 range event data, data[4,8,2,12,sidx] Compute Mean for each component and energy range, mean[4,8,2,12,cidx] Compute standard deviation for each component and energy range, noise[4,8,2,12,cidx] Check for railed component, if data = 0xfff, then upper limit (ul) = previous cidx Check for plateaued component, if mean[…,cidx] – mean[…cidx-1] < tolerance, upper limit (ul) = previous cidx Analyze Using least squares method, fit line to mean Generate distribution of deviation of mean values to fitted line, non-linearity measurements Extract max non-linearity and average non-linearity and compare to criteria Extract max noise and average noise measures from the noise distribution and compare to criteria If gain of the component at which the data was taken the lowest setting and if the ADC to energy conversion table is available, then compute maximum energy value for each range and compare against criteria |
| COMMENTS Assumptions? To minimize mean and noise statistic skewing, this test defines the upper ADC range limit for any FE to be the maximum ADC mean value for which none of the samples contributing to this mean are railed ADC values (4096). The result of this definition is that “noisy” FEs may be assigned a lower maximum ADC value that affects the maximum energy determination. For some FE energy ranges, the maximum input analog (reference DAC or Charge Injection) does not rail the ADC but instead the ADC result “plateaus” after some input analog interval. To make non-linearity evaluation practical, this test defines the upper ADC range limit for FE energy range in this case to be the maximum ADC mean value which does not deviate more than 10% from a line obtained from a linear fit of all the previous ADC mean values. The method for determining an upper limit will be referred to as the ADC “plateau” method. The test for Integral non-linearity is not gain specific. To test integral non-linearity for a given gain involves collecting event data at the requested gain and then applying the integral non-linearity test procedure to that data. A “suite” for testing integral non-linearity over one or more gains can be formed by “chaining” test procedure calf_adc_p02 along with calu_collect_ci for each gain setting. The report from that test would reference the individual calu_collect_ci and calf_adc_p02 reports. |

Evaluate channel droop

| NAME calf_adc_p05 | TEST ID CAL | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Evaluate channel droop. |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION Level IV: 9.1.4.3 The T&H circuit shall be capable of holding a constant signal amplitude for > 100 usec with less than 0.1% droop for a signal amplitude dynamic range of 500 (TBR). |
| PREREQUISITES calu_collect_ci_singlex16 with full four range readout and all 4 range first combinations. |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES Events File: yymmddhhmmss_FMx_calu_collect_ci_singlex16.fits Note: Tests can be run without the following information, but characterization in energy terms cannot be performed ADC to Energy Conversion Table. Pedestals Table Relative Gain Table | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calf_adc_p03.html Plots file: yymmddhhmmss_FMx_calf_adc_p03.pdf |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Algorithm Setup Collect data For each Range order, ridx = 0,3 For each Charge Injection (CI) setting; cidx = bDAC, eDAC,iDAC (default cidx = 0,4096,16) For N samples, sidx=0,199 (default = 200) read 4 range event data, data[4,8,2,12,ridx,sidx] Compute Mean for each component and energy range, mean[4,8,2,12,cidx] Compute standard deviation for each component and energy range, noise[4,8,2,12,cidx] Check for railed component, if data = 0xfff, then upper limit (ul) = previous cidx Check for plateaued component, if mean[…,cidx] – mean[…cidx-1] < tolerance, upper limit (ul) = previous cidx Analyze Normalize means. Compare normalized range order mean value differences to criteria. |
| COMMENTS Assumptions? Processing each range of a four range readout requires approximately 14 usec at a clock frequency of 20 Mhz. This time factor is assumed in the droop evaluation algorithm and means that a droop check over more than 56 usec with this test is not possible. |

CAL Noisy Channels

| NAME | TEST ID CAL | SVAC ID C22 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Manual procedure to generate/update CAL noisy channels list |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION SVAC C22 |
| PREREQUISITES Calf_adc_p02 Calf_trg_p03 Calf_supp_p01 |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Yymmddhhmmss_FMx_calf_adc_p02.html Yymmddhhmmss_FMx_calf_supp_p01.html Yymmddhhmmss_FMx_calf_trg_p03.html | GENERATED OUTPUT FILES CAL Noisy Channel File: Yymmddhhmmss_calu_noisy_channel_list.xml (actual format TBD) |
| COMPLETION STATUSES Not Applicable (manual procedure) |
| DESCRIPTION This is a manual procedure (for now) Evaluate Yymmddhhmmss_FMx_calf_adc_p02.html reports for noisy channels and add them to noisy channel list Evaluate Yymmddhhmmss_FMx_calf_supp_p01.html reports for channels which do not suppress data over a required range and add them to the noisy channel list for at least the LEX8 energy channel and possibly more. Evaluate Yymmddhhmmss_FMx_calf_trg_p03.html reports for channels which do not trigger data over a required range and add them to the noisy channel list for at least the LEX8 energy channel and possibly more. |
| COMMENTS CAL defines a channel to be one energy range from a crystal front end (FE). Therefore each crystal FE represents 4 channels for a total of 768 channels per Calorimeter (4 x 8 x 2 x 12). Format of CAL’s contribution to the noisy channel file needs to be defined. |

CAL Dead Channels

| NAME | TEST ID CAL | SVAC ID C23 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Manual procedure to generate/update CAL dead channels list |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION SVAC C23 |
| PREREQUISITES Calf_adc_p02 Calf_exr_p01 |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Yymmddhhmmss_FMx_calf_adc_p02.html Yymmddhhmmss_FMx_calf_exr_p01.html | GENERATED OUTPUT FILES CAL Dead Channel File: Yymmddhhmmss_calu_dead_channels_list.xml (actual format TBD) |
| COMPLETION STATUSES Not Applicable (manual procedure) |
| DESCRIPTION This is a manual procedure (for now) Evaluate Yymmddhhmmss_FMx_calf_adc_p02.html reports for unresponsive channels and add them to dead channel list Evaluate Yymmddhhmmss_FMx_calf_exr_p01.html reports for commanding problems and add them to the dead channel list. |
| COMMENTS CAL defines a channel to be one energy range from a crystal front end (FE). Therefore each crystal FE represents 4 channels for a total of 768 channels per Calorimeter (4 x 8 x 2 x 12). Format of CAL’s contribution to the dead channel file needs to be defined. |

CAL LO Discriminator

Attached is a draft of the CAL LO Discriminator procedures.  It consists of 5 procedures;

calf_trg_p03 to characterize the Low Energy Discriminator  DAC

calu_genFleTable to use that characterization table to produce an FLE trigger threshold table

calf_trg_p05 to generate an FLE trigger threshold table based on noise pedestals

calf_trg_p01 to evaluate the independence of the trigger enable/disable logic

calf_trg_p04 to characterize and evaluate the trigger arrival time behavior

calu_genLacTable is dependent on calf_supp_p01 as stated in its prerequisites

The same issues that Eduardo had with the zero data-suppression procedures also exist with these procedures.

CAL LO Discriminator 1

| NAME CALF_TRG_P03 | TEST ID CAL | SVAC ID C24 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Characterize the CAL Low Energy Discriminator wrt ADC settings |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION Level III: 5.9 Low Energy Trigger Signal: CAL to provide low energy trigger signal to the LAT trigger system.. Level IV: 9.1.10 The outputs of the two 0.5 usec shaping amplifiers (FHE and FLE) are connected to discriminators. The two outputs of the trigger discriminators logic are provided to external logic which forms the calorimeter trigger request inputs to the GLAST trigger system. Level IV: 9.1.10.3 The low energy trigger (FLE) discriminator level shall be adjustable by command input to DACs inside the ASIC. Two adjustment ranges shall be provided: lowest energies (<~60 MeV) with ~ 1 MeV resolution and moderate energies (<~400 MeV) with ~ 5 MeV resolution. |
| PREREQUISITES CALU_INIT |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES ADC to Energy Conversion Table. Pedestals Table Relative Gain Table Note: Tests can be run without the above mentioned information, but characterization in energy terms cannot be performed | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calf_trg_p03.html Register Snapshot: yymmddhhmmss_FMx_calf_trg_p03.xml FLE to ADC conversion Table: yymmddhhmmss_FMx_fle2dac.fits FLE DAC characterization Plots: yymmddhhmmss_FMx_calf_trg_p03.pdf |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Setup: Nominal with the following changes: Tack Delay setting = CI_TIMED_PEAK GLT data suppress = TRUE Gain setting = Nominal Collect FLE/FHE DAC characterization data For each of 2 cases (case 0 = FLE DAC) (case 1 = FHE DAC) For each FST DAC setting, fstDacidx = 0 to 127 default For each column, colidx = 0 to 11 For each charge injection (CI) setting, cidx=0 to 4095 and component are still suppressed For N samples, sidx = 0 to ? default = 0 Use GLT self trigger to inject charge, delay, read event data with trigger primitive diagnostic data If 90% of the samples had triggers from a component and , adc[fstDacidx,4,8,2,12]=adc Save FST to ADC conversion table, adc[128,4,8,2,12], in FITS format to file Validate FST DAC operation against criteria Check range and resolution against criteria (by using low energy lowest gain setting or by converting collected ADC data to lowest gain equivalent) Check linearity of DAC? |
| COMMENTS |

CAL LO Discriminator 2

| NAME calu_genFleTable | TEST ID CAL | SVAC ID C26 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Generate an appropriate Low Energy Discriminator threshold Table given a “target” threshold energy usin an appropriate FLE Discriminator Characterization Table |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION LAT-MD-0446-05 GLAST LAT Science Verification Analysis and Calibration (SVAC) Plan, section 5.3 SVAC Complicance, Table item C24 |
| PREREQUISITES CALF_TRG_P03 |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES ADC to Energy Conversion Table. Pedestals Table Relative Gain Table calParams.cfg (Calorimeter environment configuration file) | GENERATED OUTPUT FILES FLE Trigger Threshold Table: yymmddhhmmss_FMx_fle.xml |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Setup: Read fle2adc characterization table Read ADC 2 Energy Conversion table Read relative gain table Obtain (from operator?) energy (MeV) to use for data suppression threshold Obtain (from operator?) LE gain to be used. Process: Using the relative gain table, adjust the fle2dac characterization values to the requested gain. Using the relative gain table, adjust the Energy to ADC conversion table to reflect the requested gain. Using the adjusted Energy to ADC conversion table, convert the fle2dac characterization table to anfle2nrg (FLE to Energy) characterization table. For each FE, find the minimum FLE setting whose corresponding energy in the fle2nrg characterization table is above the request energy threshold (FLE trigger threshold table, FLEThreshold[4,8,2,12]) Save FLE trigger threshold table Save threshold table, FLEThreshhold[4,8,2,12], in xml format to file with appropriate documentation to include: Requested Energy Threshold Requested Gain FLE to ADC characterization table filename ADC to Energy conversion table filename Relative gain table filename Data generated Application Name “calu_genFleTable” |
| COMMENTS |

CAL LO Discriminator 3

| NAME CALF_TRG_P01 | TEST ID CAL | SVAC ID C24 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Test trigger enable/disables for functionality and independent operation. |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION Level III: 5.9 Low Energy Trigger Signal: CAL to provide low energy trigger signal to the LAT trigger system.. Level IV: 9.1.10.2 Each of the two trigger signals shall be individually enabled or disabled by command input to the ASIC. |
| PREREQUISITES calu_init |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calf_trg_p01.html Register Snapshot: yymmddhhmmss_FMx_calf_trg_p01.xml Trigger Enable Table: Yymmddhhmmss_FMx_calu_trg.xml |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Setup: Nominal with the following changes: Tack Delay setting = CI_TIMED_PEAK GLT trigger mask = Disabled Enable LRS counting for everything (lrs_counter_mask = 0) Process: Sequence thru each FE (all TEMs at once) temb = lat.allTEM() For trgMode (0=LE triggers, 1 = HE trigger) For ccIdx =0 to 3 cc = temb.downCCC(ccIdx) If cc is valid For rcIdx=0 to 3 rc = cc.downCRC(rcIdx) If rc is valid For feIdx=0 to 3 fe = rc.downCFE(feIdx) if fe is valid Clear lrs_counters (broadcast temb.gtic.lrs_counters=0) Verify counters are zeros For temIdx=0 to 15 If lat.downTEM(temIdx).downTIC().lrs_counters <>0 PassflagtrgMode,[temIdx,ccIdx,rcIdx,feIdx]=FAILED Enable trigger (fe.config_1 = 0x380 ¦ trgMode <<1) Inject Charge (rc.calStrobe=1) Wait for fast shaper peak logic to complete (.01 seconds) Read and verify trigger counters For temIdx=0 to 15 If lat.downTEM(temIdx).downTIC().lrs_counters <=0 Passflag[trgMode,temIdx,ccIdx,rcIdx,feIdx]=FAILED If lat.downTEM(temIdx).downTIC().lrs_counters >1 MultpleTriggerflag[trgMode,temIdx,ccIdx,rcIdx,feIdx]=TRUE Clear lrs_counters (broadcast temb.gtic.lrs_counters=0) Verify counters are zeros For temIdx=0 to 15 If lat.downTEM(temIdx).downTIC().lrs_counters <>0 PassflagtrgMode,[temIdx,ccIdx,rcIdx,feIdx]=FAILED Disable trigger (fe.config_1 = 0x380) Inject Charge (rc.calStrobe=1) Wait for fast shaper peak logic to complete (.01 seconds) Read and verify trigger counters For temIdx=0 to 15 If lat.downTEM(temIdx).downTIC().lrs_counters >0 Passflag[trgMode,temIdx,ccIdx,rcIdx,feIdx]=FAILED |
| COMMENTS |

CAL LO Discriminator 4

| NAME CALF_TRG_P04 | TEST ID CAL | SVAC ID C24 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Characterize trigger arrival time |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION Level III: 5.9 Low Energy Trigger Signal: CAL to provide low energy trigger signal to the LAT trigger system.. Level IV: 9.1.3.1 The low energy fast shaped signals shall peak at 0.5 +/- 0.2 usec. Level IV: 9.1.10.1 The variation in time of the leading edge of the trigger output from the time of energy deposition shall be less than +/- 0.2 usec. |
| PREREQUISITES calu_init |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES CI_TIMED_TRIGGER (expected trigger primitive present Tack delay value for timed Charge Injection stimulus) Note: Tests can be run without the above mentioned information, but characterization in energy terms cannot be performed | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calf_trg_p04.html Register Snapshot: yymmddhhmmss_FMx_calf_trg_p04.xml Events File: yymmddhhmmss_FMx_calf_trg_p04.fits |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Setup: Nominal with the following changes: Tack Delay setting = CI_TIMED_PEAK Setup for trigger primitive acquisition Use one range readout suppressed data mode Collect Data: For temIdx=0 to 15 For feIdx=0 to 11 Enable triggers for this “column” of FEs (lat.downTEM(temIdx).allCCC().allCRC(),downCFE(feIdx).config_1= 0x3E) For tackDelaySetting = 0 to 255 Set tack delay (tem.cal_trgSeq = tackDelaySetting For nsamples Use Timed trigger to inject charge and acquire event data Decom event data and get trigger primitive state Count triggers (increment triggers[temIdx,trgIdx,ccIdx,rcIdx,endIdx,feIdx,tackDelaySetting] Process Data: Convert trigger count array into trigger percentage (trgPct=triggers[…]/nsamples) Convert trgPct array to triggered array ( trgd[…] = 1 if trgPct[…] > 90%) Look for “dropouts” Generate distribution of trigger tack delays (trgTime[...] = min(where trgd[…]>0] Compute the mode of the triggered tack delay times (trgMode =stats.mode(trgTime)) Compare mode to expected value (if abs(trgMode -CI_TIMED_TRIGGER) > tolerance then FAILED) Compare each FEs triggered time to trgMode (if abs(trgTime[…]-trgMode)>.2usec then FAILED) Convert trgPct array to untriggered array(untrgd[…] = 1 if trgPct[…] < 10%) Look for “dropouts” Generate distribution of untrigger tack delays (untrgTime[...] = max(where trgd[…]>1] Generate distribution of trigger uncertainty times ( diff = trgTime[]-untrgTime[]) Compute mean and standard deviation of trigger uncertainty time and evaluate individual FE responses based on these statistics |
| COMMENTS |

CAL LO Discriminator 5

| NAME CALF_TRG_P05 | TEST ID CAL | SVAC ID C24 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Generate an FLE trigger discriminator table using noise pedestals as thresholds. |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION LAT-MD-0446-05 GLAST LAT Science Verification Analysis and Calibration (SVAC) Plan, section 5.3 SVAC Complicance, Table item C24 |
| PREREQUISITES calu_init |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES ADC to Energy Conversion Table. Pedestals Table Relative Gain Table Note: Tests can be run without the above mentioned information, but characterization in energy terms cannot be performed | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calf_trg_p05.html Register Snapshot: yymmddhhmmss_FMx_calf_trg_p05.xml Events File: yymmddhhmmss_FMx_calf_trg_p05.fits FLE Trigger Noise Pedestal Threshold Discriminator Table: yymmddhhmmss_FMx_calu_fle.xml |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION TBD |
| COMMENTS |

CAL HI Discriminator

Below is a draft of the CAL HI Discriminator procedures.  It consists of 5 procedures;

calf_trg_p03 to characterize the High Energy Discriminator  DAC

calu_genFheTable to use that characterization table to produce an FHE trigger threshold table

calf_trg_p05 to generate an FHE trigger threshold table based on noise pedestals

calf_trg_p01 to evaluate the independence of the trigger enable/disable logic

calf_trg_p04 to characterize and evaluate the trigger arrival time behavior

calu_genFheTable is dependent on calf_trg_p03 as stated in its prerequisites

As you can see, the same procedures are used for low and high energy trigger processing.  The procedures are written to allow processing low and/or high triggers.

CAL HI Discriminator 1

| NAME CALF_TRG_P03 | TEST ID CAL | SVAC ID C24 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Characterize the CAL High Energy Discriminator wrt ADC settings |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION Level III: 5.10 High Energy Trigger Signal: CAL to provide high energy trigger signal to the LAT trigger system. Level IV: 9.1.10.4 The high energy trigger (FHE) discriminator level shall be adjustable by command input to DACs inside the ASIC. The range of adjustment shall include the lowest 25% of the high energy charge amplifier range (<~25 GeV) and have ~ 200 MeV resolution. |
| PREREQUISITES CALU_INIT |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES ADC to Energy Conversion Table. Pedestals Table Relative Gain Table Note: Tests can be run without the above mentioned information, but characterization in energy terms cannot be performed | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calf_trg_p03.html Register Snapshot: yymmddhhmmss_FMx_calf_trg_p03.xml FHE to ADC conversion Table: yymmddhhmmss_FMx_fhe2dac.fits FHE DAC characterization Plots: yymmddhhmmss_FMx_calf_trg_p03.pdf |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Setup: Nominal with the following changes: Tack Delay setting = CI_TIMED_PEAK GLT data suppress = TRUE Gain setting = Nominal Collect FLE/FHE DAC characterization data For each of 2 cases (case 0 = FLE DAC) (case 1 = FHE DAC) For each FST DAC setting, fstDacidx = 0 to 127 default For each column, colidx = 0 to 11 For each charge injection (CI) setting, cidx=0 to 4095 and component are still suppressed For N samples, sidx = 0 to ? default = 0 Use GLT self trigger to inject charge, delay, read event data with trigger primitive diagnostic data If 90% of the samples had triggers from a component and , adc[fstDacidx,4,8,2,12]=adc Save FST to ADC conversion table, adc[128,4,8,2,12], in FITS format to file Validate FST DAC operation against criteria Check range and resolution against criteria (by using low energy lowest gain setting or by converting collected ADC data to lowest gain equivalent) Check linearity of DAC? |
| COMMENTS |

CAL HI Discriminator 2

| NAME calu_genFheTable | TEST ID CAL | SVAC ID C26 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Generate an appropriate High Energy Discriminator threshold Table given a “target” threshold energy using an appropriate FHE Discriminator Characterization Table |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION LAT-MD-0446-05 GLAST LAT Science Verification Analysis and Calibration (SVAC) Plan, section 5.3 SVAC Complicance, Table item C24 |
| PREREQUISITES CALF_TRG_P03 |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES ADC to Energy Conversion Table. Pedestals Table Relative Gain Table calParams.cfg (Calorimeter environment configuration file) | GENERATED OUTPUT FILES FHE Trigger Threshold Table: yymmddhhmmss_FMx_calu_fhe.xml |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Setup: Read fhe2adc characterization table Read ADC 2 Energy Conversion table Read relative gain table Obtain (from operator?) energy (MeV) to use for data suppression threshold Obtain (from operator?) HE gain to be used. Process: Using the relative gain table, adjust the fhe2dac characterization values to the requested gain. Using the relative gain table, adjust the Energy to ADC conversion table to reflect the requested gain. Using the adjusted Energy to ADC conversion table, convert the fhe2dac characterization table to anfhe2nrg (FHE to Energy) characterization table. For each FE, find the minimum FHE setting whose corresponding energy in the fhe2nrg characterization table is above the request energy threshold (FHE trigger threshold table, FHEThreshold[4,8,2,12]) Save FHE trigger threshold table Save threshold table, FHEThreshhold[4,8,2,12], in xml format to file with appropriate documentation to include: Requested Energy Threshold Requested Gain FHE to ADC characterization table filename ADC to Energy conversion table filename Relative gain table filename Data generated Application Name “calu_genFheTable” |
| COMMENTS |

CAL HI Discriminator 3

| NAME CALF_TRG_P01 | TEST ID CAL | SVAC ID C24 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Test trigger enable/disables for functionality and independent operation. |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION Level III: 5.10 High Energy Trigger Signal: CAL to provide high energy trigger signal to the LAT trigger system. Level IV: 9.1.10.2 Each of the two trigger signals shall be individually enabled or disabled by command input to the ASIC. |
| PREREQUISITES calu_init |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calf_trg_p01.html Register Snapshot: yymmddhhmmss_FMx_calf_trg_p01.xml Trigger Enable Table: Yymmddhhmmss_FMx_calu_trg.xml |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Setup: Nominal with the following changes: Tack Delay setting = CI_TIMED_PEAK GLT trigger mask = Disabled Enable LRS counting for everything (lrs_counter_mask = 0) Process: Sequence thru each FE (all TEMs at once) temb = lat.allTEM() For trgMode (0=LE triggers, 1 = HE trigger) For ccIdx =0 to 3 cc = temb.downCCC(ccIdx) If cc is valid For rcIdx=0 to 3 rc = cc.downCRC(rcIdx) If rc is valid For feIdx=0 to 3 fe = rc.downCFE(feIdx) if fe is valid Clear lrs_counters (broadcast temb.gtic.lrs_counters=0) Verify counters are zeros For temIdx=0 to 15 If lat.downTEM(temIdx).downTIC().lrs_counters <>0 PassflagtrgMode,[temIdx,ccIdx,rcIdx,feIdx]=FAILED Enable trigger (fe.config_1 = 0x380 ¦ trgMode <<1) Inject Charge (rc.calStrobe=1) Wait for fast shaper peak logic to complete (.01 seconds) Read and verify trigger counters For temIdx=0 to 15 If lat.downTEM(temIdx).downTIC().lrs_counters <=0 Passflag[trgMode,temIdx,ccIdx,rcIdx,feIdx]=FAILED If lat.downTEM(temIdx).downTIC().lrs_counters >1 MultpleTriggerflag[trgMode,temIdx,ccIdx,rcIdx,feIdx]=TRUE Clear lrs_counters (broadcast temb.gtic.lrs_counters=0) Verify counters are zeros For temIdx=0 to 15 If lat.downTEM(temIdx).downTIC().lrs_counters <>0 PassflagtrgMode,[temIdx,ccIdx,rcIdx,feIdx]=FAILED Disable trigger (fe.config_1 = 0x380) Inject Charge (rc.calStrobe=1) Wait for fast shaper peak logic to complete (.01 seconds) Read and verify trigger counters For temIdx=0 to 15 If lat.downTEM(temIdx).downTIC().lrs_counters >0 Passflag[trgMode,temIdx,ccIdx,rcIdx,feIdx]=FAILED |
| COMMENTS |

CAL HI Discriminator 4

| NAME CALF_TRG_P04 | TEST ID CAL | SVAC ID C24 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Characterize trigger arrival time |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION Level IV: 9.1.3.3 The high energy fast shaped signals shall peak at 0.5 +/- 0.2 usec. Level IV: 9.1.10 The outputs of the two 0.5 usec shaping amplifiers (FHE and FLE) are connected to discriminators. The two outputs of the trigger discriminators logic are provided to external logic which forms the calorimeter trigger request inputs to the GLAST trigger system. Level IV: 9.1.10.1 The variation in time of the leading edge of the trigger output from the time of energy deposition shall be less than +/- 0.2 usec. Level IV: 9.5 The calorimeter shall provide a prompt (within 2 us of an event) high-energy trigger signal with a detection efficiency of 90% (TBR) for 50 GeV gamma rays entering the calorimeter from the LAT field of view with a trajectory which traverses at least 8 RL of CsI. |
| PREREQUISITES calu_init |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES CI_TIMED_TRIGGER (expected trigger primitive present Tack delay value for timed Charge Injection stimulus) Note: Tests can be run without the above mentioned information, but characterization in energy terms cannot be performed | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calf_trg_p04.html Register Snapshot: yymmddhhmmss_FMx_calf_trg_p04.xml Events File: yymmddhhmmss_FMx_calf_trg_p04.fits |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Setup: Nominal with the following changes: Tack Delay setting = CI_TIMED_PEAK Setup for trigger primitive acquisition Use one range readout suppressed data mode Collect Data: For temIdx=0 to 15 For feIdx=0 to 11 Enable triggers for this “column” of FEs (lat.downTEM(temIdx).allCCC().allCRC(),downCFE(feIdx).config_1= 0x3E) For tackDelaySetting = 0 to 255 Set tack delay (tem.cal_trgSeq = tackDelaySetting For nsamples Use Timed trigger to inject charge and acquire event data Decom event data and get trigger primitive state Count triggers (increment triggers[temIdx,trgIdx,ccIdx,rcIdx,endIdx,feIdx,tackDelaySetting] Process Data: Convert trigger count array into trigger percentage (trgPct=triggers[…]/nsamples) Convert trgPct array to triggered array ( trgd[…] = 1 if trgPct[…] > 90%) Look for “dropouts” Generate distribution of trigger tack delays (trgTime[...] = min(where trgd[…]>0] Compute the mode of the triggered tack delay times (trgMode =stats.mode(trgTime)) Compare mode to expected value (if abs(trgMode -CI_TIMED_TRIGGER) > tolerance then FAILED) Compare each FEs triggered time to trgMode (if abs(trgTime[…]-trgMode)>.2usec then FAILED) Convert trgPct array to untriggered array(untrgd[…] = 1 if trgPct[…] < 10%) Look for “dropouts” Generate distribution of untrigger tack delays (untrgTime[...] = max(where trgd[…]>1] Generate distribution of trigger uncertainty times ( diff = trgTime[]-untrgTime[]) Compute mean and standard deviation of trigger uncertainty time and evaluate individual FE responses based on these statistics |
| COMMENTS |

CAL HI Discriminator 5

| NAME CALF_TRG_P05 | TEST ID CAL | SVAC ID C24 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Generate an FHE trigger discriminator table using noise pedestals as thresholds. |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION LAT-MD-0446-05 GLAST LAT Science Verification Analysis and Calibration (SVAC) Plan, section 5.3 SVAC Complicance, Table item C24 |
| PREREQUISITES calu_init |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES ADC to Energy Conversion Table. Pedestals Table Relative Gain Table Note: Tests can be run without the above mentioned information, but characterization in energy terms cannot be performed | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calf_trg_p05.html Register Snapshot: yymmddhhmmss_FMx_calf_trg_p05.xml Events File: yymmddhhmmss_FMx_calf_trg_p05.fits FHE Trigger Noise Pedestal Threshold Discriminator Table: yymmddhhmmss_FMx_calu_fhe.xml |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION TBD |
| COMMENTS |

CAL Zero-Suppress Thresh.

Below is a draft of the CAL zero-suppress threshold procedures.  It consists of 3 procedures;

calf_supp_p01 to characterize the data suppress DAC

calu_genLacTable to use that characterization table to produce a threshold table

calf_supp_p02 to generate a noise pedestal threshold table

calu_genLacTable is dependent on calf_supp_p01 as stated in its prerequisites

CAL Zero-Suppress Thresh. 1

| NAME CALF_SUPP_P01 | TEST ID CAL | SVAC ID C26 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Characterize the Log Accept Discriminator wrt ADC settings |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION Level IV: 9.1.9.1 The amplitude of the LEX8 output shall be compared with a programmable threshold, the accept lower level discriminator, to identify CsI crystals with measurable energy depositions. This crystal-accept signal shall be transmitted to external logic for determination of crystals to be included in the event readout message. Level IV: 9.1.9.2 The accept discriminator level shall be adjustable by command to the ASIC a) with adjustment resolution of ~0.25 MeV b) over the lowest approximately 10% of the LEX8 energy range. |
| PREREQUISITES CALU_INIT |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES ADC to Energy Conversion Table. Pedestals Table Relative Gain Table Note: Tests can be run without the above mentioned information, but characterization in energy terms cannot be performed | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calf_supp_p01.html Register Snapshot: yymmddhhmmss_FMx_calf_supp_p01.xml LAC 2 ADC conversion Table: yymmddhhmmss_FMx_lac2dac.fits LAC DAC characterization Plots: yymmddhhmmss_FMx_calf_supp_p01.pdf |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Setup: Nominal with the following changes: Tack Delay setting = CI_TIMED_PEAK GLT data suppress = TRUE Gain setting = Nominal Collect suppression data For each of 3 cases (case 0 = + LAC DACs set to maximum, - LAC DACs varied) (case 1 = - LAC DACs set to maximum, + LAC DACs varied) (case 2 = -/+ LAC DACs varied; result should be equal to the lower threshold of cases 0 & 1) For each LAC DAC setting, lacDacidx = 0 to 127 default For each charge injection (CI) setting, cidx=0 to 4095 and not all component thresholds found For N samples, default = 10? Use GLT self trigger to inject charge, delay, read event data For each channel (FE), save the average ADC reading obtained from the first charge injection setting, cidx, that causes data from that channel to be present in the event readouts for 90% of the samples, adc[lacDacidx,4,8,3,12] = ADC Save LAC to ADC conversion table, ADC[128,4,8,2,12], in FITS format to file. Validate LAC DAC operation against criteria Check range and resolution against criteria (by using low energy lowest gain setting or by converting collected ADC data to lowest gain equivalent?) Verify case 2 results equal minimum of case0 and case 1 results. |
| COMMENTS |

CAL Zero-Suppress Thresh. 2

| NAME calu_genLacTable | TEST ID CAL | SVAC ID C26 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Generate an appropriate Data Suppression Table for a specified energy given a LAC Discriminator Characterization Table and corresponding ADC to Energy Conversion Table |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION LAT-MD-0446-05 GLAST LAT Science Verification Analysis and Calibration (SVAC) Plan, section 5.3 SVAC Complicance, Table item C26 |
| PREREQUISITES CALF_SUPP_P01 |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES ADC to Energy Conversion Table. Pedestals Table Relative Gain Table | GENERATED OUTPUT FILES LAC 2 ADC conversion Table: yymmddhhmmss_FMx_lac.xml |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Setup: Read Lac2ADC characterization Read ADC 2 Energy Conversion table Read relative gain table Obtain (from operator?) energy (MeV) to use for data suppression threshold Obtain (from operator?) LE gain to be used. Process: Using the relative gain table, adjust the lac2ADC characterization values to the requested gain. Using the relative gain table, adjust the Energy to ADC conversion table to reflect the requested gain. Using the adjusted Energy to ADC conversion table, convert the Lac2ADC characterization table to an Lac2NRG (LAC to Energy) characterization table. For each FE, find the minimum LAC setting whose corresponding energy in the Lac2NRG characterization table is above the request energy threshold (LAC threshold table, LACThreshold[4,8,2,12]) Save LAC threshold table Save threshold table, LACThreshhold[4,8,2,12], in xml format to file with appropriate documentation to include: Requested Energy Threshold Requested Gain LAC to ADC characterization table filename ADC to Energy conversion table filename Relative gain table filename Data generated Application Name “calu_genLacTable” |
| COMMENTS |

CAL Zero-Suppress Thresh. 3

| NAME CALF_SUPP_P02 | TEST ID CAL | SVAC ID C26 |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS Generate a pedestal noise threshold Data Suppression Table. |
| AUTHOR NRL/Code 7650/B. Leas | OWNER/MAINTAINER/CONTACT PERSON NRL/Code 7650/B.Leas |
| MOTIVATION LAT-MD-0446-05 GLAST LAT Science Verification Analysis and Calibration (SVAC) Plan, section 5.3 SVAC Complicance, Table item C26 |
| PREREQUISITES calu_init |
| REQUIRED EGSE LATTE (latest?) SciPy package Dislin package (if hardcopy plots are desired) LAT TestStand (includes TEM?) Calorimeter Schema describing Calorimeter ($CAL_ROOT\FMx\Configurations\FMx_schema.xml) |
| REQUIRED INPUT DATA OR FILES ADC to Energy Conversion Table. Pedestals Table Relative Gain Table Note: Tests can be run without the above mentioned information, but characterization in energy terms cannot be performed | GENERATED OUTPUT FILES Test Report: yymmddhhmmss_FMx_calf_supp_p02.html Register Snapshot: yymmddhhmmss_FMx_calf_supp_p02.xml Events File: yymmddhhmmss_FMx_calf_supp_p02.fits LAC Noise Pedestal Threshold Discriminator Table: yymmddhhmmss_FMx_lac.xml |
| COMPLETION STATUSES PASS IPASS (Incomplete Pass – partial system…only applicable to development phase) FAIL ABORT |
| DESCRIPTION Setup: Nominal with the following changes: Tack Delay setting = CI_TIMED_PEAK GLT data suppress = TRUE Gain setting = Nominal Disable calibration enable bits (config_1 = 0x80) Collect suppression data Initialize LACThreshhold[4,8,2,12] = -1 For each of 2 cases (case 0 = + LAC DACs set to maximum, - LAC DACs varied) (case 1 = - LAC DACs set to maximum, + LAC DACs varied) For each LAC DAC setting, lacDacidx = 63 to 0 For N samples, default = 10? Use GLT self trigger inject no charge, delay, read event data For each channel (FE), save the LAC reading obtained from the first charge injection setting, cidx, that causes data from that channel to be present in the event readouts for 90% of the samples, LACThreshhold[4,8,2,12] = lacDacidx Check against Criteria Flag channels with LACThreshhold = -1 for not having a range low enough to allow the most-probable pedestal Save LAC noise pedestal threshold table Adjust LACThreshholds for a minimum LAC setting of 0 (change -1 to 0) Save LAC noise pedestal threshold table, LACThreshhold[4,8,2,12], in xml format to file with appropriate documentation to include: Requested Energy Threshold Requested Gain LAC to ADC characterization table filename ADC to Energy conversion table filename Relative gain table filename Data generated Application Name “calf_supp_p02” |
| COMMENTS |

CAL High Rate Trigger

| NAME | TEST ID CAL | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY CAL |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD (WBS 4.1.6)

ACD Test Script Outline (This section from D. Thompson)

ACD Functional Tests (not a single script) – The following items must be set before starting this test: voltage (3.3V nominal), system clock frequency (20 MHz nominal).

(Indentation indicates nested scripts – suites?)

Normal text – G2 script exists, not necessarily debugged; Underlined italics – Script outline exists;

Bold underlined text – Script does not exist

ACD Comprehensive Performance Test

ACD Short Functional (goal: 2 hours for this test)

ACD Electronics Short Functional (12 iterations of the Chassis Short Functional)

Chassis Short Functional (Unless otherwise noted , run with both A & B interfaces.)

1  Initial Current Measurements

GARC Registers Initial Reset Test

Initial GAFE Logic Reset Test (18)

2  Power Consumption Tests

GARC/GAFE Register Read/Write Tests (multiple small scripts)

Parity Error Detection by GARC

Maximum PHA Return Test

PHA Enable/Disable Test

PHA Threshold Test

GAFE Register Tests (18)

GAFE Broadcast Command Verification

Characterization of GAFE chips (18, A interface only)

GAFE BIAS_DAC Calibration

GAFE Hold Delay Optimization using TCI

GAFE HitMap Delay Test

GAFE VETO Calibration (using GASU hardware scalers)

GAFE Noise Test (using GASU hardware scalers)

GAFE HLD Calibration (using GASU hardware scalers)

GAFE Discriminator Enable/Disable Test (using GASU hardware scalers)

GAFE TCI Regular Range Tests

GAFE TCI High Range Tests

GAFE Parity Error Test

HitMap Width Test

HitMap Deadtime Stretch Test

VETO and ADC Crosstalk Test

ADC Start Time (TACQ) Test

TCI Comparison of VETO, Hitmap, and PHA

HVBS and PMT Aliveness

HVBS DAC Commands and HV Monitor Differential Drivers

SAA/HV Normal Modes

PMT Aliveness

Test of Look-At-Me Circuitry

Power-on AEM electronics

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Power-on FREE cards

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

GAFE and GARC configure & readback

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD pedestal readback

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD Strobe

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD Veto Threshold

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD HLD Threshold

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD Trigger

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD Low Range PHA

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD High Range PHA

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD Zero-Suppress

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD Non-linearity

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD light tightness

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD Power-On High Voltage

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD Raise/Lower High Voltage

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD pedestal calculation

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD MIP threshold

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD pedestal measurement

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD False VETO

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD discriminator mask

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD Limit Check

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD Gain Calibration

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD SAA Mode

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD Operating Power Consumption

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD Efficiency

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD Timing

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD High Rate Trigger

| NAME | TEST ID ACD | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY ACD |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ELX (WBS 4.1.7)

Power Supply Assembly voltage measurement test

| NAME PSAtest.py | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Electronics – Power supplies |
| SYNOPSIS PSA voltage test |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITE SUCCESSFULLY COMPLETED TEST SCRIPTS None |
| REQUIRED EGSE GPIB Model ??? DVM with GPIB option Dummy load module |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES PASSED FAILED |
| DESCRIPTION This test measures the voltages produced by the tower Power Supply Assembly using a calibrated GPIB readable DVM and compares the result with limit values found in the configuration file. If any of the values are found to be outside of the red limits, the test fails. Bias voltages are measured against their set points as given in the configuration file. [Perhaps we should consider ramping the bias voltages and testing against several set points?] This test must be carried out using an appropriate dummy load that mimics the TEM. [Should this test perform a single measurement and/or sample (randomly?) over a configurable time period?] Results of all voltages are reported in the test report. [How do we handle the input voltage from the spacecraft battery? Do we need to carry out margin testing by ramping the battery up and down or is that already guaranteed to be okay when the PSA is delivered from ELX to I&T (e.g., by design)?] |
| COMMENTS This test is normally carried out when a PSA unit is received by I&T and before a PSA unit is to be integrated with a TEM unit. |

The idea of this test is to qualify a PSA unit.  As described below, it is done using a dummy load and a calibrated GPIB voltmeter.  Possibly an alternative way to do it is to use a “standard” TEM, perhaps not fully functional, and use its environmental quantity measurement features to satisfy this test’s intention.  Dummy loads would have to be applied to the TEM’s cable connectors to simulate the current draw of the front ends.  The “standard” TEM would have to undergo some sort of certification procedure to ensure that its calibration is correct.  What do we want to do?

Power Supply Assembly current limit test

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Electronics – Power supplies |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Power Distribution Unit voltage measurement test

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Electronics – Power supplies |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Power Distribution Unit current limit test

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Electronics – Power supplies |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Power Distribution Unit voltage sequencing test

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Electronics – Power supplies |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Voltage margin test

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Electronics – Power supplies |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Done by ELX?  Determined by design, or needed for every component instance?  Any component requiring a power supply for input voltages needs this test.  List each one seperately?

SysClk margin test

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Electronics |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Same comments as for voltage margin test.  Also useful for each component because it can help shake out incorrect loading of electronic components like resistors, capacitors, etc.

Environmental monitoring test

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Electronics |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION Vary measured item (voltage, current, temperature, etc) over range of device and verify digitized value matches. Checks constants for converting to engineering units as well. Probably this is design/layout dependent, but may be cabling dependent as well, so test cross talk with power glitches, other environmental quantities, command/event/trigger path activity? Test stability of each quantity over time. Also against environment temperature? |
| COMMENTS |

Writeable register test

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Electronics |
| SYNOPSIS Test writeable registers |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION To be done for each component having writable registers: walking ones walking zeros 0's f's a's 5's addressing check MBZ recognition check Parity test Other error testing |
| COMMENTS |

Read-only register test

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Electronics |
| SYNOPSIS Test readable registers |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION To be done for each component having read-only registers: Recognize MBZ fields Verify response to stimuli Parity test Other error testing |
| COMMENTS |

Dataless command tests

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Electronics |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION To be done for each component having dataless commands: Test whether corresponding effect is initiated Parity test Other error testing |
| COMMENTS |

Event path tests

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Electronics |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION Bit path liveness [verify all bits in the path work independently (no 0s, 1s, shorted together bits)] Cross talking bits in the bit path? [Different from detector crosstalk test?] Data bit liveness (PHAs, Log End values & ranges, TOTs) [verify ADCs work] Error reporting for each error type [can we induce each error type?] Event path parity error test Other error reporting Diagnostic reporting [determine whether trigger primitives are being reported correctly; ensure all bits are working (all trigger primitive messages can be generated)] FIFO and other memory tests Backpressure/Rate tests |
| COMMENTS |

Trigger path tests

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Electronics |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION Test of trigger types Trigger type cross-talk test? Veto cross-talk test? Timing in (TACK delay, etc.) [also provides delay register values for configuration file] Zero suppression test Marker test Other modes |
| COMMENTS |

Detector (sensor?) tests

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Electronics |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION Dead channels [also supplies bad channel list] Noisy channels [also supplies bad channel list] Cross talking channels Thresholds [also supplies threshold list] Pedestals [also supplies pedestal list] Linearity Noise & Gain Inter-layer TKR alignment Detection efficiency test |
| COMMENTS |

FSW (WBS 4.1.7)

1553 Interface Test

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION Booting tests |
| COMMENTS |

Command Functional

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Memory Upload and Dump

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Narrowband Telemetry

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Wideband Telemetry

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Vehicle Signals Interface

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

CPU-CPU Communications

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

EPU Internal Configuration

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

T&DF Internal Configuration

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

TKR Internal Configuration

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

CAL Internal Configuration

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

ACD Internal Configuration

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Event Filtering

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Electronic Calibration

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

FSW and LAT Initialization

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

FSW and LAT recovery

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

LAT Pointing Calculations

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

GRB Handling

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

GRB Detection

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Repointing Logic

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Safe Modes

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Science Modes

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Diagnostic and Calibration Modes

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Thermal Control System

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

LAT On-Orbit Initialization

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Sky Survey Mode

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Pointed Observation Mode

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

LAT Performance Verification

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

LAT Airborne End-to-End Test

| NAME | TEST ID ELX | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY Flight Software |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

I&T (WBS 4.1.9) System level tests

Inter-subsystem timing-in script

| NAME | TEST ID INT | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY I&T |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Inter-subsystem cross talk test

| NAME | TEST ID INT | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY I&T |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Data taking

| NAME | TEST ID INT | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY I&T |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

- Muons

  - External trigger

  - External trigger with lead

- Van de Graaff

Comprehensive test

| NAME | TEST ID INT | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY I&T |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Limited performance test

| NAME | TEST ID INT | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY I&T |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Aliveness test

| NAME | TEST ID INT | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY I&T |
| SYNOPSIS |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Single contributor trigger

| NAME | TEST ID INT101 | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY I&T |
| SYNOPSIS Check the relative efficiency of the 3-in-a-row trigger |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES None |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Single contributor synchronization

| NAME | TEST ID INT102 | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY I&T |
| SYNOPSIS Check for integrity of the combined tracker and calorimeter data from a single tower |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES TKR504 |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Single contributor muon survey

| NAME | TEST ID INT103 | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY I&T |
| SYNOPSIS TKR tray-to-tray alignment and CDE performance |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES TKR503 |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Multi-contributor synchronization

| NAME | TEST ID INT301 | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY I&T |
| SYNOPSIS Check for synchronization of the event data |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES INT200-INT215 |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

Multi-contributor high rate trigger

| NAME | TEST ID INT302 | SVAC ID |
| --- | --- | --- |
| ALIASES None | SUPERCEDES None | CATEGORY I&T |
| SYNOPSIS Check high rate trigger data integrity |
| AUTHOR TBD | OWNER/MAINTAINER/CONTACT PERSON TBD |
| MOTIVATION TBD |
| PREREQUISITES INT301 |
| REQUIRED EGSE |
| REQUIRED INPUT DATA OR FILES Configuration file | GENERATED OUTPUT FILES Test Report |
| COMPLETION STATUSES |
| DESCRIPTION |
| COMMENTS |

File formats

Files used as input or generated as output will have well known formats.  There are only two acceptable storage protocols: XML and FITS.

Schema and configuration files

Schema and configuration files are XML files.  They contain several blocks denoted by XML tags:

- schema

- configuration

- engineering units conversion (egu)

- rules

- constraints

These files are shared with Flight Software.

Calibration files

XML

- Dead tracker strips

- Noisy tracker strips

- Threshold data

FITS binary tables

- Calorimeter pedestal data

- ACD pedestal data

- TKR ToT calibration constants

Event data files

Event data is a FITS file containing event data in binary images.  The event data topology is described in LAT-TD-01546.

# Comments

OBE when TEMPowerUp is implemented