|  | Document # | Date Effective |
| --- | --- | --- |
|  | LAT-TD-07066-01 | March 26, 2004 |
|  | Author(s) | Supersedes |
|  | Richard Claus |  |
| LAT Interface Document |  |  |
|  | Subsystem/Office |
|  | Integration & Test/Online |
| Document Title |
| LAT I&T Online System Science Data Format: LDF |

This copy dated: 10/3/2005 11:29 AM

LAT I&T Online System Science Data Format: LDF

CHANGE HISTORY LOG

| Revision | Effective Date | Description of Changes |
| --- | --- | --- |
| 01 | March 29, 2004 | Preliminary release of incomplete document to FSW |

TABLE OF CONTENTS

1.	Purpose	4

2.	Scope	4

3.	Acronyms	4

4.	Definitions	6

5.	Applicable Documents	6

6.	The LAT Data Format	7

6.1.	lat Datagram	7

6.1.1.	The Identity word	7

6.1.2.	The Length word	9

6.2.	lat Datagram contribution	9

6.3.	ebf events	9

7.	Summary	9

8.	Parsing LDF data	11

8.1.	C++ API	11

8.1.1.	Mapping between electronics and detector space	11

8.1.2.	Accessing data elements	11

8.1.2.1.	Time	12

8.1.2.2.	Trigger	12

8.1.2.3.	ACD	12

8.1.2.4.	CAL	12

8.1.2.5.	TKR	12

8.1.2.6.	Errors	12

8.1.3.	Contributions	12

8.1.3.1.	Event Builder Format (EBF)	12

8.1.4.	Iterators	13

8.2.	Python API	13

Purpose

This document describes the data format used to store LAT science data.

Scope

The online system ...

Acronyms

ACD	LAT AntiCoincidence Detector subsystem

AEM	ACD Electronics Module

CAL	LAT Calorimeter subsystem

CCSDS	Consultative Committee for Space Data Systems

COTS	Commercial Off-The-Shelf

CU	Calibration Unit

EGSE	Electronics Ground Support Equipment

EM1	Engineering Model 1 EGSE

EM2	Engineering Model 2 EGSE

EPU	Event Processing Unit

FITS	Flexible Image Transport System

FSW	Flight SoftWare

FU	Flight Unit

GEM	Global trigger Electronics Module

GLT	GLobal Trigger

GUI     	Graphical User Interface

I&T	Integration and Test

ICS	Interface Control Systems – makers of SCL

IDL     	Interactive Data Language

LAN	Local Area Network

LAT	Large Area Telescope

ODBC	Open DataBase Connectivity

ROOT     	Rene's (?) Object Oriented Tool

RPC	Remote Procedure Call

RTE      	Run Time Engine

SAS	Science Analysis Software

SBC	Single Board Computer

SCADA	Supervisory Control And Data Acquisition

SCL      	Spacecraft Control Language

SSR	Solid State Recorder

TBD      	To Be Determined

TBR	To Be Resolved

TBS      	To Be Supplied

TEM      	Tower Electronics Module

TKR	LAT Tracker subsystem

Definitions

| 1553 | MIL-STD-1553 – An electronics bus standard that is used in GLAST for communication between the Spacecraft and the LAT |
| --- | --- |
| cPCI | Compact PCI: an electronics bus specification used on the LAT |
| Downstream | Data-path direction toward the user interface and persistent storage |
| Embedded system | The processors and associated software embedded in some approximation of the LAT. For EM-1 this is typically a VME crate containing a VME SBC, although cPCI components can also be used. |
| Upstream | Data-path direction toward instrument sensors |
| VME | An electronics bus specification |
| XML | Extensible Markup Language – a universal format for structured documents and data used on the Web and elsewhere |

Applicable Documents

| LAT-TD-00606 | LAT Inter-module Communications |
| --- | --- |
| LAT-TD-00639 | ACD Electronics Module (AEM) |
| LAT-TD-00605 | The Tower Electronics Module (TEM) |
| LAT-TD-01545 | The GLT Electronics Module (GEM) |
| LAT-TD-01546 | The Event Builder Module (EBM) |

The LAT Data Format

Data produced by the glast lat is stored in a format called the LAT Data Format (ldf).  ldf data contains ebf (Event Builder Format) data, amongst other contributions, in the native format of the ppc.  The lat uses the big endian mode of the ppc, and that has been allowed to drive the endianness of the rest of the ldf.  A software package called LDF has been created to parse ldf data.

lat Datagram

An ldf record consists of a structure with several layers.  The outermost layer is called a LATdatagram.  A LATdatagram consists of two data members: the identity field and the length field.  Both are 32 bit longwords (Figure 1).

Figure 1 Datagram format

The Identity word

The identity word is an encoded field containing two components.  The first component is the structure type identifier.  The least significant 20 bits are reserved for this field.  It is also sometimes called the Primary ID.  The remaining 12 bits form the Secondary ID and are used to store a version number of the type identifier.  Thus, identity words look like what’s shown in Figure 2.

Figure 2 Identity word format

TypeIds are uniquely assigned to data structures they describe.  The range of allowed values is broken up in sections of 0x1000 types.  This allows for 256 major blocks.  Blocks are assigned according to major disparate types, e.g. subsystems.  The currently defined type base values are shown in Table 1.  Base values were chosen to provide a characteristic appearance to facilitate their recognition in hexadecimal dumps of the data and also to avoid simple values like 0x00000000.  Specific type values are determined by offsets from a type base value.  All these values are kept in a file in the LDF package called LATidentity.h.

Table 1 TypeId (PrimaryID) block assignments

| Major Block | Name | Value |
| --- | --- | --- |
| Flight Software | BASE_FSW | 0xF0000 |
| Online Event Format | BASE_OEF | 0xF1000 |
| AntiCoincidence Detector | BASE_ACD | 0xF2000 |
| Calorimeter | BASE_CAL | 0xF3000 |
| Tracker | BASE_TKR | 0xF4000 |
| Online SoftWare | BASE_OSW | 0xF5000 |
| Scratch | BASE_SCRATCH | 0xFF000 |

Some specific typeIds are show in Table 2.

Table 2 TypeIds for specific data structures

| Major Block | Name | Value |
| --- | --- | --- |
| Event Builder Format | ID_EBF | 0xF0010 |
| EBF from Monte Carlos | ID_EBF_MC | 0xF0020 |
| LATdatagram | ID_Datagram | 0xF1010 |
| Unrecognized buffer | ID_UnrecBuf | 0xF1020 |
| OSW time structure | ID_Time | 0xF5010 |

The version space was similarly broken up in 0x100 chunks.  This allows for 256 versions of each typeId.  To further make the identity words easily recognizable, the initial version numbers assigned to the major blocks above start with the major block nibble, as shown in Table 2.  These values are also maintained in the LATidentity.h file of the LDF package.

Table 3 Initial version number (SecondaryID) assignments

| Major Block | Name | Value |
| --- | --- | --- |
| Flight Software | BASE_FSW | 0x000 |
| Online Event Format | BASE_OEF | 0x100 |
| AntiCoincidence Detector | BASE_ACD | 0x200 |
| Calorimeter | BASE_CAL | 0x300 |
| Tracker | BASE_TKR | 0x400 |
| Online SoftWare | BASE_OSW | 0x500 |
| Scratch | BASE_SCRATCH | 0xF00 |

Care must be taken to keep these identity values unique so that software can recognize which particular structure type it is dealing with.  A typical identity word value therefore looks like 0x102F0010, in this case describing the second version of the EBF event data format.

The Length word

The length field contains the length of the datagram in units of bytes.  The length is inclusive of the identity and length words themselves.  It also includes the size of the LATdatagram payload, also called a LATcontribution.  This simplifies navigation by software from one LATdatagram to the next since a char pointer to a LATdatagram only needs to be incremented by the length value to find the next LATdatagram in the list.

lat Datagram contribution

The payload of a LATdatagram is called a LATcontribution.  The form of a LATcontribution is shown in Figure 3.

Figure 3 The form of a LATcontribution

The identity word in the LATcontribution is the same form as described above in 6.1.1.  Currently, only two specific types of LATcontributions exist: ebf event data and Monte Carlo generated ebf event data.  Several other kinds of LATcontribution are envisioned for the future, for example, subsystem test application supplied opaque data, instrument configuration records, etc.

The second longword after the identity word contains the LATcontribution’s length and potentially some application dependent opaque data.  The two items are treated as unsigned shorts, in other words, 16 bits.  This implies that the maximum length of a LATcontribution is 64 Kbytes.

A particular type of LATcontribution is an EBFevent.  It uses the opaque word to store an acquisition status value.

ebf events

The topology of ebf events is described in LAT-TD-00606: “LAT Inter-module Communications” and LAT-TD-01546: “The Event Builder Module (EBM)”.  ebf events are made up of contributions from individual Electronics Modules.  The description of these contributions can be found in the corresponding documents:

- LAT-TD-01545: “The GLT Electronics Module (GEM)” for the GEM contribution,

- LAT-TD-00605: “The Tower Electronics Module (TEM)” for the TEM contribution (which covers both Calorimeter an Tracker data)

- LAT-TD-00639: “ACD Electronics Module (AEM)” for the AEM contribution

Summary

Figure 1 shows the generic layout of a LAT data event.

Figure 4 LAT datagram shape

Parsing LDF data

There is a software package by the name of LDF that can be used to parse buffers conforming to the ldf structure.  Both a C++ and a Python API are presented.  The APIs are documented using the doxygen (http://www.doxygen.org/index.html) in-line documentation method.  The resulting web pages from the C++ code are stored at http://www-glast.slac.stanford.edu/IntegrationTest/ONLINE/docs/LDF/ in folders corresponding to the package release number.  Thus, the main web page for release v5.6.2 is at http://www-glast.slac.stanford.edu/IntegrationTest/ONLINE/docs/LDF/doxygen_v05-06-02/html/index.html, for example.  The python API is not separately presented since it is the same as the C++ one, with the exception of syntax details.  The link for the version in use should be consulted for the API details.  What’s described in the sections below is the general philosophy of the package, and may not be correct in detail with respect to the version in use.

The active portion of LDF is generic C++ code.  It is compliable on both UNIX and Windows operating systems.  For UNIX, an automake/autoconf-style set of configuration and makefile files are provided.  For Windows a Visual Studio project file is used to build the package.

LDF is written to handle all byte ordering issues in the data without application intervention.  This can only work if the convention that the data is stored in big-endian format is adhered to.  The decision to store the data in big-endian format comes from the desire to not put extra load on the processors that produce it (PowerPCs).  The code is compiled according to the endianness of the CPU on which it is compiled.

The LDF package is basically a collection of classes providing accessor methods and iterators.

C++ API

Mapping between electronics and detector space

The following classes are used to map between electronics and detector space.

ACDmap

TWRmap

CALmap

TKRmap

Accessing data elements

EventSummary

Identifiers

LATPcellHeader

LATprimaryId

LATsecondaryId

LATtypeId

LDFversion

Time

OSWtimeBase

OSWtimeSpec

Trigger

GEMcondArrivalTime

GEMcontribution::sent_condArr

GEMonePPStime

GEMtileList

ACD

ACDpha

ACDtileSide

AEMheader

CAL

CALlog

CALlogEnd

CALdiagnostic

TKR

TKRstrip

TKRdiagnostic

Errors

ErrorSummary

GCCCerror

GTCCerror

GTRCerror

Contributions

LATdatagram

LATcontribution

EBFevent

Event Builder Format (EBF)

The Event Builder Format is made up of a bunch of contributions of type EBFcontribution.

OSWcontribution

OSWtimeContribution

GEMcontribution

GLTcontribution

AEMcontribution

TEMcontribution

CALcontribution

TKRcontribution

Iterators

LATdataBufferIterator

LATdatagramIterator

LDBI_LATdatagramIterator

LATcontributionIterator

LDBI_LATcontributionIterator

EBFeventIterator

LDBI_EBFeventIterator

EBFcontributionIterator

LATcomponentIterator

OSWcontributionIterator

AEMcontributionIterator

CALcontributionIterator

TKRcontributionIterator

DIAGcontributionIterator

ERRcontributionIterator

TEMcontributionIterator

LATcomponentIterator

Python API

Other than syntactical details, the Python API is essentially the same as the C++ one.

# Text boxes

19

20

31

0

Version

TypeId

Increasing Address

31

0

Length

Identity

Increasing Address

31

0

LATcontribution Identity

Increasing Address

Opaque

Length

Identity

EBFcontribution

EBFcontribution

LATdatagram Length

LATdatagram Identity

LATcontribution Opaque

LATcontribution Length

LATcontribution Opaque

LATcontribution Length

LATcontribution Identity

LATdatagram Length

LATdatagram Identity

LATcontribution Opaque

LATcontribution Length

LATcontribution Identity

EBF event

…

…