|  | Document # | Date |
| --- | --- | --- |
|  | LAT-TD-00640 | 22 July 2002 |
|  | Author(s) |  |
|  | Xin Chen, Eduardo do Couto e Silva |  |
| GLAST LAT System Specification |  |  |
|  | Subsystem/Office |
|  | Integration and Test |
| Document Title |
| LAT I&T SVAC Calibration Database |

Change History Log

| Revision | Effective Date | Description of Changes |
| --- | --- | --- |

Gamma Ray Large Area Space Telescope (GLAST)

Large Area Telescope (LAT)

Integration &Test Subsystem

The LAT I&T SVAC Calibration Constants Database

Contents

1.	Purpose	3

2.	Purpose	3

3.	Acronyms and Definitions	3

3.1.	Acronyms	3

3.2.	Definitions	3

4.	Applicable Documents	3

5.	Overview	4

6.	Servers	4

7.	Web interface	5

8.	Input Data	5

9.	Reports	5

10.	Data	5

10.1.	TKR	5

10.1.1.	Dead and Noisy Channels	5

10.1.2.	TOT	6

10.2.	CAL	6

11.	Metadata	12

12.	Queries	12

12.1.	TKR	13

12.2.	CAL	13

13.	Table Schema	15

14.	Data Size	19

15.	Relation among tables	20

- Purpose

This document describes the SVAC database to be implemented for the LAT integration activities.

- Purpose

This document presents details on the choice of technology and describes prototype queries and reports.

Acronyms and Definitions

Acronyms

ADC	Analog to Digital Converter

ASP	Active Server Pages

DAC	Digital to Analog Converter

EM	Engineering Model

FEE	Front-End Electronics

I&T	GLAST LAT Integration and Test

JAS	Java Analysis Studio

SAS	Science Analysis Software subsystem

SVAC	Science Verification Analysis and Calibration

OCI               Oracle Call Interface

Definitions

Subsystem:  A functional subdivision consisting of two or more components or assemblies.

System:  A functional subdivision consisting of two or more subsystems

Applicable Documents

LAT-MD-00573 " LAT I&T SVAC Plan for the Engineering Model"

LAT-TD-00640, “The implementation of histogram servlet under an NT environment”

LAT-TD-00680, “Servlets for the SVAC Engineering Model Database”

Overview

The primary calibration database (SAS database) is developed and maintained by the SAS group and is intended to support the necessary inputs to the reconstruction software. The SVAC database uses the same data but emphasizes on report generation, trend analysis and  a web based query system that produce histograms and graphs from the data stored in the database. Data from the SVAC database will reside in ORACLE. We plan to use as much as possible the technology already developed by the SAS subsystem. However, under the current Windows NT server setup, maintained by the SAS subsystem, only Active Server Pages (ASP) are supported. Currently ASP does not support binary writing functions nor graphical function libraries, which are necessary to build graphics “on the fly” as required by the SVAC database. There are two options to solve this problem: either  to use  a third party NT component or to develop in-house component (e.g. JAVA servlet). For this prototype we chose the latter approach (see LAT-TD-680) since we could use the existing development from Java Analysis Studio (JAS) used by the BaBar Collaboration.

Servers

In the current development there are 2 database servers. Unix where the ORACLE database  resides, TOMCAT that creates the environment for running Servlets.  Figure 1 shows a diagram with connections between servers. At the moment we don’t use ASP, clients interact directly with TOMCAT server.

Figure 1. Diagram of SVAC database

Web interface

The web interface must allow the graphical results from queries to be displayed in a page whose format is adequate for printing  (e.g. a single histogram is not split in more than one page).  At the moment, a prototype has been implemented using JAS libraries.

Input Data

Two steps are involved to input calibration data to SVAC database.

- To retrieve the calibration constants,  there are two options :

  - The SAS group developed an interface in GlastRelease so that the calibration data can be retrieved through this interface

  - An XML parser using Xerces library can be built which directly retrieve the calibration data from xml files.

We may choose the first approach since it shields us from potential changes in data format in future.

- Codes using OCI library is being implemented by the SVAC group to insert data into the database.

Reports

During data retrieval a software script will generate a summary report with the contents of the calibration data for archival in the SVAC database (TBD).

Data

Each calibration constant is uniquely identified using the schema described in the following section. Actual formats of tables in Oracle database will be described in the last two sections.

TKR

Table 1. TKR detector elements

|  | Tower | Trays/Tower | Layers/Tray | Ladders/Layer | SSD/Ladder | Strips/SSD |
| --- | --- | --- | --- | --- | --- | --- |
| Number | 16 | 19 | 2 | 4 | 4 | 384 |

Dead and Noisy Channels

In Table 2 the column view correspond to the position of the layer in a tray  (top or bottom), 0 for bottom and 1 for top

Table 2.TKR  Dead and Noisy channels

|  | Tower | Tray | View | Strip |
| --- | --- | --- | --- | --- |
|  | 0-15 | 0-18 | 0-1 | 0-1535 |
| Type | Int | int | int | int |

TOT

Calibration algorithm for TOT is under investigation.

Table 3. TOT

|  | Tower | Trays | View | TOTA | ErrorA | TOTB | ErrorB |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0-15 | 0-18 | 0-1 |  |  |  |  |
| Type | Int | Int | Int | Float | Float | Float | Float |

CAL

Following calibration constants are generated for the calorimeter:

- C14 - CAL Light Asymmetry:

- C15 - Light attenuation , light taper

- C16 - Light yeild (electrons per MeV)

  - for flight electronics - not needed : replaced by gain (adc/MeV) calibration

  - for PEM electronics - exist as IDL code, used for crystal acceptance test

- C17 -scintillation efficiency (for heavy ions): work is going on in France (Montpelier, Bordeaux)

- C18 - cal pedestals:

- C19 - CAL electronic gain (adc/MeV):

- C20 - Integral nonlinearity:

- C21 - differential nonlinearity:

- C22 - CAL noisy channels - doesn't exist (?)

- C23 - CAL dead channels - doesn't exist (?)

- C24 - CAL LO Discriminator - exist as Python script (Byron Leas)

- C25 - CAL HI Discriminator - exist as Python script (Byron Leas)

- C26 - CAL Zero-suppress threshold - exist as Python script (Byron Leas)

At the moment, the SAS software uses only 3 types of calibration constants from the calorimeter: light asymmetry, pedestal and electronic gain.  As described below, we defined table formats for most of the calibration constants list above. However, at the moment, we only intend to implement the three types of constants used by the SAS software. We should discuss whether the other constants are required.

Following two tables described the schema used to uniquely identify each calibration constants. Actual table formats used in the oracle database are described in the last two sections.

CAL detector elements

|  | Tower | Column | Layer | Crystals | Face/Crystal | Diodes/Face | Energy Range/Diode |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Number | 16 | 12 | 8 | 96 | 2 | 2 | 2 |

CAL energy ranges

| Range name | Description | Energy Range | Range number |
| --- | --- | --- | --- |
| LEX8 | Low Energy High Gain | < 200 MeV | 0 |
| LEX1 | Low Energy Low Gain | < 1.6 GeV | 1 |
| HEX8 | High Energy High Gain | < 12.5 GeV | 2 |
| HEX1 | High Energy Low Gain | < 100 GeV | 3 |

- CAL electronic gain (MeV/adc) (muon peak)

Description: Gain and width for  LEX8 range of each face for every crystal.

Output data:

|  | Tower | Column | Layer | Face | Range | Peak position (MeV/ADC) | Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0-15 | 0-11 | 0-7 | 0-1 | 0-3 |  |  |
| Type | int | Int | int | int | int | float | float |

- Light Asymmetry (muon slope)

Description  At the moment, light asymmetry is described as light attenuation length in the crystal in unit of mm (muon slope). If new method is used to calibrate light asymmetry, this format may change.

Output data:

|  | Tower | Column | Layer | Face | Range | Asymmetry |
| --- | --- | --- | --- | --- | --- | --- |
|  | 0-15 | 0-11 | 0-7 | 0-1 | 0-3 | mm |
| Type | int | Int | int | int | int | float |

- Light Attenuation (light taper)

Description  Relative variation  of scintillation light yield in a PIN diode with longitudinal position along CsI crystal, normalized to the light yield at the center of this crystal.

Output data:

|  | Tower | Column | Layer | Face | Range | Position (cm) | Attenuation |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0-15 | 0-11 | 0-7 | 0-1 | 0-3 | 0-32 | 0.5 - 2.0 |
| Type | int | Int | int | int | int | float | float |

- Light Yield

Description :   Number of photoelectrons in the diode, generated by 1 MeV of energy deposition at the center of the crystal.  This constant may not be required for flight unit calibration.

Output data:

|  | Tower | Column | Layer | Face | Diode | Light yield (e/MeV) | MeV (ADC units) |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0-15 | 0-11 | 0-7 | 0-1 | 0-1 | 0-4096 | 0-4096 |
| Type | int | int | Int | Int | int | Float | float |

- Scintillation Efficiency

Description   Light yield for heavy ions, divided by light yield for showers and minimum ionizing particles. Measure the scintillation light yield as a function of energy deposition for heavy ion beams with different Z. Number of different Z and dE/dx values – to be defined.

Output data:

|  | Tower | Column | Layer | Diode | dE/dx, | Z | Scintillation efficiency |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0-15 | 0-11 | 0-7 | 0-1 | 0.001 - 100 | 1-56 | 0.2 -1.0 |
| Type | int | Int | int | int | float | int | float |

- Integral non-linearity

Description: This is the look-up table which results from charge injection calibration and provides the conversion from possibly non-linear ADC scale to the linear DAC scale. The calibration input pulse height  is defined in terms of DAC settings. For each DAC setting one provides 1000 charge injection pulses and obtain the average ADC value of the peak of the distribution. The conversion is accomplished by using a look-up table where adjacent points are linearly interpolated.

Output data:

|  | Tower | Column | Layer | Face | Range | DAC Setting | ADC Value |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0-15 | 0-11 | 0-7 | 0-1 | 0-3 | 0-2000 | 0 -4095 |
| Type | Int | int | int | Int | Int | float | float |

- Differential non-linearity

Description:    The histogram of  ADC values produced by energy depositions with smooth spectrum, covering whole dynamic range of ADC, normalized by the source spectrum. For ideal ADC one should get the flat distribution with value=1.0 in each bin.

Output data:

|  | Tower | Column | Layer | Face | Range | ADC bin | Non-linearity |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0-15 | 0-11 | 0-7 | 0-1 | 0-3 | 0 -4095 | 0.5-1.5 |
| Type | Int | int | int | Int | Int | int | float |

Algorithm:

Notes:

- Pedestals

Pedestals correspond to an ADC output for zero input to front-end electronics (FEE).  There is a pedestal value per energy range of each crystal face. Each pedestal is characterized by a centroid and a width of a distribution of a given (TBD) number of triggers. Since there are two diodes in each of the two crystal faces, we will have eight pedestal distributions per crystal. A combination of Tower, Column and Layer uniquely identifies a crystal, so crystal numbers vary from 0 to 95 and should also be present in the database.

Output data:

|  | Tower | Column | Layer | Face | Range | ADC value |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Ped | Width |
|  | 0-15 | 0-11 | 0-7 | 0-1 | 0-3 | 0-1000 | 0-100 |
| Type | int | Int | Int | int | Int | float | float |

Algorithm:

Notes:

- Noisy Channels

Description:   list of channels with pedestal width value above defined limit.

Output data:

|  | Tower | Column | Layer | Face | Range |
| --- | --- | --- | --- | --- | --- |
|  | 0-15 | 0-11 | 0-7 | 0-1 | 0-3 |
| Type | Int | Int | int | int | int |

- Dead Channels

Description:   list of channels which doesn’t produce output signal

Output data:

|  | Tower | Column | Layer | Face | Range |
| --- | --- | --- | --- | --- | --- |
|  | 0-15 | 0-11 | 0-7 | 0-1 | 0-3 |
| Type | int | Int | int | int | int |

Algorithm:

Notes:

- Lo Discriminator

Description:  for each crystal face – the average signal value (in MeV) for which Lo discriminator output changes from false to true and the sigma (in MeV) of this transition, as a function of  DAC value defining this discriminator threshold. Calibration will be done for 10 different DAC settings

Output data:

|  | Tower | Column | Layer | Face | DAC setting | Threshold value (MeV) | Threshold width (MeV) |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0 | 0-11 | 0-7 | 0-1 | 0-4095 |  |  |
| Type | int | Int | int | int | int | float | float |

Algorithm:

Notes:

- Hi Discriminator

Description  :  for each crystal face – the average signal value (in MeV) for which Hi discriminator output changes from false to true and the sigma (in MeV) of this transition, as a function of  DAC value defining this discriminator threshold. Calibration will be done for 10 different DAC settings.

Output data:

|  | Tower | Column | Layer | Face | DAC setting | Threshold value (MeV) | Threshold width (MeV) |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0 | 0-11 | 0-7 | 0-1 | 0-4095 |  |  |
| Type | int | Int | int | int | int | float | float |

Algorithm:

Notes:

- Zero Suppress Threshold

Description:  zero suppress threshold defines the minimum signal necessary in given channel to triger its digitization and readout.

Output data:

|  | Tower | Column | Layer | Face | DAC setting | Threshold value (MeV) | Threshold width (MeV) |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0 | 0-11 | 0-7 | 0-1 | 0-4095 |  |  |
| Type | int | Int | int | int | int | float | float |

Algorithm:

Notes:

Metadata

Metadata will be stored in the SVAC database using the following format.  In general each data record should be accompanied by the following information (most of it extracted from the SAS tables).

Table 10. Metadata

| Instrument calibrated | Engineering Model (EM), Calibration Unit (CU) or Flight Unit (LAT) |
| --- | --- |
| Location of calibration | SLAC-Clean Room, SLAC-Beam Test, NRL-Environmental test, Airplane, Mission Integration, On-orbit |
| Orbit Position | If on-orbit, specify either RA or DEC or latitude or longitude (TBD) |
| Particle Type | Cosmic Rays, Photons, Positrons, Hadrons |
| Temperature | Temperature in degree Celsius of the location of the instrument calibration (or a given point within the instrument – TBD) |
| Humidity | Relative Humidity in % of the location of the instrument calibration |
| Calibration type | e.g., TKR noisy channel, CAL light asymmetry, ACD pulse height etc. |
| Serial number | Unique serial number for this record and the corresponding calibration output (TBD: is the serial number unique over all records, just for records for this calibration type, or do we want two serial numbers?). This is useful for SAS, is it useful for SVAC too ? |
| Validity start time | Demarcate time interval for which calibration is known to be valid |
| Validity end time | Demarcate time interval for which calibration is known to be valid |
| Procedure completion time | Time the dataset was made |
| Calibration procedure level | Possible values will come from a predefined list including 'test', 'development', 'production' and 'superseded'. These terms refer to the procedure being used and say nothing about whether the component being calibrated was deemed acceptable. |
| Calibration status | Possible values will come from a predefined list including 'OK' and things like 'incomplete' or 'aborted' |
| Data size | Could be number of bytes, number of records, or something else. Precise meaning will depend on data format and calibration type. |
| Creator | Could be hardware procedure or software algorithm. Should also include procedure or software version information. |
| Comment field | Anything which might be of interest but doesn't fit in any of the other categories. |

Queries

The query system shall allow all queries to be displayed for a given detector (e.g. CAL or TKR). The default values will be the last calibrations performed.

  - TKR

Must be able to query database according to different combinations of primary keys. This can be implemented by combination of various check boxes / drop down menus.

12.1.1 Noisy channel and dead channel

Latest page:  tables of no of dead/noisy channels on each layer from latest measurement.

History page: plots of no of dead/noisy channels vs. time.  In the plots, time is represented as  a set of sequence numbers corresponding to dates of different measurements. Two tables are displayed to show relationship between the sequence numbers and the measurement dates.

Detail page:  Drop down menus to let users to select tower, biLayer and date of the measurements. Four histogram plots to show dead/noisy channel ids according to selection. A table button allows users to see details of dead/noisy strips.

    - Time over threshold distribution

Latest calibration page:  Table of latest TOT data with drop down menu to select different tower.

History page:  4 X-Y plots: TOT data vs. date. Drop down menus select different towers and bi-layers.

Detail page:  4 X-Y plots: TOT data vs. bi-layer no. Drop down menus select different towers and dates.

CAL

Must be able to query database according to different combinations of primary keys. This can be implemented by combination of various check boxes / drop down menus. Can we do date?

    - Electronics Gain

Histogram:  Muon peak for every tower, column, layer, face and position

X-Y plot: Peak value vs. date

Peak value vs.  layer

    - Light Asymmetry

Histogram:  Light asymmetry for every tower, column, layer, range and position

X-Y plot:  Mean light asymmetry vs. date

12.2.3    	  Light Attenuation

Histogram:  Light attenuation for every tower, column, layer, face range and position

X-Y plot: Mean light attenuation value vs. date

Mean light attenuation value vs.  position

    - Light yield

Histogram:  light yield for every tower, column, layer, face and diode

X-Y plot: Mean light yield value vs. date

Mean light yield value vs.  ADCValue

12.2.5.  Scintillation Efficiency

Histogram:  Scintillation efficiency for every tower, column, layer, diode

X-Y-Z plot: Mean scintillation efficiency value vs. dEdX and Z

    - Integral non-linearity

X-Y plot: Mean ADC value vs. DAC setting

    - Differential non-linearity

X-Y plot:   Mean Non-linearity vs. ADC bin

12.2.7  Pedestals

Histogram:  Pedestal value, pedestal width

X-Y plot:   Mean pedestal value vs. date

Mean pedestal width vs.  date

12.2.8 Electronic gain

Histogram:  Electronic gain

X-Y plot:   Mean gain vs. date

12.2.9 Noisy channel and dead channel

X-Y plot:   no of noisy channels vs. tower

no of noisy channels vs. layer

no of noisy channel vs. no of dead channel

no of dead channels vs. tower

no of dead channels vs. layer

  - Lo  Discriminator

X-Y plot:  Threshold value vs. DAC setting

Threshold width vs. DAC setting

12.3.1  Hi  Discriminator

X-Y plot:  Threshold value vs. DAC setting

Threshold width vs. DAC setting

    - Zero Suppress Threshold

X-Y plot:  Threshold value vs. DAC setting

Threshold width vs. DAC setting

This is a list of queries that must be supported in the form of histograms

- Pedestal values for all diodes for all four gain ranges

- Pedestal width values for all diodes for all four gain ranges

This is a list of queries that must be supported in the form of an XY graph

- Pedestal versus width values for all diodes for all four gain ranges

Table Schema

PK = Primary Key, FK = Foreign Key, I = Index, TBD = To Be Defined

  - Description tables

Some basic info such as location of calibration are stored as integers in the data tables to reduce table size and improve query performance. The description tables explain meaning of the integers and also serve as constraints to improve data integrity. Table definitions are shown below:

1.Calibration source:

| Column Name | CalSrcID (PK) | Description |
| --- | --- | --- |
| Data Type | Integer | Varchar2 |

2. Hardware

| Column Name | HardwareID (PK) | Description |
| --- | --- | --- |
| Data Type | Integer | Varchar2 |

3. Location

| Column Name | LocationID (PK) | Description |
| --- | --- | --- |
| Data Type | Integer | Varchar2 |

4. CalibrationType

This table may not be necessary in I&T database as calibration type can be directly deduced from namesof data

tables.

| Column Name | CalTypeID (PK) | Description |
| --- | --- | --- |
| Data Type | Integer | Varchar2 |

5. CalibrationProcedureLevel

| Column Name | CalProcLevelID (PK) | Description |
| --- | --- | --- |
| Data Type | Integer | Varchar2 |

6. CalibrationStatus

| Column Name | CalStatusID (PK) | Description |
| --- | --- | --- |
| Data Type | Integer | Varchar2 |

13.2  Index tables

There are many duplicated info such as tower no and column no in the calibration data tables. Index tables gather these info together, it not only reduce data size significantly but also improve the query speed. Table definitions are shown below:

- CalibrationDescription

Each row in this table describes situation of each calibration test such as test start time and test end time.

CalDesID is a oracle sequence number

| Column Name | CalDesID (PK) | LocationID (FK, I) | CalSrceID(FK,I) | StartTime (I) |
| --- | --- | --- | --- | --- |
| Data Type | Integer | Integer | Integer | Date |
| Column Name | EndTime (I) | DataCreationTime (I) | OrbitPosition | Temperature |
| Data Type | Date | Date | TBD | Number |
| Columnd Name | Humidity | Hardware ID(FK, I) | CalTypeID(FK, I) | CalProLevelID(FK, I) |
| Data Type | Number | Integer | Integer | Integer |
| Column Name | CalStatusID(FK, I) | DataSize | Creator | Description |
| Data Type | Integer | Number | Varchar2 | Varchar2 |

2 CALInstrument

Note it is “Ccolumn” instead of “Column” as “Column” is the key word and can not be used as the column name.

CalInstrumentID is calculated as column+layer*12+tower*8*12

| Column Name | CalInstrumentID (PK) | Tower (I) | CColumn (I) | Layer (I) |
| --- | --- | --- | --- | --- |
| Data Type | Integer | Integer | Integer | Integer |

3. CALIndex

This table combines indexes from the CalibrationDescription table and the CALInstrument table.

CalIndexID is a oracle sequence number

| Column Name | CalIndexID (PK) | CalDesID(FK,I) | CALInstrumentID (FK,I) |
| --- | --- | --- | --- |
| Data Type | Integer | Integer | Integer |

4. TKRInstrument

TkrInstrumentID is calculated as pos+tray*2+tower*2*20

| Column Name | TkrInstrumentID (PK) | Tower (I) | Tray (I) | Pos (I) |
| --- | --- | --- | --- | --- |
| Data Type | Integer | Integer | Integer | Integer |

5. TKRIndex

This table combines indexes from the CalibrationDescription table and the TKRInstrument table.

| Column Name | TkrIndexID (PK) | CalDesID(FK,I) | TKRInstrumentID (FK,I) |
| --- | --- | --- | --- |
| Data Type | Integer | Integer | Integer |

  - Data tables

    - TKR data tables

- TKRNoisyChannel

TkrNoisyChID is an oracle sequence to serve as the primary key.

| Column Name | TkrNoisyChID(PK) | TKRIndexID(I) | Strip(I) |
| --- | --- | --- | --- |
| Data Type | integer | Integer | Integer |

- TKRDeadChannel

TkrDeadChID is an oracle sequence to serve as the primary key.

| Column Name | TKRDeadChID(PK) | TKRIndexID(I) | Strip(I) |
| --- | --- | --- | --- |
| Data Type | integer | Integer | Integer |

- TKRFEElectronics

TKRFEElectronicsID is an oracle sequence to serve as the primary key.

| Column Name | TKRFEElectronicsID(PK) | TKRIndexII, FK) | CardNo(I) |
| --- | --- | --- | --- |
| Data Type | Integer | Integer | Integer |
| Column Name | ThresholdDAC | Occupancy | CountingRate |
| Data Type | Integer | Number | Number |
| Column Name | ErrRate | TOTA | TOTB |
| Data Type | Number | Integer | Integer |

- TKRTimeOverThreshold

TKRTimeOverThresholdID is an oracle sequence to serve as the primary key

| Column Name | TKRTimeOverTID(PK) | TKRIndexII, FK) | TOTA |
| --- | --- | --- | --- |
| Data Type | Integer | Integer | Number |
| Column Name | ErrTOTA | TOTB | ErrtTOTB |
| Data Type | Number | Number | Number |

    - CAL data tables

1.CALElectronicGain

CalElectronicGainID is an oracle sequence to serve as the primary key.

| Column Name | CalElectronicGainID (PK) | CALIndexID(I,FK) | Face(I) | Range(I) | Peak | Width |
| --- | --- | --- | --- | --- | --- | --- |
| Data Type | integer | Integer | Integer | Integer | Number | Number |

2.CALLightAsymmetry

CalLightAsyID is an oracle sequence to serve as the primary key.

| Column Name | CalLightAsyId (PK) | CALIndexID(I,FK) | Face(I) | Range(I) | LightAsymmetry |
| --- | --- | --- | --- | --- | --- |
| Data Type | integer | Integer | Integer | Integer | Number |

3. CALLightAttenuation

CalLightAttId is an oracle sequence to serve as the primary key.

| Column Name | CalLightAttId(PK) | CALIndexID(I,FK) | Face(I) | Range(I) | Position(I) |
| --- | --- | --- | --- | --- | --- |
| Data Type | integer | Integer | Integer | Integer | Number |
| Column Name |  | LightAttenuation |  |  |  |
| Data Type |  | Number |  |  |  |

4. CALLightYield

CalLightYieldID is an oracle sequence to serve as the primary key.

| Column Name | CalLightYieldId(PK) | CALIndexID(I,FK) | Face(I) | DiodeI) | LightYield |
| --- | --- | --- | --- | --- | --- |
| Data Type | integer | Integer | Integer | Integer | Number |
| Column Name |  | ADCValue |  |  |  |
| Data Type |  | Number |  |  |  |

5. CALScintillationEfficiency

CalScinEffID is an oracle sequence to serve as the primary key.

| Column Name | CalScinEffId(PK) | CALIndexID(I,FK) | Diode(I) | dEdX(I) | Z(I) |
| --- | --- | --- | --- | --- | --- |
| Data Type | Integer | Integer | Integer | Number | Integer |
| Column Name |  | ScintillationEfficiency |  |  |  |
| Data Type |  | Number |  |  |  |

6. CALIntegralNonLinearity

CalIntNonLinearID is an oracle sequence to serve as the primary key.

| Column Name | CalIntNonLinearId (PK) | CALIndexID(I,FK) | Face(I) | Range(I) | DACSetting(I) |
| --- | --- | --- | --- | --- | --- |
| Data Type | integer | Integer | Integer | Integer | Number |
| Column Name |  | ADCValue |  |  |  |
| Data Type |  | Number |  |  |  |

7. CALDifferentialNonLinearity

CalDiffNonLinearID is an oracle sequence to serve as the primary key.

| Column Name | CalDiffNonLinearID (PK) | CALIndexID(I,FK) | Face(I) | Range(I) | ADCBin(I) |
| --- | --- | --- | --- | --- | --- |
| Data Type | Integer | Integer | Integer | Integer | Integer |
| Column Name |  | DifferentialNonLinearity |  |  |  |
| Data Type |  | Number |  |  |  |

8. CALPedestal

CalPedGainID is an oracle sequence to serve as the primary key.

| Column Name | CalPedestalID (PK) | CALIndexID(I,FK) | Face(I) | Range(I) |
| --- | --- | --- | --- | --- |
| Data Type | integer | Integer | Integer | Integer |
| Column Name |  | ADCPedestalValue | ADCPedestalWidth |  |
| Data Type |  | Number | Number |  |

9. CALNoisyChannel

CalNoisyChID is an oracle sequence to serve as the primary key.

| Column Name | CalNoisyChId(PK) | CALIndexID(I,FK) | Face(I) | Range(I) |
| --- | --- | --- | --- | --- |
| Data Type | integer | Integer | Integer | Integer |

10. CALDeadChannel

CalDeadChID is an oracle sequence to serve as the primary key.

| Column Name | CalDeadChId(PK) | CALIndex3ID(I,FK) | Face(I) | Range(I) |
| --- | --- | --- | --- | --- |
| Data Type | integer | Integer | Integer | Integer |

11. CALDiscriminatorZeroSuppress

CalDisZeroID is an oracle sequence to serve as the primary key.

| Column Name | CalDisZeroId (PK) | CALIndexID(I,FK) | Face(I) | DACSetting(I) | LoThresholdValue |
| --- | --- | --- | --- | --- | --- |
| Data Type | integer | Integer | Integer | Integer | Number |
| Column Name |  | LoThresholdWidth | HiThresholdValue | HiThresholdWidth | ZeroSuppressThresholdValue |
| Data Type |  | Number | Number | Number | Number |
| Column Name |  | ZeroSuppressThresholdWidth |  |  |  |
| Data Type |  | Number |  |  |  |

Data Size

Following table presents estimated data size produced by every calibration process in a single calibration run.

| Calibration Type | Data Size (byte) | Comment |
| --- | --- | --- |
| CalibrationDescription | ~ 364 | Assume description is short, less than 200 characters |
| CALInstrument | ~24576 |  |
| CALIndex | ~18432 |  |
| TKRInstrument | ~9216 |  |
| TKRIndex | ~6912 |  |
| TKRNoisyChannel | ~10368 | Assume 0.1% channels are noisy |
| TKRDeadChannel | ~10368 | Assume 0.1% channels are dead |
| TKRTimeOverThreshold | ~13824 |  |
| CALElectronicGain | ~294912 |  |
| CALLightAsymmetry | ~245760 |  |
| CALLightAttenuation | ~9437184 | Assume a crystal is divided into 32 bins |
| CALLightYield | ~147456 |  |
| . CALScintillationEfficiency | ~1474560 | Assume using 10 different heavy elements |
| . CALIntegralNonLinearity | ~1474560 | Assume using 10 different DAC settings |
| CALDifferentialNonLinearity | ~1474560 | Assume using 10 ADC bins |
| CALPedestal | ~147456 |  |
| CALNoisyChannel | ~200 | Assume 0.1% channels are noisy |
| CALDeadChannel | ~200 | Assume 0.1% channels are dead |
| CALDiscriminatorZeroSuppress | ~1105920 | Assume 10 DAC settings |
| Total | ~ 16 MB |  |

Sizes of description tables are negligible.  Because we have to build many indexes in order to speed up the query, the actual size could be 30% more than the size calculated above.

Relation among tables

Following is a graphic presentation of relations among tables in the SVAC database.