| Table 3. Test Instrumentation (page 1 of 2) - Thermocouples | Rev Date: | 03-Mar-02 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Print Date: | 11-Feb-04 |  |  |  |  |  |
|  | Description of Instrumentation |  | Source of Instrumentation |  |  |  |  |  |
|  |  |  |  |  |  | Side of | Test Instrument. |  |  |  |
| Line # | Description | Type | Part No. | SS | Location | Shield | Fly-Away | Remov. | Total | Count |
| 1 | ACD TDA tile TS | Thermocouple |  | ACD | On ACD tiles at center of each (out)side | Out | 5 |  | 5 | 1 x 5 surfaces |
| 2 | ACD mount TS | Thermocouple |  | I&T | ACD side of 4 corner & 4 mid-side structure mounts | Out |  | 8 | 8 | 1 x 4 interfaces |
| 3 | Deleted |  |  |  |  |  |  |  | 0 |  |
| 4 | CAL baseplateTS | Thermistor |  | I&T | Center of CAL baseplate, -Z surface | In | 16 |  | 16 | 1/baseplate |
| 5 | T-Vac support TC | Thermocouple |  | I&T | LAT mount point on T-Vac stand | Out |  | 4 | 4 | 1 x 4 mount bosses |
| 10 | SC mount TC | Thermocouple |  | I&T | Grid at SC mount boss (LAT side) | Out |  | 4 | 4 | 1 x 4 mount bosses |
| 6 | SC simulator panel TC | Thermocouple |  | I&T | 1 on each side of SC simulator | Out |  | 5 | 5 | 1 x 5 sides |
| 7 | Chill bar TC | Thermocouple |  | I&T | On chill bars mount to Grid X-sides | Out |  | 8 | 8 | 2 per x 4 chill bars |
| 8 | T-Vac chamber TC | Thermocouple |  | I&T | T-Vac chamber walls, ceiling | Out |  | 20 | 20 | 20 on chamber |
| 9 | X-LAT sink plate TC | Thermocouple |  | I&T | Corners and middle of sink plate | Out |  | 5 | 5 | 5 points on plate |
| 11 | Rad Mnt Bkt TC | Thermocouple |  | I&T | Ends of Radiator Mount Bracket, near radiator | Out |  | 4 | 4 | 1 x 4 interfaces |
| 14 | Radiator top mount TC | Thermocouple |  | I&T | Radiator at mount to Rad Mnt Bkt | Out |  | 4 | 4 | 1 x 4 mount points |
| 12 | VCHP mount point TC | Thermocouple |  | I&T | VCHP at connection to DSHP | Out |  | 12 | 12 | 1 x 12 VCHP's |
| 13 | XLHP TC | Thermocouple |  | I&T | Ends of X-LAT heat pipes | Out |  | 12 | 12 | 2x3 XLHP'sx2 Ends |
| 15 | Radiator bot mount TC | Thermocouple |  | I&T | Radiator at mount to SC struts | Out |  | 4 | 4 | 1 x 4 mount points |
| 25 | SC-side of RAD structure | Thermocouple |  | I&T | RAD struts near SC | Out |  | 4 | 4 | 1 x 4 struts |
| 16 | Rad VCHP TC | Thermocouple |  | I&T | VCHP's at top of Radiator (Side of S-bend) | Out |  | 12 | 12 | 1 x 12 VCHP's |
| 17 | VCHP reservoir TC | Thermocouple |  | I&T | VCHP reservoirs | Out |  | 12 | 12 | 1 x 12 reservoirs |
| 18a | Radiator panel TC | Thermocouple |  | I&T | On Rad panel | Out |  | 20 | 20 | 2 Rad's x 10/Rad |
| 18b | Radiator panel TC | Thermocouple |  | I&T | On Rad panel | Out |  | 4 | 4 | 2 Rad's x2/Rad |
| 19 | TKR top center TS | Thermocouple |  | I&T | Top center of ctr. TKR module (+Z surface) Bay# 5, 6, 9, 10 | Out | 4 |  | 4 | 1 x 4 modules |
| 20 | TKR top center TS | Thermocouple |  | I&T | Top center of edge & corner TKR modules (+Z surface) | In | 12 |  | 12 | 1 x 12 modules |
| 21 | TKR top perimeter TS | Thermocouple |  | I&T | Sides of perimeter modules facing ACD, 15mm below top | Out | 16 |  | 16 | 1x 2sides x4+1x 8sides |
| 22 | X-LAT Plate | Thermocouple |  | I&T | -Z-side of X-LAT Plate on heat pipes | Out |  | 6 | 6 | 1/heat pipe |
| 23 | E-Boxes TS | Thermistor |  | Elect | Top surface (+Z) of E-Boxes in Bay# 0, 3, 4, 6, 7, 10, | In | 6 |  | 6 | 1/ box stack |
| 24 | E-Boxes TS | Thermistor |  | Elect | Top surface (+Z) of E-Boxes in all other bays | In | 10 |  | 10 | 1/ box stack |
| 26 | Downspout HP | Thermocouple |  | I&T | On HP and opposite on GRID, at 1/4 and 2/3 along HP length. | Out |  | 48 | 48 | 4 each x 12 HPs |
|  | Notes: (1) Temperature sensors in shaded areas are retained for Observatory testing, total = 16+4+16+6+4+4+4 |  | 54 |  |  |  |
|  | (2) The following line # goes together: 11&14, 5&10, 15&25, 19&20. |  |  |  |  |  |
|  | (3) "SS" indicates which subsystem is responsible for purchase of the test sensors |  |  |  |  |  |