ACD CDR RFA #3

Requestor:	Jim Ryan	301-286-4975		GSFC/543

Subject Area:	Testing

Specific Request:

Demonstrate adequate venting of the tile detector assemblies and the micrometeoroid shield.

Rationale:

Tile detector assemblies are wrapped well to be light tight.  Trapped air must be adequately vented to prevent damage to light tight covering during ascent.

The micrometeoroid shield (MMS) venting scheme was not clear at CDR.  Need to finalize the design and demonstrate that trapped air can adequately vent from under the MMS.