ACD CDR RFA #8

Requestor:	Ted Michalek		301-286-1956		GSFC/545

Subject Area:	Thermal

Specific Request:

Check to make sure that the thermal conduction from the BFA to the LAT grid is representative of the planned mechanical connection of the BFA to the LAT grid.

Rationale:

Since shims will be used to make the BFA to LAT grid mechanical joints, this may not give a good thermal conductive interface.