ACD CDR RFA #5 Response

Requestor:	Ted Michalek	301-286-1956		GSFC/545

Steve Scott	301-286-2529		GSFC/500

Subject Area:	EMI/EMC

Specific Request:

Provide the concept and details of how the various layers of the micrometeoroid shield will be electrically grounded to prevent static charge build up within and between the layers.

Rationale:

It’s not obvious how this will be done since it seems to require a certain level of sheet electrical conductivity within each layer of the shield.

Responder:  Tom Johnson		x61284	Code 556

Response:

The micrometeoroid shield will be sandwiched between a grounded MLI Thermal Blanket and a grounded piece of aluminized Kapton. The MLI and aluminized Kapton will be grounded following standard Goddard procedures, using ground straps attached to the LAT instrument grid.  The grounding procedure is that used for the EGRET instrument on the Compton Observatory, which had a similar shield.