# LAT CAL-Grid Peer Review RFA Response #3

Action Requested:

Include lateral load factor with vertical 1 G for crane lifting

Reason:

Suggest use 0.25 G's lateral within 1 G vertical for crane lifting case

Response:

SLAC is not comfortable reducing the Z-direction loading to 1.0g and would like to keep the current level at 1.25g.  The lateral loads have been increased (X & Y axes applied separately) from 0.0g to 0.25g, as requested by Swales.  Margins are reduced, but remain positive.