Request For Action Number: 20 Project Gamma-ray Large Area Space Telescope (GLAST) System/Instrument: Large Area Telescope (LAT) Review: Critical Design Review (CDR) Date: May 12-16, 2003 Originator: Tom McCarthy Phone: 301-286-4710 Organization: GSFC/545 Category: Thermal Title: Thermal Design Failure Mitigation Scenario Action Requested: a) Investigate the addition of over-temperature thermostats to VCHP reservoir to preclude over-temperature condition identified in failure analysis summary on chart 40. b) Evaluate the use of dual line CCHP (versus baselined single line CCHP) to the X–LAT heat pipe panel at GASU location. Supporting Rationale: a) Over-temperature of the VCHP reservoir could result in catastrophic loss of radiator. b) Design needs to be one heat pipe failure tolerant. This design does not meet this requirement. Project Response: