Request For Action Number: 30 Project Gamma-ray Large Area Space Telescope (GLAST) System/Instrument: Large Area Telescope (LAT) Review: Critical Design Review (CDR) Date: May 12-16, 2003 Originator: Steve Scott Don Kniffen Phone: 301-286-2529 Organization: GSFC/500 Category: Testing Title: Beam Test Plan Action Requested: The test plan shows no tagged photons between 17.6 MeV and 100 MeV. The gap between these two energies represents an energy range where the instrument sensitivity varies most rapidly with energy. In principle, bremsstrahlung photons can be produced in this gap. A couple of energy points should be inserted in the beam test plan. Supporting Rationale: The energy range below 100 MeV is very important astrophysically. The instrument response in this region needs to be confirmed. Project Response: