Request For Action Number: 33 Project Gamma-ray Large Area Space Telescope (GLAST) System/Instrument: Large Area Telescope (LAT) Review: Critical Design Review (CDR) Date: May 12-16, 2003 Originator: Jim Rose Phone: 818-354-4491 Organization: HQ/IRT Category: Systems Engineering Title: Possible Temperature Rise Due to Rise in Detector Event Rate Action Requested: Describe the design/operations process/procedure that will prevent excessive temperature rise due to extraordinary event rate of detections (exciting science) sustained for multiple hours. a) What causes the instrument to reach its maximum power consumption? b) What limits the duration of this maximum power state? c) Is it possible to exceed temperatures predicted on a 750 W for 10 minutes specification basis? Supporting Rationale: Don’t know about the universe, but it seems like the hot thermal case is marginal, and the instrument could exceed the 10 minute limit on maximum power consumption. Project Response: