Request For Action Number: 7 Project Gamma-ray Large Area Space Telescope (GLAST) System/Instrument: Large Area Telescope (LAT) Review: Critical Design Review (CDR) Date: May 12-16, 2003 Originator: Fred Huegel Chris Bebek Phone: 301-286-2285 510-486-6447 Organization: GSFC/560 LBNL Category: Electrical Title: Verification Plan for LAT Hardware and FSW Control of VCHP Action Requested: Provide a verification plan for LAT hardware and flight software control of VCHP, including required LAT hardware and fight software support at Lockheed-Martin for VCHP testing. Supporting Rationale: Lockheed will provide algorithm for processing greater than 100 temperature sensors into twelve “on” times for VCHP heaters. LAT electronics and flight software are responsible for control of the heaters. The plan for verifying electrical/flight software with VCHP was described. Project Response: