Request For Action Number: Suggestion Project Gamma-ray Large Area Space Telescope (GLAST) System/Instrument: Large Area Telescope (LAT) Review: Critical Design Review (CDR) Date: May 12-16, 2003 Originator: Tom McCarthy Phone: 301-286-4710 Organization: GSFC/545 Category: Thermal Title: Improving Radiator Efficiency Action Requested: Consider adding horizontal CCHPs to radiator to increase radiator efficiency, and thereby gain some thermal design margin on Tracker temperature. Supporting Rationale: a) Changes to radiator configuration for PDR have decreased radiator efficiency. In addition, instrument dissipation has increased by 12 W. b) Note that in test, the horizontal heat pipe won’t operate and this efficiency will only be realized on orbit. Project Response: