# LAT CDR RFA #13 Response

# Action Requested:

a) Perform detailed dimension study. Crane hook height appears inadequate for installation of ACD:

I&T. pg 30 – crane hook height = 134 in.

I&T, pg 31 – ACD needs              124 in.

10 in.

Lift Fixture Box Beam, pg 32 -       -6 in.

Difference (including ACD Clearance and Crane Fittings = 4 in.

b) Provide information on the clean room entrances and clearances that will exist when equipment (including GSE) is brought in and out.

# Supporting Rationale:

a) Risk of damage to ACD hardware during installation, or inadequate facilities to perform operation.  Minimum clearance between the bottom of the ACD and top of tracker recommended to be at least 6 inches.

b) Not enough detail presented.

# Response:

- SLAC will develop a low profile integration stand. When ready for ACD mate operations, the LAT will be lifted from the Rotation / Support Stand and set onto the low profile stand.  The crane lift block maximum height is 134 inches [3,403 mm] (Hook removed). The available clearances assume an 8” [203 mm] high spreader (i.e., rectangular structural tubing that is also 6” wide and 0.375” thick). See figures below.

Figure 1: LAT with ACD To/From the Rotation Stand

Figure 2: ACD Installation, Low Profile Integration Stand

- Large, double door to Class 100K crane room is 111” [2,819 mm] wide by 108” [2,743 mm)] high.  Small, single door to Class 100K clean room is 59” [1,499 mm] wide by 79” [2,007 mm] high.  The LAT on the integration stand, the low profile ACD integration stand and the 8’ x 8’ x 6.2’ tall ACD dolly all fit in the room.  See figure below.