# LAT CDR RFA #16 Response

# Action Requested:

The low-level sine sweep test out to 150 Hz for assessment of the MECO high frequency transient event was not presented for any of the LAT subsystems.  This testing is required by the MAR, and would be best performed at both the subsystem and LAT levels.  Finding issues during subsystem testing reduces risk.

Supporting Rationale:

At a minimum the LAT level test must be performed.

# Response:

Sine sweep testing of the LAT up to 150 Hz is part of the LAT dynamics test baseline.  This is described in LAT-MD-01196, the "LAT Dynamics Test Plan."  However, sine sweep testing of LAT subsystem up to 150 Hz is NOT required by the MAR, so not all subsystems will perform this.  Subsystems with high natural frequencies, such as the TKR and CAL, will by default capture modes up to 150 Hz as part of their normal testing, but a 150 Hz sine sweep is not planned as a discrete test.