# LAT CDR RFA #2 Response

# Action Requested:

Provide a LAT baseplate mock-up to the harness manufacturer for harness fabrication.

Supporting Rationale:

The LAT electrical system harness is a fairly complex one with tight spacing in areas.  Wiring to a harness mock-up will provide the best fit harness with the least amount of stress at the connectors.

# Response:

LAT electronics is designing cables to a mock-up and resulting cable drawings will be provided to an outside vendor for assembly.  The harness lengths were double checked on the LAT test bed, which is a higher fidelity model of the LAT.  The harness fabrication will not use the mockup.  Multiple sets of the harness will be built, with one of the sets installed on the test bed to verify harness lengths (and electrical connectivity) before the harness is installed in the LAT.

Fred Huegel comment 8/13/04

SLAC responds that they will measure the harness length on a mock-up but will not fabricate the harness on a mock-up. This is not best aerospace practice. If this were a simple harness I would not be so concerned but the LAT electrical system harness is a fairly complex one with tight spacing in several areas.  Wiring to a harness mock-up would provide the best fit harness with the least amount of stress at the connectors.