# LAT CDR RFA #2 Response

# Action Requested:

Provide a LAT baseplate mock-up to the harness manufacturer for harness fabrication.

Supporting Rationale:

The LAT electrical system harness is a fairly complex one with tight spacing in areas.  Wiring to a harness mock-up will provide the best fit harness with the least amount of stress at the connectors.

# Response:

LAT electronics is designing cables to a mock-up and resulting cable drawings will be provided to an outside vendor for assembly.  We will give the cable assembly house the option to use the mock-up and provide one if requested.  It will be part of the RFP.