# LAT CDR RFA #30 Response

Action Requested:

The test plan shows no tagged photons between 17.6 MeV and 100 MeV.  The gap between these two energies represents an energy range where the instrument sensitivity varies most rapidly with energy.  In principle, bremsstrahlung photons can be produced in this gap.  A couple of energy points should be inserted in the beam test plan.

# Supporting Rationale:

The energy range below 100 MeV is very important astrophysically.  The instrument response in this region needs to be confirmed.

# Response:

In all past LAT hardware test beams at SLAC satisfactory calibration results below 100 MeV have not been obtained with the tagged photon beam or the bremsstrahlung beam. We expect to improve the tagged photon beam by using a double arm silicon telescope instead of a scintillation hodoscope to tag the positrons. We have changed the beam test plan to include a 50 MeV point as a goal. If we manage to upgrade the tagger to a double arm silicon telescope, we are likely to achieve this goal. As the Van de Graff gives a sharp line at 17.6 MeV that is very clean, the I&T team is confident that we will be able to establish our 20 - 99.9 MeV science requirements (via Monte Carlo verification) using this photon source.  The beam test plan (LAT-TD-00440) describes the planned tests of hardware units with cosmic rays and/or particle beams.