# LAT CDR RFA #34 Response

Action Requested:

Equip Calorimeter Test Module with flight ICs before passing it on to I&T.

# Supporting Rationale:

System test with flight ICs should commence as soon as practical

# Response:

Prior to delivery of the EM CAL, the 16 GCRC ASICs were replaced with the flight version - GCRC5.  However, due to problems discovered in the GCFE9 parts, they were not placed on the EM CAL.  EM CAL was delivered with GCRC5s and GCFE7s.  This configuration operated at spec'ed communication speeds.  On return from I&T, GCFE7s will be replaced with GCFE9As at the earliest possible time that is consistent with scheduled beam test at GSI.