Meeting:	GLAST Preliminary Design Review, January 8-11, 2002

Subsystem:	Systems Engineering 	Response Accepted/

RFA Closed:

RFA Number:	25	_________________

(Originator’s initials)

Originator:	Cliff Jackson, Code 556, 301-286-6862

Specific Request:

Re-examine the operational and survival temperature limits prior to the start of component qual testing. Consider whether it is feasible to establish survival limits that are 15 degrees beyond normal operational ranges.  This will assure that operational performance 10 C beyond the normal operational range can be verified without significant risk of exceeding survival limits.

Supporting Rational:

Current temperature limits would require testing at or beyond survival limits if a 10 degree margin is applied to the operational limits.

Response: