Meeting:	GLAST Preliminary Design Review, January 8-11, 2002

Subsystem:	Thermal 	Response Accepted/

RFA Closed:

RFA Number:	32	_________________

(Originator’s initials)

Originator:	D. Hewitt/T. McCarthy, Code 545, 301-286-5115

Specific Request:

Review individual box temperature requirements to ensure these limits are based on box capability not on the TCS capability.

Supporting Rational:

The results of the review demonstrated that box temperature limits were being set by the capability of the TCS versus designing a TCS to use the allowable limits of the boxes; i.e., electronics boxes limits at 15 degrees C versus its capability of 40 degrees C.

Response:

Box operating and test temperatures (acceptance and qualification) have been established, and are detailed in the LAT environmental specification (LAT-SS-00788).  This document is being reviewed by the Project.