Meeting:	GLAST Preliminary Design Review, January 8-11, 2002

Subsystem:	Thermal 	Response Accepted/

RFA Closed:

RFA Number:	35	_________________

(Originator’s initials)

Originator:	D. Hewitt/T. McCarthy, Code 545, 301-286-5115

Specific Request:

Perform a thermal vacuum cycle test on the flight grid assembly with heat pipes installed to verify workmanship.

Supporting Rational:

Test flow shows a T/V test on Flight Grid only.  Cycling the grid with the bonded heat pipes assembled to it is critical to verify the integrity of the thermal joints.

Response:

This has been added to the Mechanical Systems Test Plan.