Meeting:	GLAST Preliminary Design Review, January 8-11, 2002

Subsystem:	Mechanical 	Response Accepted/

RFA Closed:

RFA Number:  48	_________________

(Originator’s initials)

Originator:	Jim Ryan, Code 543, 301-286-4975

Specific Request:

Generate a comprehensive strength qualification plan for the LAT instrument.

Supporting Rational:

There is no instrument level strength test planned.  A comprehensive document defining the strength qualification plans will ensure that all interfaces and subsystems will be adequately strength qualified.

Response:

An updated strength qualification plan has been developed, that removes the need for a LAT sine burst test.  Strength qualification of the Grid and key interfaces is performed at the Grid Box subsystem level, only, through static load testing.