Request For Action Number: 14 Project GLAST - GAMMA-RAY LARGE AREA SPACE TELESCOPE Spacecraft (SC/GS/LV): System/Instrument: LAT - LARGE AREA TELESCOPE Review: PDR2 - PRELIMINARY DESIGN REVIEW Date: Originator: D. Hewitt Phone: 301-286-5115 Organization: CODE 545 Category: THERMAL Title: Date Closed: Residual Risk: Action Requested: Include an i.r. scan of the front side of the radiators with a heat load on each evaporator prior to and after mechanical and thermal cycling tests at Lockheed/Martin. Supporting Rationale: This will show the bond integrity of the heat pipes to the panel. Project Response: