Request For Action Number: 14 Project GLAST - GAMMA-RAY LARGE AREA SPACE TELESCOPE Spacecraft (SC/GS/LV): System/Instrument: LAT - LARGE AREA TELESCOPE Review: PDR2 - PRELIMINARY DESIGN REVIEW Date: Originator: D. Hewitt Phone: 301-286-5115 Organization: CODE 545 Category: THERMAL Title: Date Closed: Residual Risk: Action Requested: Include an i.r. scan of the front side of the radiators with a heat load on each evaporator prior to and after mechanical and thermal cycling tests at Lockheed/Martin. Supporting Rationale: This will show the bond integrity of the heat pipes to the panel. Project Response: This RFA is redundant to RFA #6: The LAT will develop an IR test plan and cost estimate to complete IR testing on each radiator panel. IR testing is not currently part of the Radiator testing program, so the costs and benefits will be evaluated by a CCB at the time of review.