Request For Action Number: 16 Project GLAST - GAMMA-RAY LARGE AREA SPACE TELESCOPE Spacecraft (SC/GS/LV): System/Instrument: LAT - LARGE AREA TELESCOPE Review: PDR2 - PRELIMINARY DESIGN REVIEW Date: Originator: D. Hewitt Phone: 301-286-5115 Organization: CODE 545 Category: THERMAL Title: Date Closed: Residual Risk: Action Requested: Be certain that a shimming at interfaces is included in thermal model. It does not appear that the X-LAT heat pipes shims have been included. Supporting Rationale: Need to consider shimming for accurate of prediction of gradients across these interface. Project Response: This RFA is redundant to RFA #10: Agreed. The LAT design engineering team accepts this required activity and plans to present the results of a thermal analysis that accounts for temperature changes across the X-LAT Heat Pipe shimmed interface at the LAT instrument CDR.