Request For Action Number: 17 Project GLAST - GAMMA-RAY LARGE AREA SPACE TELESCOPE Spacecraft (SC/GS/LV): System/Instrument: LAT - LARGE AREA TELESCOPE Review: PDR2 - PRELIMINARY DESIGN REVIEW Date: Originator: D. Hewitt Phone: 301-286-5115 Organization: CODE 545 Category: CONTAMINATION Title: Date Closed: Residual Risk: Action Requested: Work contamination issues with the LAT project. Many cleaning steps were identified in the mechanical flow. How 'clean' must the structure and subsystems be? Define level of clearing required and if any bake outs are required. Supporting Rationale: Contamination control plan must be flowed down to hardware. Project Response: The GLAST LAT Contamination Control Plan, LAT-MD-00404, has been established to define the overall contamination control requirements necessary to establish hardware cleanliness for the GLAST LAT Project. The contamination critical hardware of the LAT shall meet the surface particulate and molecular cleanliness requirements of Level 750B per MIL-STD-1246. The LAT will perform thermal vacuum bakeouts of all hardware as necessary to ensure outgassing requirements are met.