Request For Action Number: 2 Project GLAST - GAMMA-RAY LARGE AREA SPACE TELESCOPE Spacecraft (SC/GS/LV): System/Instrument: LAT - LARGE AREA TELESCOPE Review: PDR2 - PRELIMINARY DESIGN REVIEW Date: Originator: Tom McCarthy Phone: 301-286-4710 Organization: 545 Category: THERMAL Title: Date Closed: Residual Risk: Action Requested: Verification chart reporting Qual levels (required) should be based on Acceptance levels (planned) plus or minus 5 degrees C. (See chart 3.1-33) Supporting Rationale: Plus or minus 5 margin is required between acceptance and qual level. Project Response: Agreed where possible based upon the concept that at Qualification temperatures the unit can meet performance requirements at End of Life. Since this will not be the case for several units, exceptions will be made and noted in the LAT Environmental Specification. To demonstrate robustness, these units will have a qualification limit greater than 5 degrees C above Acceptance levels. A draft of LAT-SS-01190-01, “LAT Environmental Specification” is currently out for review. This details all thermal test levels for all subsystems and the LAT, including the minimum 5 deg C margin between acceptance and qual. test levels. See Section 11.3 of the document for a table of test temperatures for all subsystems