Request For Action Number: 6 Project GLAST - GAMMA-RAY LARGE AREA SPACE TELESCOPE Spacecraft (SC/GS/LV): System/Instrument: LAT - LARGE AREA TELESCOPE Review: PDR2 - PRELIMINARY DESIGN REVIEW Date: Originator: Tom McCarthy Phone: 301-286-4710 Organization: CODE 545 Category: TESTING Title: Date Closed: Residual Risk: Action Requested: Include an IR camera test as part of the NDT methods used on radiator panel to assess panel workmanship. Supporting Rationale: IR camera testing at panel level to assess heat pipe/panel face sheet bonding as well as heat pipe operation has proven to be a good check on this system. Project Response: The LAT will develop an IR test plan and cost estimate to complete IR testing on each radiator panel. IR testing is not currently part of the Radiator testing program, so the costs and benefits will be evaluated by a CCB at the time of review.