Request For Action Number: 8 Project GLAST - GAMMA-RAY LARGE AREA SPACE TELESCOPE Spacecraft (SC/GS/LV): System/Instrument: LAT - LARGE AREA TELESCOPE Review: PDR2 - PRELIMINARY DESIGN REVIEW Date: Originator: Tom McCarthy Phone: 301-286-4710 Organization: CODE 545 Category: THERMAL Title: Date Closed: Residual Risk: Action Requested: 1. Ensure that HP stress analysis accounts for mechanical loading due to both external as well as internal forces. 2. Ensure that HP stress concentrations due to extrusion machining @ transition areas is addressed in stress analysis. Watch for wall thinning in bend areas due to tolerances of extrusion ID/OD. Supporting Rationale: HP stress analysis shown at panel level w/o consideration of internal pressures. Project Response: Accepted. The LAT Radiator design team accepts this required activity and plans to present the results of a heat pipe stress analysis at the LAT instrument CDR.