Proposed test sequence starting Oct 1 (Very rough draft)

| Operation/Test | Functions verified | H/W selection | LATC | LCI | HKPG schedule | LRS | FSW others??? |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Power up test | Commands paths, telemetry paths, telemetry, basic LAT health (power consumption, …) | X | Needed? | N/A | Baseline1 | Baseline2 | ??? |
| Load baseline configuration and verify | Ability to load configuration files, ability to apply configuration files. Includes LATC files and other TBD uploads | From power up test4 | Baseline3 |  | Baseline | Baseline2 | ??? |
| Calorimeter CI tests | See table 1 | From power up test4 |  |  | Baseline | Baseline2 | ??? |
| Calorimeter muon tests | See table 2 | From power up test4 |  | N/A | Baseline | Baseline2 | ??? |
| Tracker CI tests | See table 3 | From power up test4 |  |  | Baseline | Baseline2 | ??? |
| Tracker muon tests | See table 4 | From power up test4 |  | N/A | Baseline | Baseline2 | ??? |
| ACD CI tests | See table TBD | From power up test4 |  |  | Baseline | Baseline2 | ??? |
| ACD muon tests | See table TBD | From power up test4 |  | N/A | Baseline | Baseline2 | ??? |
| System muon tests | Gather ETE muon data with ACD installed | From power up test4 |  | N/A | Baseline | Baseline2 | ??? |
| Crosstalk test | Engineering test to see if subsystems crosstalk. Based on recommendation from Mike. May be performed during testing with ACD and 8 towers before FSW. | From power up test4 |  |  | Baseline | Baseline2 | ??? |
| LRS | Demonstrate LRS capability | From power up test4 |  | N/A | TBD combinations | TBD command scripts | ??? |

1-Baseline housekeeping schedule TBD, but default is likely acceptable

2-Baseline LRS register settings TBD

3-Baseline LATC will be an extension of one of the existing ETE run configurations. Still need to determine how to factor in presence of the ACD. This baseline will not be the in-orbit baseline, since the in-orbit baseline will be designed to ignore muons.

4-Assumes that the suite of files needed to set up the rest of the LAT configuration do not depend on the physical hardware powered (e.g. which side of the GASU is in use). Whether the suite of files depends on which towers are powered is TBD.

Calorimeter charge injection tests

| Script | Purpose | Required configuration files (LCI and LATC) |
| --- | --- | --- |
| CALF_PEDESTALS_CI: | Compute pedestals. | X LATC files, y LCI files |
| CALF_SHP_P01: | Calibrate slow shaper and determine optimal charge-injection Tack time delay under Timed Readout. | X LATC files, y LCI files |
| CALF_GAIN_P01: | Calibrate relative electronic gains with charge injection. | X LATC files, y LCI files |
| CALU_COLLECT_CI_SINGLEX16 | determine front-end integral non-linearity and noise | X LATC files, y LCI files |
| CALU_COLLECT_CI_SINGLEX16 | Test CAL-LO and CAL-HI trigger enable/disable with charge injection | X LATC files, y LCI files |
| CALF_TRG_P03 | Characterize FLE and FHE DAC settings with charge injection. | 24 LATC files (12 columns by FHE/FLE) 24 LCI files, (possibly thousands) |
| CALF_SUPP_P01 | Characterize LAC DAC settings with charge injection. | X LATC files, y LCI files |
| CALF_RNG_P01 | Characterize ULD DAC settings with charge injection. | X LATC files, y LCI files |

Calorimeter muon tests

| Script | Purpose | Required configuration files (LATC) |
| --- | --- | --- |
| CALF_MU_OPTICAL: | Analyze muon data for changes in relative optical performance. | 1 file, differs from nominal by TBD |

Tracker charge injection tests

| Script | Purpose | Required configuration files (LCI and LATC) |
| --- | --- | --- |
| TE301 – Gain and Noise Measurement | Measure gain and noise for each channel, detect dead or disconnected channels |  |
| TE302 – Single Strip Noise Occupancy | Detects noisy channels |  |
| TE303 – GTFE Noise Occupancy Scan | Health check |  |
| TE305 – Layer Trigger Threshold Scan | Health check |  |
| TE306 – TOT Test | Demonstrates functionality of TOT circuit |  |
| TE307 – TREQ Check | Demonstrates functionality of TREQ circuits |  |
| TE601 – Threshold Calibration 2 | Determines optimum threshold |  |
| TE602 – TOT Conversion Parameter Calibration 2 | Provides calibration data for TOT conversion |  |
| TE603 – MIP Calibration 2 | Calibrates charge injection scale VS TOT for each GTFE |  |
| TE604 – Threshold Dispersion 2 | Verifies threshold dispersion specification |  |
| TE702 – Trigger Jitter Measurement | Verifies trigger jitter specification |  |
| TE703 – Dead Time Measurement | Measures dead time |  |
| TE704 - Noise Occupancy with Readout in Progress | Verifies noise occupancy specification |  |

Tracker muon tests

| Script | Purpose | Required configuration files (LATC) |
| --- | --- | --- |
| TE401 – Self-Triggering Test | Demonstrates functionality of the trigger system |  |
| TE403 - Efficiency, Resolution, and Alignment 2 |  |  |

Notes/issues

How is diagnostic tlm set up and what test do we want/need.

32 fsw config file slots – need column added for them