Test Case Summary

| Test No | Test Title | Description |
| --- | --- | --- |
| LAT00x | Power On | Turn the LAT on. In the process, verify the health of the LAT by checking housekeeping telemetry as each box in the LAT is turned on. |
| LAT01x | Power Off | Safe and orderly shutdown of the LAT, again verifying each step with housekeeping telemetry |
| LAT02x | Reinitialization | Demonstrate the following low level functionality: 1) LAT Reinitialization when SC communications is lost 2) Reboot of the SIU and EPU on receipt of the SIU_RESET from the SC 3) Watchdog reinitialization of the SIU 4) SIU Watchdog reinitialization of the EPUs 5) SIU configuration of EPUs 6) SIU Primary Boot 7) SIU Secondary Boot In addition, verification of the Boot Housekeeping and Boot Diagnostic telemetry functions will be performed. |
| LAT03x | EPS performance | Power consumption, turn-on/ turn-off transients Muon run at max/min bus voltages LAT input impedance (one time), |
| LAT04x | Baseline Science Ops Config | Load the “complete” LAT configuration. This includes ensuring that all the flavors of configuration files are loaded and available. |
| LAT05x | Register test | FSW LATC capability to set and read registers |
| LAT06x | SIU/EPU hardware functional | Proves memory is healthy through environments. Read and write to every area in hardware memory. Verify hardware memory scrub function is working on every processor. |
| LAT08x | Safe Modes | Send the Load Shed/Safe Mode command to the LAT and verify that it responds properly. SIU should turn off the LAT. SIU should issue an Alert Telemetry message and reboot. Change the limits on the ACD Current Alert function such that those limits will fail and verify the appropriate Alert is issued. |
| LAT12x | Science Modes | Command the LAT through a series of mode transitions focused on the Science modes. Verify the proper response to each of the transitions. This includes transition from quiescent to Science mode and various combinations of Target of Opportunity, ARR, and SAA. |
| LAT13x | LAT/SC I/F Functional | Verify the functionality of the LAT/SC Interfaces not tested during the power on tests. The functionality tested may include (TBR) the GPS Message, the GPS Time Hack (1 PPS signal), the Observatory attitude data all provided by the SC, the LAT Time Consistency Check, Clock Correlation, Event Time Stamp, and Event Ancilliary Data functions that operate on the SC supplied data. In addition, verify the successful collection, sample rate, format, and transmission to the SC-LAT wideband interface of LAT event and associated data. |
| LAT15x | Thermal Control | For first time tests, for the TCS devices present, perform the following: 1) Verify the FSW TCS algorithm can be enabled and disabled; 2) Verify the FSW has control over all of the VCHP heaters by commanding it turn each heater on and off individually; 3) Verify that the FSW collects and accurately interprets the temperature sensors identified for LAT Thermal Control; and 4) Manipulate heater set points and verify with flight thermistors, IR guns, test thermocouples, etc. that the correct heaters turn on and off when commanded automatically by the FSW. Following Radiator Integration, repeat steps 1 thru 4 above for the entire TCS. In LAT Thermal Vacuum testing, with the LAT On and operating, verify by telemetry and additional temperature sensors that the FSW maintains the LAT within operational temperatures at all phases of the TV test. |
| LAT16x | Survival Heater Test | Once at Cold Survival in LAT Thermal Vacuum testing, with the LAT Off, insure that the primary thermostatically controlled heaters maintain the RIT at or above survival temp (currently -6 C). Remove power from the primary heaters and insure that the redundant thermostatically controlled heaters and also verify the RIT is kept at or above survival temperature. |
| LAT17x | Conducted & Radiated Emissions | Set the LAT up in a configuration expected to maximize emissions. This will likely be a charge injection test case, but the details are yet to be defined. |
| LAT18x | Conducted & Radiated Susceptibility | Set the LAT up in a configuration that will measure susceptibility to noise. The exact cases have not yet been determined, but will likely be measuring noise levels (pedestals or noise occupancy) in all 3 detectors. The light tight test case will be similar. |
| LAT20x TBR | Science Perf Diagnostics | Verify the LAT, upon receipt of the appropriate command, performs the following Science Performance monitoring Diagnostic functions during normal operations: 1) ACD Cosmic Ray (CR) Sample Events; 2) CAL CR Calibration; 3) CAL CR Calibration Prescale; 4) CAL Calibration Enable/Disable; 5) CAL CR Calibration Trigger; 6) TKR CR Calibration; 7) TKR CR Calibration Excluding Showering Events; and 8) TKR CR Calibration Excluding Low Energy Tracks. Note that the FSW requirements/implementation has changed here, and this test may collapse to a SVAC run. |
| LAT21x | Timing Measure & Adjust | Following the successful completion of the ACD, CAL, and TKR CPTs measure and adjust LAT level timing as necessary for the following parameters: 1) ACD Hold Delays; 2) ACD Hit Map Timing; 3) ACD TACK Delays; 4) CAL-Lo TREQ Delay; 5) CAL-Hi TACK Delay; 6) TKR TREQ Delays; 7) TKR TACQ Delays; 8) Trigger Window; and 9) Deadtime. Note that Eric Grove documented a set of tests that were signed off in a CR to go into the P&OTP. He is making a list to delineate which of those tests are LATTE 4x only, which are priority for LYCOS and which to put on the back burner for LYCOS. |
| LAT22x | Event Handling | Collect muons. SASS reading and processing this data demonstrates LAT end-to-end handling of event data monitoring, readout, filtering, formatting, building, time stamping, Observatory position and attitude data correlation (TBR), energy measurement, angular resolution, position resolution, data contents, and data delivery to the Science Data Port. |
| LAT23x | GRB Handling | Verify the LAT properly handles and responds to GRB alerts and repointing requests both from the ground and the GBM. This test picks up the test of the copper paths and relies on the FQT to verify all functionality. |
| LAT30x | ACD CPT | ACD CPT |
| LAT31x | ACD LPT | ACD LPT |
| LAT40x | CAL CPT | CAL CPT |
| LAT41x | CAL LPT | CAL LPT |
| LAT50x | TKR CPT | TKR CPT |
| LAT51x | TKR LPT | TKR LPT |
| LAT52x | LAT Config 1 Light Tight Test | Put the LAT in a susceptible mode and measure Cal, Tracker and ACD noise while a bright light is moved around the LAT. |
| LAT65x TBD | T&DF False Triggers | Data collection that searches for evidence of false triggering suchs as: 1) Galloping trigger rate; 2) Adjacent event similarity; 3) Adjacent event trigger pattern similarity; 4) Non-Poisson's distribution for Cosmic Rays. Note, may be analysis of existing runs… |
| LAT66x | T&DF Data Transport Errors | Data transport errors are deliberately induced by setting configuration registers to reverse the expected parity. The behavior of the LAT is observed with data transport errors present. |
| LAT67x |  | Measure temperature dependent instrument parameters to be used to update the LAT configuration (e.g. Cal pedestals) |
|  | SVAC-ETE Tests | Perform SVAC and ETE tests described in a version updated for LAT level test of the matrix Van de Graaf and Cosmic Ray Data Runs for LAT Integration (LAT-TD-04136). |