March 29, 2004

Pat Hascall

Agenda for meeting on 29 March:

Review action items

Define sub teams to address tracker and cal details

Tracker rep is Hiro

Cal rep is Eric Grove

| No. | Action | Actionee | Due date/Status | Results |
| --- | --- | --- | --- | --- |
| 1 | Define functionality of external test crate | Hascall/Wai/Claus/Waite | 8 March 04 Closed | Viewgraphs generated for March 7 meeting that defines possibilities, but firm requirements need to be generated as part of ongoing planning |
| 2 | Complete subsystem test list, coordinate with Subsystems managers and get agreement on when the scripts will be delivered to I&T | Hascall/Claus | 15 March 04 for Cal and Tracker | Still in work, focus has been on TEM and TEM/PS |
| 3 | Examine single tower tests to see which of them could (or should) use combined scripts. Discussion topic at next meeting | Hascall | TBD | Viewgraphs generated, more work needed, defer until first level of tests are defined |
| 4 | Define "in-orbit calibration" and document resulting software requirements. | Schalk, DeKlotz and Eduardo. Schedule - First cut at meeting in 2 weeks. | First cut at meeting on 22 March 04 | Viewgraphs reviewed on 22 March. |
| 5 | Define 2 tower test suite | Ritz | Draft by 15 March 04 | First cut presented at next meeting on 29 March CANCELLED |
| 6 | Provide test procedure for TEM/TEMPS EGSE | Haller | 31 March |  |
| 7 | Provide test procedure for the GASU EGSE | Haller | 31 March |  |
| 8 | Provide test procedure for the PDU EGSE | Haller | 31 March |  |
| 9 | Provide test procedure for the SIU EGSE | Haller | 31 March |  |
| 10 | Provide test procedure for the EPU EGSE | Haller | 31 March |  |
| 11 | Provide dates for delivery of updated Tracker test plan and for test scripts | Robert Johnson |  | New rev of test procedure by 2 April |
| 12 | Provide delivery plan for scripts. Is the plan to deliver one CPT test script or a set of scripts that make up the CPT? | Neil Johnson |  |  |
| 13 | Define the Safe to Mate requirements |  |  |  |
| 14 | For the calorimeter to TEM/TEMPS integration, are there any other tests (e.g. more noise characterization) that is necessary? Set up meeting with calorimeter, electronics and I&T to discuss | Hascall | 15 April | Need to get Cal rep, DAQ rep and copy of the ICD. Any requirements not verified at the lower level need to be verified here. |
| 15 | What is the turn on sequence for cal and tracker? Do the individual voltages need to be sequenced or is it a single command for cal and a single command for tracker | Hascall | 29 March | Per section 2.3.1 of the TEM Programming ICD (LAT-TD-00605), there is a single register in the TEM that has a single bit for the tracker and a single bit for the calorimeter. This register defaults to zero (off) at power on. Note that putting both values in one register means that in order to turn on the cal without affecting the state of the tracker, the state of the tracker must be known by the command generation process. Interleaving scripts will be more difficult. The TEM Power Supply Specification and ICD (LAT-SS-01281) block diagram in Figure 1 shows a single signal for the tracker that applies 28V to the tracker low voltage converter and to the high voltage converter in parallel. The calorimeter configuration is the same. The spec states that “all voltages of a given sub-system are turned on and off together.” |
| 16 | Define mechanism for capturing parameters to be trended from SVAC plan, I&T, subsystems, operations, … | Hascall | 29 March | Plan is poll subsystem managers, Eduardo, and IOC to get lists of parameters to be trended. That effort will start when the first round of test definitions is completed. In the mean time, I&T should be prepared to have the capability to trend telemetry data and specified test results (including calibration data) |
| 17 | Power on sequencing from flight software – is it a single command or a series of commands under ground control | Tony Waite | 29 March |  |
| 18 | Is SLAC responsible for capturing capture run times at the observatory level? | Hascall | July |  |
| 19 | Poll the subsystem managers to see if there are any commands that would at any time damage the LAT. For example, are there any outgassing requirements before the high voltages are applied. | Hascall | 29 March | Email sent on 3/22. ACD stated that the high voltage should not be turned on when the pressure is 0.5 atmospheres to 10e-3 torr due to risk of corona. DAQ/ELX said no susceptibility Tracker said that there may be danger of corona discharge at intermediate pressures. Cal said NO |

| Test Name | Status | Open issues |
| --- | --- | --- |
| TEM/TEM PS receiving test | Gunther to provide test procedure for the equivalent EGSE as soon as it is ready so that I&T can get familiar with contents | AI 6 |
| Tracker receiving test | Suite of tests worked out in concept. Actual test scripts being defined/refined. Schedule TBD | AI 11 |
| Calorimeter receiving test | Suite of tests worked out in concept. Will be provided as a single script for comprehensive test and single script for functional test. Additional data was provided by the Cal team, that data is under review. | Script design may make it difficult to combine with other scripts to minimize test time. See AI 12 |
| GASU receiving test | Gunther to provide test procedure for the equivalent EGSE as soon as it is ready so that I&T can get familiar with contents | AI 7 |
| EPU receiving test | Gunther to provide test procedure for the equivalent EGSE as soon as it is ready so that I&T can get familiar with contents | AI 10 |
| SIU receiving test | Gunther to provide test procedure for the equivalent EGSE as soon as it is ready so that I&T can get familiar with contents | AI 9 |
| PDU receiving test | Gunther to provide test procedure for the equivalent EGSE as soon as it is ready so that I&T can get familiar with contents | AI 8 |
| Empty crate receiving test | No electrical test |  |
| TEM/TEM PS to Calorimeter integration tests | Strategy is to perform the cal receiving test to generate a new baseline for calorimeter performance |  |
| Single tower (outside of grid) tests |  |  |
| Single tower (in grid) tests |  |  |
| Two tower test |  |  |
| GASU integration test |  |  |
| PDU integration test |  |  |
| SIU integration test |  |  |
| EPU integration test |  |  |
| Heater control box receiving test |  |  |
| Heater control box integration test |  |  |
| Integrated system test |  |  |