| Step No. | Description of Step | Step Verification | Requirement Sold/ Function Validated | Step Verification in the Report | Step Outcome |
| --- | --- | --- | --- | --- | --- |
| 1 | LAT is powered on . | LatPowerOn or LatPowerOnTurbo has been successfully completed. LAT is in Quiescent Mode. | N/A | N/A | Complete/ Not Complete |
| 2 | From the primary spacecraft (SC-P) command an SIU Reset using the Spacecraft Discrete Control lines. | Discrete Monitor lines indicate SIU in Primary Boot SIU Boot HSK telemetry received. Verify Boot Mode (LPCBOOTTYPE=5) SIU-A Watchdog function Disabled | LVP222 – Discrete Control Signals LVP223 – Discrete Monitor Signals LVP532 – Discrete Control Signals – LVDS Std LVP533 – Discrete Control Signals Types LVP536 – Discrete Control Signal Pulse Logic LVP539 – Discrete Monitor Signal Characteristics LVP540 – Discrete Monitor Redundancy IN24 – SIU Reset/Reboot | Reset SIU (Spacecraft) | Pass/Fail |
| 3 | Command Memory Dump (LMEMDUMPMEM) of contents of fixed areas of SIU SUROM, EEPROM, and RAM | Dump address/contents = expected address/ contents | LVP94 – SIU Boot Memory Dump | Moved to LAT06x | Pass/Fail |
| 4 | Command EPU-A Reset (LPBCRESET) | EPU-A Boot HSK telemetry received. Verify Boot Mode (LPCBOOTTYPE=5) EPU-A Watchdog function Disabled | IN24 – EPU-A Reset/Reboot | Not currently in report, see message log for verification (JIRA LS76) | Complete/ Not Complete |
| 5 | Command EPU-B Reset (LPBCRESET) | EPU-B Boot HSK telemetry received. Verify Boot Mode (LPCBOOTTYPE=5) EPU-B Watchdog function Disabled | IN24 – EPU-B Reset/Reboot | Not currently in report, see message log for verification (JIRA LS76) | Complete/ Not Complete |
| 6 | Command Memory Dump (LMEMDUMPMEM) of contents of fixed areas of EPU-A SUROM, EEPROM, and RAM | Dump address/contents = expected address/ contents | LVP94 – EPU-A Boot Memory Dump | Moved to LAT06x | Pass/Fail |
| 7 | Command Memory Dump (LMEMDUMPMEM) of contents of fixed areas of EPU-B SUROM, EEPROM, and RAM. | Dump address/contents = expected address/ contents | LVP94 – EPU-B Boot Memory Dump | Moved to LAT06x | Pass/Fail |
| 8 | Dump SIU-A RAM Scrub and CPU Self Test Log file. | Offline, review contents of Log File for errors | N/A | Moved to LAT06x | Pass/Fail |
| 9 | Dump EPU-0 RAM Scrub and CPU Self Test Log file. | Offline, review contents of Log File for errors | N/A | Moved to LAT06x | Pass/Fail |
| 10 | Dump EPU-1 RAM Scrub and CPU Self Test Log file. | Offline, review contents of Log File for errors | N/A | Moved to LAT06x | Pass/Fail |
| 11 | Command SIU-A Secondary Boot (LBTRTOSEXEC) | SIU-A Housekeeping telemetry received. SIU-A Watchdog function Enabled | N/A | Secondary SIU Boot | Complete/ Not Complete |
| 12 | Command EPU-A Secondary Boot (LBTRTOSEXEC) | EPU-A Housekeeping telemetry received. EPU-A Watchdog function Enabled | N/A | Not currently in report, see message log for verification (JIRA LS76) | Complete/ Not Complete |
| 13 | Command EPU-B Secondary Boot (LBTRTOSEXEC) | EPU-B Housekeeping telemetry received. EPU-B Watchdog function Enabled | N/A | Not currently in report, see message log for verification (JIRA LS76) | Complete/ Not Complete |
| 14 | Induce SIU Watchdog Timeout (MEMLOADREG; Register = 0xBF880058; Value = 0) | Verify Boot Type (LPCBOOTTYPE=2) | IN24 – SIU Reset/Reboot | Not currently in report, see message log for verification (JIRA LS76) | Pass/Fail |
| 15 | Command SIU Secondary Boot (LBTRTOSEXEC) | SIU-A Housekeeping telemetry received. SIU-A Watchdog function Enabled | N/A | N/A | Complete/ Not Complete |
| 16 | Induce EPU-A Watchdog Timeout (MEMLOADREG; Register = 0xBF880058; Value = 0) | Verify Boot Type (LPCBOOTTYPE=2) | IN24 – EPU-A Reset/Reboot | Not currently in report, see message log for verification (JIRA LS76) | Pass/Fail |
| 17 | Command EPU-A Secondary Boot (LBTRTOSEXEC) | EPU-A Housekeeping telemetry received. EPU-0 Watchdog function Enabled | N/A | N/A | Complete/ Not Complete |
| 18 | Induce EPU-B Watchdog Timeout (MEMLOADREG; Register = 0xBF880058; Value = 0) | Verify Boot Type (LPCBOOTTYPE=2) | IN24 – EPU-B Reset/Reboot | Not currently in report, see message log for verification (JIRA LS76) | Pass/Fail |
| 19 | Command EPU-B Secondary Boot (LBTRTOSEXEC) | EPU-B Housekeeping telemetry received. EPU-B Watchdog function Enabled | N/A | N/A | Complete/ Not Complete |