|  | Document # | Date |
| --- | --- | --- |
|  | LAT-TD-04136-02 | 16-Mar-2005 |
|  | Author(s) |  |
|  | Gary Godfrey |  |
| GLAST LAT System Specification |  |  |
|  | Subsystem/Office |
|  | Integration and Test |
| Document Title |
| VG and CR Data Runs for LAT Integration |

Gamma-ray Large Area Space Telescope (GLAST)

Large Area Telescope (LAT)

Integration & Test Subsystem

VG and CR Data Runs for LAT Integration

Change History Log

| Revision | Effective Date | Description of Changes |
| --- | --- | --- |
| -01 | 2/8/05 | Original |
| -02 | 3/16/05 | Updated E2E table to agree with Eduardo’s reviewed shorter set of runs |

Contents

1.	Purpose	4

2.	Scope	4

3.	Definitions	4

3.1.	Acronyms	4

3.2.	Definitions	5

4.	Applicable Documents	5

5.	Description of the Equipment	5

6.	Description of the Tests	5

7.	Settings of DACs and Delays	6

8.	Data Taking Procedure	6

Purpose

The purpose of this document is to specify the VG and CR data runs that will be taken with the LAT (or subsets of LAT towers) during LAT integration.  This document contains both the End-To-End Test committee runs and SVAC runs.  Configurations and run times are specified.

Scope

Runs are specified in Table 1 for various configuration from the EM2 up to the full LAT.

Definitions

Acronyms

ACD	Anti-Coincidence Detector

AIDS	Assembly Instruction Data Sheet

CAL	Calorimeter

CNO	Carbon Nitrogen Oxygen

CR	Cosmic Ray

CU	Calibration Unit (1 or 2 tower array for Beam Test)

CVS	Configuration controlled software repository at SLAC

DAQ	Data Acquisition system

EM	Engineering Model tower.

E2E	End-to-End Test Committee

EGSE	Electronic Ground Support Equipment

GEM	Global Trigger Electronics Module

GLAST	Gamma-ray Large Area Space Telescope

GLT	Global Lat Trigger

ID	Identification

LAT	Large Area Telescope.

ROI	Region of  Interest

SLAC	Stanford Linear Accelerator Center in Menlo Park, California

SVAC	Science Verification, Analysis, and Calibration

TKR	Tracker

TBD	To Be Determined

TBR	To Be Reviewed

TACK	Trigger Acknowledge

TREQ	Trigger Request

VG	Van de Graaff

Definitions

Tracker	Silicon strip tracker within each tower of the LAT

Applicable Documents

[1]	LAT-TD-00440		Particle Test Plan

[2]	LAT-MD-00575-01		SVAC LAT Plan for LAT Integration at SLAC

[3]	LAT-MD-02730-01-D1	LAT Performance and Operations Test Plan

[4]	LAT-MD-03489-02		Ad Hoc Committee on End-to-End Testing

Description of the Equipment

The equipment is the LAT (or subset of towers) with a GLT module and EGSE hardware and software to read out the LAT.

Description of the Tests

Testing recommendations have been provided by the End to End Testing Committee (LAT-MD-03489-02).  Specific tests have also been required by SVAC in LAT-MD-00575.

The following tests are required by the End to End Testing Committee  or SVAC.

1)  Basline CR Tests					BCR

2)  Consdition Scan CR Tests				CSCR

3)  Basline CR Trigger Subtests			BCR

4)  Nominal Rate CR Tests				NCR

5)  Nominal Rate Condition Scan Tests		NRCSCR

6)  CAL Nominal Rate CR Tests			CNRCR

7)  Baseline CR Data Volume Sub Tests		BCRDV

8)  Nominal Rate CR Data Volume Sub Tests	NRCRDV

9)  Van de Graaff Tests				VG

B)  SVAC Tests					SVAC

C)  Calorimeter Calibration				CALCALIB

Each line in Table 1 corresponds to a required test from E2E (LAT-MD-03489 Section 2.2.1) or SVAC (LAT-MD-00575).  The first column in Table 1 contains the paragraph ID (1 through 9) of LAT-MD-03489 Section 2.2.1, and SVAC tests are under the first column label B.

Settings of DACs and Delays

For most runs in Table 1, individual DACs and delays are set to their nominal values.  The nominal value of DACs are the values we intend to use in orbit as determined by the various subsystems.  The nominal delays are those determined during I+T testing.  For the condition scan tests, min/max settings of DACs and delays are chosen to be extremum values that the instrument should be able to operate successfully at when in orbit.

Data Taking Procedure

A Procedure will call for the mechanical setup up the device being tested.  It will also call for the execution of  a particular line (or lines) from Table 1.  Via a GUI the operator will select the request.  The Data Taking Script will directly read the requested line from Table 1, set up the instrument electronically, and acquire data for the time specified in the appropriate Table 1 column.  The line from Table 1 will be written out with the event data being accumulated.

Table 1 is embedded in this document in .xls format.  This .xls file is the primary document.  The Data Taking Script reads an asci .csv fill which is created by opening the .xls file in Excel and then saving it in the .csv format.

Table 1.  Configurations and run times for testing the full 16 tower LAT and its subsets.  The final columns indicate run times for various subassemblies of the full LAT.  Zoom in with Word to read the Excel spread sheet, or click on it to open it in Excel.