|  | Document # | Date |
| --- | --- | --- |
|  | LAT-TD-04980-01 | 2-Feb-2005 |
|  | Author(s) |  |
|  | Gary Godfrey |  |
| GLAST LAT System Specification |  |  |
|  | Subsystem/Office |
|  | Integration and Test |
| Document Title |
| Use of an AM241 Source for High Rate Trigger EM, Tower, and LAT Data Runs |

Gamma-ray Large Area Space Telescope (GLAST)

Large Area Telescope (LAT)

Integration & Test Subsystem

Use of an Am241 Source for High Rate Trigger EM, Tower, and LAT Data Runs

Change History Log

| Revision | Effective Date | Description of Changes |
| --- | --- | --- |
| -01 | 2/2/05 | Original |

Contents

1.	Purpose	4

2.	Scope	5

3.	Definitions	5

3.1.	Acronyms	5

3.2.	Definitions	6

4.	Applicable Documents	6

5.	Description of the Equipment	6

6.	Results of Am241 Source on EM2 Trigger Rate	6

7.	Calculation of Am241 Source on LAT Trigger Rate	7

8.	X-raying a Tower to Verify Material Thickness	10

9.	Procedure for Using the Am241 Source	11

10.	Appendix A:	11

Purpose

The Ad Hoc Committee on End-to-End Testing (LAT-MD-03489-01) has required runs at trigger rates up to 10 KHz by the use of “solicited triggers” or lowering discriminators (Tracker or Cal) to trigger on noise.  Solicited triggers are triggers initiated under program control from a buffer of  random spaced times.  Presumably,  random triggers into the external trigger input (eg. from a random pulse generator or PMT noise) might instead be used, the difference being that the same pattern is not repeatable.  With both the normal 3-in-a-row trigger and random triggers enabled, muons or Van de Graaff photons will be studied for any differences between the low and high rate data.

The purpose of this document is to describe the use of an Am241 source for making a high trigger rate in the EM, single Tower, and LAT.  Source triggers would have some advantages over noise, solicited, and random external triggers as listed in Table 1.  The data runs for which the source will be used are listed in  LAT-TD-04136  “VG and CR Data Runs for LAT Integration”.

Table 1.  Source trigger advantages compared to other methods of high rate triggering.

| High Rate Trigger | Pros and Cons |
| --- | --- |
| Noise triggers from lowered disc or turning some layers on | Triggers always come from the same set of noisy strips or xtals. Since the noise is barely exceeding the disc, the strips that trigger will not be recorded later at the Level 1 Trigger time and thus will not be in the data stream. Maybe some other noisy strips will get recorded depending on noisy strip masking. Data stream loading will be typical of empty events. |
| Solicited triggers | Data stream loading will be typical of empty events. These high rate triggers are outside the normal in-orbit data taking path. |
| External triggers (Berkeley Nucleonics Random Pulse Generator) | Data stream loading will be typical of empty events. FFT of time spectrum not Poisson at >10 sec time scales (probably unimportant) |
| External triggers (PMT noise) | Data stream loading will be typical of empty events. These high rate triggers are outside the normal in-orbit data taking path. |
| Am241source Tracker Trigger | The hits that caused the trigger are captured in the data stream (60 KeV energy deposition in Si causes the 1/3 mip disc to stay high for ~4 usec). The hits populate many different strips. The data loading (≥6 hits/event) is closer to that of real muons. Unlike muons though, the vast majority of triggers are only in the top 6 layers of silicon closest to the source. The tracker trigger rate is highly dependent on the tracker comparators’ time over threshold (a well defined time since 60 KeV is always left in the silicon) and the material thickness of the layers. The measured rate may be compared to calculation. Unfortunately, source photons are still only a poor approximation of the real high muon rate we would see in an airplane flight. |
| External triggers (Berkeley Nucleonics Random Pulse Generator), all other triggers disabled, Am241 source is present. | For random pulse generator triggers with the source present, the ratio of layer occupancies measures the transmission of 60 KeV x-rays. This provides a measure of the amount of material present in the various layers (primarily tungsten). |

Scope

The methods described in this document can be used on the full 16 tower LAT or any subset of towers.

Definitions

Acronyms

ACD	Anti-Coincidence Detector

CAL	Calorimeter

CNO	Carbon Nitrogen Oxygen

DAQ	Data Acquisition system

EM	Engineering Model tower.

EM2	Engineering Model 2 tower.

GEM	Global Trigger Electronics Module

GLAST	Gamma-ray Large Area Space Telescope

GLT	Global Lat Trigger

EGSE	Electronic Ground Support Equipment

LAT	Large Area Telescope.

ROI	Region of  Interest

SLAC	Stanford Linear Accelerator Center in Menlo Park, California

TKR	Tracker

TBD	To Be Determined

TBR	To Be Reviewed

TACK	Trigger Acknowledge

TREQ	Trigger Request

Definitions

Tracker	Silicon strip tracker within each tower of the LAT

Applicable Documents

[1]	LAT-MD-03489-01	Ad Hoc Committee on End-to-End Testing

[2]	LAT-TD-04136	VG and CR Data Runs for LAT Integration

[3]	LAT-PS-04511	Data Taking Procedure

Description of the Equipment

The equipment is the LAT (or a subset of towers) with a GLT module and EGSE hardware and software to read out the LAT.  The source is 40 mCurie of Am241 available from SLAC Radiation Protection Department.  The Tower or LAT is pointing vertically. The source ( 10 mm diam x 3 mm thick disc covered with .010 of stainless steel) is removed from its lead pig and placed in the center of the top Tower tray. For the EM2 measurements reported in this document, the EM2 was rotated horizontal and the source was placed at various distances from the tracker front face.

A single 60 Kev x-ray only makes a hit in one silicon layer.  A trigger arises when 6 different photons cause hits in 6 silicon layers sufficiently close in time.  These triggers do not show a track in the event display.  Instead, each of the six silicon layers shows one (or more) hits randomly scattered around in the layers .

Results of Am241 Source on EM2 Trigger Rate

An Am241 source was placed at several distances from the +z face of EM2.  The source was at x=y=0 and moved along the z axis to different distances from the EM2 front face.  The standard 3-xy layers-in-a-row tracker trigger was used.  Figure 1 shows the measured trigger rate as a function of distance from the top layer of silicon.  One more measurement was taken at  33 cm but the system immediately crashed due to the EGSE not being to handle the rate (~500 Hz according to the curve).  This EGSE problem has since been fixed.

Figure 1.  Calculated EM2 3-in-a-row trigger rate versus distance of the Am241 source from the top silicon layer.  The red points are measurements on EM2. Cal 4 range readout was enabled so there was 100 usec deadtime per L1T.

Measurements were also taken with a Geiger counter at the same distances from the source.  The results are shown in Figure 2.  A Geiger counter is calibrated to report Rads (1 Rad = 100 ergs/ gram of water).  Using the attenuation length of 60 Kev x-rays in water and a source strength of .040 Curies, a calculation yields the line in Figure 2.

Figure 2.  Geiger counter reading versus distance from the .040 Curie source.  The points are measurements and the line is a calculation of what a Rad means.

Calculation of Am241 Source on LAT Trigger Rate

The calculation for the trigger rate of the LAT is shown in Figure 3.  There is no ACD in the calculation.  As the source is moved in along the central axis of a tower, the adjacent towers contribute negligibly to the trigger rate.  The red curve is for the central tower alone, while the blue curve includes the trigger rate contribution of all 8 neighboring towers.

Figure 3.  LAT trigger rate versus source distance.  The source is moved along the central axis of a tower.  The red curve is for the central tower.  The blue curve includes the trigger rate including the contribution of the 8 neighboring towers.  The calculation assumes zero suppressed data and thus uses 25 usec deadtime per L1T.

For a 40 mCurie source, the trigger rate of the LAT (or a single tower) has a maximum of  4.4 kHz when the source is as close as it can get to the top silicon layer (assumed 3.9 cm).  For random triggers at this source position, the layer occupancies are shown in Figure 4.  For tracker triggers at this source position, the recorded multiplicity is slightly greater (always >1 in each layer) for the top 6 layers, since they made the trigger.  The maximum trigger rate is shown as a function of source strength in Figure 5.

Figure 4.  The layer occupancies for random triggers of a .040 Curie source placed at 3.9 cm from the top silicon layer (4.4 KHz trigger rate).  On average there are 11.4 hits per event (the sum of these multiplicities) with the triggers predominately coming from coincidences of the top 6 layers of silicon.

Figure 5.  The tower trigger rate as a function of source strength for the source at 3.9 cm distance.

The trigger rate as a function of x-ray energy for a fixed source distance of 3.9 cm is shown in Figure 6.  There is a peak in the trigger rate at 69 KeV which fortuitously is close to the x-ray energy available from an Am241 source.  The K edge in tungsten is at 69.5 Kev.  Above this energy, the x-rays are much more strongly absorbed by the tungsten.

Figure 6.  The tower trigger rate as a function of x-ray energy for a .040 Curie source at 3.9 cm distance.

For 60 KeV photons, the majority of interactions in Si are photoelectric rather than Compton.  The photoelectron has 1.8 KeV (the n=1 binding energy in Si) less energy than the photon.  The energy of the photoelectron then goes into making electron-hole pairs in the silicon just like any other charged particle. The maximum energy that a Compton scattered photon can give to the electron is 3.6 KeV (when the photon scatters backwards).  This is not enough to work the 40 KeV tracker comparator.  The occupancy and trigger rate calculations use the sum photoelectric+Compton for calculating the silicon transmissions, but only use the photoelectric cross section for the silicon occupancy.

The digitized measurement of the GTFE-G pulse shape is shown in Figure 7.  The red curve is minI and the blue curve in 60 Kev.  The black line is the comparator setting at 1/3 MinI (MinI=115 Kev).  As can be seen,  the blue signal is above the line for ~4 usec.  The layer occupancies (and the trigger rate) is a function of the product  (Source Strength x Time above Threshold).

Figure 7.  The tracker’s GTFE-G preamp pulse output.  The red curve is for MinI energy deposition (115 Kev) in the silicon, and the blue curve is for 60 Kev deposition.  The black line is the strip comparator setting of 1/3 MinI.

X-raying a Tower to Verify Material Thickness

Leaving the .040 Curie source in place but disabling all internal trigger sources, the tower may be read out at random times by using a random pulse generator to trigger the external trigger input.  The average number of hits per layer can then be measured.  The transparency of layer m is the ratio of  average hits in layer m+1 to layer m.  The error on this transparency (due to statistics on the number of events) translates into an error on the tungsten radiator thickness. Figure 8 shows the x-ray transmission and the error (not including how accurately the x-ray attenuation coefficient for Tungsten is known) on the tungsten thickness as a function of layer number for 1 hour of triggers at 1 KHz (=3.6 x 106 events).  The statistical measurement error on the average tungsten thickness is <1% down to layer 11 and <10% down to layer 22.

Figure 8. The average transmission of 60 KeV x-rays and the fractional error in Tungsten thickness for 3.6 x 106 random triggers ( .040 Curie Am241 source at the center of the top tray) is shown as a function of the layer number.

Procedure for Using the Am241 Source

- Arrange with the SLAC Radiation Protection (RP) Department to borrow the “40 mCurie  Am241  source” (Jim Allan x 4064).  An RP technician will accompany the source.  The RP technician will be the only one to handle and place it.  The RP technician will upgrade Building 33 Room 104 to a “Radiation Area” while these source measurements are being made, and only RWT trained workers with their dosimeters will be allowed to remain in the room.

- The technician will remove the source (10 mm diam disk whose mass is ~1 gram) from its lead container and place the disk in the center of the top tower tray.  The source will just sit on the horizontal top tray.  The tower should be pointing vertically.

- Follow the procedure (LAT-PS-04511) for taking whatever data is desired with the source in place.

- When data taking is finished,  ask the RP technician to remove the source from the tower and place it back in its lead shielded container.  Also ask that the “Radiation Area” signs be removed from Room 104 to return the room to its previous status.  The technician will then return the source to the RP vault.

Appendix A:

The first two icons are the MathCad programs which calculated the EM2 and LAT trigger rates due to the source.  The third icon is an asci data file of x-ray transmission coefficients.  You must have MathCad 8 or latter on your computer.  Put all 3 files in a directory.  Open each of the MathCad programs and at one place in each program (near the top) find where the x-ray coefficient file is opened and modify “C:=” in your copy of the programs to point at it.