Van de Graaff – EM Data Analysis

Progress Report

LAT-TD-5160-01

November 20,2003

I&T Meeting

Gary Godfrey

- The DAQ for the BGO is DOS writing an ASCI file.  We tried to start/stop a concurrent VG BGO run for each EM run.  The BGO files were analyzed using MathCad.

- The EM analysis is done using IDL to read ntuple files using Heather’s Root2IDL subroutine.  For requested runs,  Xin made the ntuple files:

ebf000000000000_cal.root		cal xtals for each event	Root2IDL works

ebf000000000000_merit.root		standard merit ntuple	Root2IDL works

ebf000000000000_ra.root		Eduardo’s variables		No – Root2IDL doesn’t work

- Single runs were analyzed for 6 different configurations – shown in red on the next page.

- Attempt to measure energy resolution, efficiency, and psf for the VG photons (without an EM Monte Carlo).

Van de Graff  Runs

| Date | VG data ~start time | I col [ua] | I beam [ua] | BGO Data File | BGO Run Time [sec] | Avrg [/sec] in peak | EM Run ID | EM Fits File | EM Run start | EM Time [sec] | EM # of trigs | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 9-24-03 | OFF |  |  |  |  | 0. | 101001265 | 030924144055 | 07:41 | 10435 | 106788 | VG off, EM Vertical, TkrTrig |
| 9-27-03 | OFF |  |  |  |  | 0. | 101001527 | 030928030904 | 20:09 | 7762 | 224519 | VG off, EM Vertical, CalLoTrig |
| 10-2-03 | OFF |  |  |  |  | 0. | 101001565 | 031002070924 | 00:07 | 7029 | 200759 | VG off, EM Vertical, CalLoTrig |
| 10-6-03 |  |  |  |  |  |  | 101001659 | 031006203658 | 13:37 | 2909 | 45649 | BGO(-45º,6.0”), VG into EM front face, TkrTrig |
| 10-6-03 | 15:43 | 75 | 75 | VG27.DAT | 568 | 8.23 | 101001662 | 031006223700 | 15:37 | 676 | 13939 | BGO(-45º,6.0”), VG into EM front face, TkrTrig |
| 10-6-03 | 15:50 | 75 | 75 | VG28.DAT | 3438 | 11.16 | 101001663 | 031006225113 | 15:51 | 3542 | 96331 | BGO(-45º,6.0”), VG into EM front face, TkrTrig |
| 10-6-03 | 16:51 | 75 | 75 | VG29.DAT | 2736 | 14.30 | 101001664 | 031006235353 | 16:54 | 2828 | 97705 | BGO(-45º,6.0”), VG into EM front face, TkrTrig |
| 10-6-03 | 17:45 | 75 | 75 | VG30.DAT | 1196 | 13.35 | 101001665 | 031007004501 | 17:45 | 1152 | 38411 | BGO(-45º,6.0”), VG into EM front face, TkrTrig |
| 10-7-03 | 08:50 | 75 | 75 | VG31.DAT | 3541 | 9.67 | 101001716 | 031007155141 | 08:52 | 3800 | 89112 | BGO(-45º,6.0”), VG into EM front face, TkrTrig |
| 10-7-03 | 10:56 | 75 | 75 | VG32.DAT | 4918 | 5.53 | 101001717 | 031007174453 | 10:45 | 5392 | 82419 | BGO(-45º,6.0”), VG into EM front face, TkrTrig |
| 10-7-03 | 12:31 | 75 | 75 | VG33.DAT | 4145 | 5.29 | 101001718 | 031007191651 | 12:17 | 4789 | 70305 | BGO(-45º,6.0”), VG into EM front face, TkrTrig |
| 10-7-03 | 13:49 | 75 | 75 | VG34.DAT | 3057 | 4.49 | 101001719 | 031007204622 | 13:46 | 325 | 7154 | BGO(-45º,6.0”), VG into EM front face,1/16” Pb after target, TkrTrig |
| 10-7-03 |  |  |  |  |  |  | 101001720 | 031007205902 | 13:59 | 1292 | 23039 | BGO(-45º,6.0”), VG into EM front face,1/16” Pb after target, TkrTrig |
| 10-7-03 |  |  |  |  |  |  | 101001723 | 031007213829 | 14:39 | 1499 | 6152 | BGO(-45º,6.0”), VG into EM front face,1/16” Pb after target, TkrTrig |
| 10-7-03 | 16:46 | 75 | 75 | VG35.DAT | 4986 | 5.47 | 101001726 | 031007231726 | 16:18 | 226 | 10023 | BGO(-45º,6.0”), VG into Cal side hole ¾” from Al, CalLowTrig |
| 10-7-03 |  |  |  |  |  |  | 101001727 | 031007232933 | 16:30 | 25 | 81 | BGO(-45º,6.0”), VG into Cal side hole ¾” from Al, CalLowTrig |
| 10-7-03 |  |  |  |  |  |  | 101001728 | 031007233111 | 16:32 | 1509 | 70541 | BGO(-45º,6.0”), VG into Cal side hole ¾” from Al, CalLowTrig |
| 10-7-03 |  |  |  |  |  |  | 101001729 | 031008000405 | 17:04 | 209 | 10043 | BGO(-45º,6.0”), VG into Cal side hole ¾” from Al, CalLowTrig |
| 10-7-03 |  |  |  |  |  |  | 101001730 | 031008001544 | 17:16 | 22 | 50 | BGO(-45º,6.0”), VG into Cal side hole ¾” from Al, CalLowTrig |
| 10-7-03 |  |  |  |  |  |  | 101001731 | 031008002123 | 17:22 | 854 | 10093 | BGO(-45º,6.0”), VG into Cal side hole ¾” from Al, TkrTrig |
| 10-7-03 |  |  |  |  |  |  | 101001734 | 031008005351 | 17:54 | 1065 | 54476 | BGO(-45º,6.0”), VG into Cal side hole ¾” from Al, CalLowTrig |
| 10-8-03 |  |  |  |  |  |  | 101001747 | 031008165824 | 09:59 | 117 | 5382 | BGO(-45º,6.0”), VG 45º into 1-2 xtals below EM-Cal boundary, CalLoTrig |
| 10-8-03 |  |  |  |  |  |  | 101001748 | 031008170312 | 10:04 | 65 | 3228 | BGO(-45º,6.0”), VG 45º into 1-2 xtals below EM-Cal boundary, CalLoTrig |
| 10-8-03 |  |  |  |  |  |  | 101001749 | 031008170650 | 10:07 | 107 | 5534 | BGO(-45º,6.0”), VG 45º into 1-2 xtals below EM-Cal boundary, CalLoTrig |
| 10-8-03 |  |  |  |  |  |  | 101001750 | 031008171135 | 10:12 | 197 | 5087 | BGO(-45º,6.0”), VG 45º into 1-2 xtals below EM-Cal boundary, CalLoTrig |
| 10-8-03 | 10:19 | 60-75 | 75 | VG36.DAT | 515 | 8.98 | 101001751 | 031008171719 | 10:18 | 381 | 20180 | BGO(-45º,6.0”), VG 45º into 1-2 xtals below EM-Cal boundary, CalLoTrig |
| 10-8-03 | 10:31 | 60-75 | 75 | VG37.DAT | 1231 | 7.85 | 101001752 | 031008172901 | ? | 1150 | 55560 | BGO(-45º,6.0”), VG 45º into 1-2 xtals below EM-Cal boundary, CalLoTrig |
| 10-8-03 | 10:53 | 75 | 75 | VG38.DAT | 1167 | 8.88 | 101001754 | 031008175214 | 10:53 | 958 | 50725 | BGO(-45º,6.0”), VG 45º into 1-2 xtals below EM-Cal boundary, CalLoTrig |
| 10-8-03 | 11:16 | 75 | 75 | VG39.DAT | 3812 | 9.44 | 101001755 | 031008181231 | 11:13 | 3598 | 22447 | BGO(-45º,6.0”), VG 45º into 1-2 xtals below EM-Cal boundary, TkrTrig |
| 10-8-03 | 12:20 | 75 | 75 | VG40.DAT | 7755 | 10.47 | 101001756 | 031008191523 | ? | 5669 | 36656 | BGO(-45º,6.0”), VG 45º into 1-2 xtals below EM-Cal boundary, TkrTrig |
| 10-8-03 | 14:30 | 75 | 75 | VG41.DAT | 5699 | 11.56 | 101001757 | 031008212455 | 14:25 | 6080 | 41733 | BGO(-45º,6.0”), VG 45º into 1-2 xtals below EM-Cal boundary, TkrTrig |
| 10-8-03 | 16:13 | 75 | 75 | VG42.DAT | 5926 | 12.02 | 101001758 | 031008230822 | 16:09 | 6011 | 41835 | BGO(-45º,6.0”), VG 45º into 1-2 xtals below EM-Cal boundary, TkrTrig |
| 10-9-03 | OFF |  |  |  |  | 0. | 101001759 | 031009071605 | 00:16 | 7768 | 30939 | VG off, EM Horizontal, TkrTrig |
| 10-9-03 | OFF |  |  |  |  | 0. | 101001760 | 031009092725 | 02:27 | 4942 | 19594 | VG off, EM Horizontal, TkrTrig |
| 10-9-03 | OFF |  |  |  |  | 0. | 101001761 | 031009105206 | 03:52 | 3871 | 15401 | VG off, EM Horizontal, TkrTrig |
| 10-9-03 | OFF |  |  |  |  | 0. | 101001762 | 031009115801 | 04:58 | 3966 | 99874 | VG off, EM Horizontal, CalLowTrig |
| 10-10-3 | OFF |  |  |  |  | 0. | 101001792 | 031010110401 | 06:16 | 7923 | 28260 | VG off, EM Vertical, ScintTrig |
| 10-10-3 | OFF |  |  |  |  | 0. | 101001793 | 031010131704 | 08:54 | 9404 | 33506 | VG off, EM Vertical, ScintTrig |

BGO Van de Graaff Photon Flux Monitor

The BGO Monitor is a  (7 x 7)  array of  (2 cm x 2 cm x 20 cm)  BGO xtals placed a fixed distance behind the VG target at -45°.

The gains of all xtals were adjusted to be the same (~±5%) by using a Co60 source and adjusting the individual PMT HVs.

The xtals in each of the four regions in red are analog summed, and the four analog sums are digitized by an Xtal Ball Integrate/Hold Module.

The trigger is:  Analog Sum of All  25 Xtals in red > 4 MeV

A  3 x 3 fiducial volume is defined by requiring  ( E1+E2 )  >  (E3+E4 ).

A cosmic spectra (blue) with the VG off is scaled and subtracted from the VG on spectra (red).

The histograms are in 5% energy bins.

An average BGO photon rate is measured for a BGO run corresponding to each EM run.

.1	1	10	100	1000  MeV

1	10	100  MeV

Calorimeter Plots

VG_Front_TkrTrig	VG30.dat

ebf031007004501	BGO=13.35 Hz

38,410 events / 1152 sec = 33.3 Hz

EM Energy Spectra for Various Configurations

Only LEX8 used.	Nov 19, 2003

Pedestals are the average of the lowest 90% of events for each adc.                     Gary Godfrey

Gain of .05 MeV/chan used for all adcs.

Plots are the sum of largest 18 adc energies for each event.

Require at least one adc > 2 MeV before adding the event a histogram.

Histogram bins are 10% wide in energy		Calculated

EM/BGO	EM/BGO

Cosmics – EM Horizontal – TkrTrig	0.	0.

VG–Front Center of EM–TkrTrig (trig rate slope)	2.2	2.2

VG–Front Center of EM–TkrTrig (ecal peak area)	  .61	  .57

VG–2 xtals below CalTkr interface at -45º–TkrTrig (ecal peak area)	.029

Cosmics – EM Vertical – Cal Low Trig

VG–Cal Side Hole–Cal Low Trig (trig rate slope)	3.5	20.

VG–Cal Side Hole–Cal Low Trig (ecal peak area)	2.9	20.

1	10	100	1000  MeV

EM Angular Resolution

Tkr1 position in top layer	Tkr1 extrapolated to Target Z=50. mm

Tkr1ZDir

Van de Graaff Radiation

The VG produces ~2 mR/hr of radiation downstream of the target.  The radiation is in a tightly collimated beam approximately the same diameter as the beampipe.  It is low energy photons because 1/16” of lead cuts the rate by approximately a factor of 10.

OHP provided a high purity Ge detector and we measured the following spectrum.  The detector is ~10 feet downstream of the target and the VG is set to ~70 uA column current (~700 kV).

The line at 59 keV is from an Am241 source that was briefly put in front of the detector for calibration. The Am241 also has a 26 keV line of ~1/15 the intensity which is not seen (presumably because of some source or Ge window absorber).

The present hypothesis is that the xrays are bremstrauhlung photons from electrons traveling back upstream in the VG.  The 700 keV electrons brems in a low or medium Z material such as the silver (?) accelerating electrodes (K ~22 keV).  Some of the brems photons Compton scatter backwards off electrons (calculated max energy of 174 keV).  These xrays are collimated by the steel beampipe and emerge downstream.  The K xrays are not seen because of the window or inefficiency of the Ge detector at lower energies (as indicated by the absence of the AM241 26 keV line).

Some Fixes for Next  EM Data Taking

- For the VG into the front face of the horizontal EM, take data at several distances of the Target to Tracker Face as shown in the table below.  This will allow an extrapolation of the target angular size to 0. for measuring the EM PSF.

| Target to TkrFace [inches] | Target to first converter layer [cm] | ±Angular size of target [degrees] | Relative photon flux |
| --- | --- | --- | --- |
| .75 | 5. | 21. (Oct 2003) | 1 (~32 Hz  + 2 Hz cosmic) |
| 2.75 | 10. | 11. | 1/4 |
| 4.0 | 15. | 7. | 1/9 |

- Since the VG intensity is often variable, be more careful to start/stop VG runs in unison with the EM runs.

- Take runs at various CalLow discriminator settings to know that the CalLow trigger is at max efficiency for 17.6 Mev photons.

- Lead collimate the photons (to the size of the 3” diam hole in the grid aluminum) entering the Cal from the side so a well defined solid angle of photons from the source enters the CsI.  This defined solid angle and an ~100% efficient CalLow will provide a check on the assumption of isotropic photon flux from the target.

- Be more accurate in measuring the distance from the BGO to the target and from the EM to the target (eg: 6.0” ±1/16”  instead of  ±1/4”).

- Put run comments into the end of run comment box, rather than in the daily log file.  Otherwise, it is difficult/time consuming to associate the comment with its run.

- Make the event time stamps work (now they are all zero).

- Write down the various data taking configurations beforehand and keep a running total of the number of triggers collected for each one.

# Text boxes

2

4

11

1

3

Cos95=.46      Cos68=.88

95=63.°           68=30.°

(68%)

~0° Effic  =  per steradian seen in EM

 per steradian seen in BGO

= 1200/(.02 x 2 ster)

1152 sec x 13.35 Hz /(.15 ster)

= .093 ± .01   (due to ±5% BGO dist error)

68 Measured = acos(.88) = 28°   (at 0°)

95 Measured = acos(.46) = 63°   (at 0°)

target ~ (.75”/2.0”) x (180/) = 21°

68 EM PSF ~ sqrt(68 Measured2 -target2) = 21°

95 EM PSF ~ sqrt(95 Measured2 -target2) = 59°

CalLow Xtal > 4Mev seems very inefficient for 17.6 MeV photons.