|  | Document # | Date Effective |
| --- | --- | --- |
|  | LAT-SS-05141 |  |
|  | Prepared by(s) | Supersedes |
|  | M. Arndt |  |
| GLAST LAT Project Technical Document | L. Steele |  |
|  | Subsystem/Office |
|  | Electronics and DAQ Subsystem |
| Document Title |
| GLAST FSW-ISOC Interface Control Document |

Gamma-ray Large Area Space Telescope (GLAST)

Large Area Telescope (LAT)

GLAST ISOC-FSW Interface Control Document

CHANGE HISTORY LOG

| Revision | Effective Date | Description of Changes | DCN # |
| --- | --- | --- | --- |
| 0.1 |  | Initial release for comments from ISOC and FSW |  |

TABLE OF CONTENTS

CHANGE HISTORY LOG	2

TABLE OF CONTENTS	3

TABLE OF FIGURES	3

TABLE OF TABLES	3

1	Scope	3

1.1	Purpose	3

1.2	Document Overview	3

2	Applicable Documents	3

3	Acronyms	3

4	Overview of the Subsystems Exchanging Data	3

4.1	Flight Software	3

4.2	Instrument Science Operations Center	3

4.3	Other Subsystems Associated with the Interface	3

5	Conventions	3

5.1	File Types and File Layouts	3

5.2	Representation of Time	3

5.3	Representation of Spacecraft Position and Orientation in Science Data	3

6	Summary of Data Described in this ICD	3

6.1	FSW Download Data Products Summary	3

6.2	FSW Upload Data Products Summary	3

7	Science Data	3

7.1	Science Data Delivery Mechanism	3

7.2	Event Data	3

7.3	Instrument Calibration Data	3

7.4	Instrument Diagnostic Data	3

8	Memory Writes and Reads	3

8.1	General Memory Map	3

8.2	Dumps of the Boot Diagnostics Region	3

8.3	Dumps of the Watchdog Timer Circular Buffer	3

9	Software File Uploads and Dumps	3

9.1	Software File Delivery Mechanism	3

9.2	Secondary Boot Code	3

9.3	RTOS Image Files	3

9.4	Secondary Boot Application Database Files	3

9.5	FSW Code Modules	3

9.6	Software Configuration Files	3

9.7	Application Configuration Files	3

9.8	Instrument Configuration Files	3

Appendix A: LAT Register List	3

TABLE OF FIGURES

Figure 1: Summary of the Interface Between ISOC and FSW	3

Figure 2: LAT CCSDS Telemetry Packet Layout	3

Figure 3: CCSDS Packet Header Layout with Example Timestamps	3

Figure 4: LAT Onboard File General Format	3

Figure 5: LAT Onboard File Header Format	3

Figure 6: Layout of a LAT Data Format (LDF) Record	3

Figure 7: Layout of Streaming Uncompressed Event Data	3

Figure 8: Layout of Batched Uncompressed Event Data	3

Figure 9: FSW Hardware Memory Map	3

Figure 10: cPCI Configuration Registers	3

Figure 11: Layout of EEPROM (Upper Bank Shown)	3

Figure 12: Structure of the 32bit Event Filter Configuration Mask (TBD)	3

TABLE OF TABLES

Table 1: FSW Download Data Products Summary	3

Table 2: FSW Upload Data Products Summary	3

Table 3: Contents of Individual EBFcontributions in Event Data	3

Table 4: Structure of the Timestamp Record Included in Streaming Uncompressed Event Data	3

Table 5: Structure of the Records in the Event Summary Table (Batched Compressed Event Data)	3

Table 6: Header for Timestamp Table Records (Batched Compressed Event Data)	3

Table 7: Timestamp Records (Batched Compressed Event Data)	3

Table 8: Instrument Calibration Data Summary Contents	3

Table 9: Volume and Collection Time for Calibration Data	3

Table 10: Boot Shell SDRAM Memory Map	3

Table 11: RTOS initialization and Application SDRAM Memory Map	3

Table 12: Detailed FSW Application SDRAM Memory Map	3

Table 13: RAD750 CPU Register Types and Usage	3

Table 14: CPU Register Offsets	3

Table 15: Layout of the SDRAM Boot Diagnostics Region	3

Table 16: Secondary Boot Code File Set	3

Table 17: RTOS Image File Set	3

Table 18: Secondary Boot Application Database File Set	3

Table 19: Parameters Defined in the Secondary Boot Application XML Specification	3

Table 20: FSW Code Module File Set	3

Table 21: Software Configuration File Set	3

Table 22: Housekeeping Configuration File Set	3

Table 23: Parameters Defined in the Housekeeping Configuration XML Specification	3

Table 24: Thermal Control System Configuration File Set	3

Table 25: Instrument Physics Filter Algorithm File Set	3

Table 26: Instrument Physics Filter Algorithm File Set	3

Table 27: Instrument Physics Data Compression Table File Set	3

Table 28: Instrument Physics Filter Geometry File Set	3

Table 29: Calibration Configuration File Set	3

Table 30: LAT Diagnostics Framework Configuration File Set	3

Table 31: Instrument Configuration File Set	3

Table 32: Parameters Defined in the Instrument Configuration XML Specification	3

Table 33: LAT Register List	3

# Scope

## Purpose

The Instrument Science Operations Center (ISOC) to LAT Flight Software Interface (FSW) Control Document (ICD) delineates interfaces so that subsystems can transfer, interpret, store, read and execute software instructions, files, databases and protocols between ISOC-designed software programs and FSW-designed software. This ICD will ensure compatibility between the ISOC ground systems and the FSW executing onboard the LAT instrument.

The FSW receives telecommands from the ISOC, including commands to write data to onboard memory and commands to write uploaded files to the EEPROM file system. The FSW sends housekeeping, alert, diagnostic, and science data telemetry back to the ISOC; it also sends memory data and file dumps in response to command. These exchanges are mediated by the GLAST Science Support Center and the Mission Operations Center. The interfaces are shown schematically in Figure 1 below.

Figure 1: Summary of the Interface Between ISOC and FSW

This document defines the components of the ISOC to FSW interface shown in bold in Figure 1:

Science data telemetry. This telemetry interface allows transmission of event data (both uncompressed and compressed), instrument calibration data, and instrument diagnostic data. This interface also handles data resulting from requests for memory reads and file dumps.

Writes to and reads from onboard memory. This telecommand interface allows the ISOC to perform direct writes to memory addresses and request dumps of memory at specified addresses.

Writes to and reads from the onboard EEPROM file system. This telecommand interface allows the ISOC to upload source code and software configuration files to the onboard CPUs.

The present document is not intended to serve an exhaustive reference for all telecommands and telemetry exchanged by the ISOC and onboard FSW; it focuses on the three components of the interface listed above. In addition, this document does not present the detailed layout of individual telecommand or telemetry packets. The full set of telecommands and telemetry is documented in detail in the Telecommand and Telemetry Formats handbook, [19].

## Document Overview

This document is organized as follows:

- Section ‎1, Scope, briefly describes this ICD and its objectives.

- Section ‎2, Applicable Documents, lists the documents that are referenced in this ICD or that are applicable to the interface between ISOC and the FSW.

- Section ‎3, Acronyms.

- Section ‎4, Overview of the Subsystems Exchanging Data, describes the organizational entities exchanging the data described in this ICD.

- Section ‎5, Conventions, specifies the types of files used to package the data described in this ICD and the layout of those files. The section also defines how FSW represents time and attitude in the data it generates.

- Section ‎6, Summary of Data Described in this ICD, presents an overview of the data defined in this ICD.

- Section ‎7, Science Data, defines the structure and contents of the uncompressed and compressed event data, instrument calibration data, and instrument diagnostic data written by FSW to the Solid State Recorder.

- Section ‎8, Memory Writes and Reads, defines the SDRAM regions, areas of PCI memory  space, and CPU registers which can be written and read using FSW telecommands.

- Section ‎9, Software File Uploads and Dumps, defines the format and contents of the secondary boot code files, RTOS image files, secondary boot application database files, software configuration files, application configuration files, and instrument configuration files that must be updated and uploaded by telecommand in order to configure the FSW and put the LAT in a defined state.

# Applicable Documents

| Citation Number | Document Number | Document Title |
| --- | --- | --- |
| 1 | GSFC 433-MAR-0001 | Mission Assurance Requirements (MAR) for Gamma-Ray Large Area Telescope (GLAST) Large Area Telescope (LAT) |
| 2 | LAT-MD-00033 | Gamma-ray Large Area Space Telescope (GLAST) Large Area Telescope (LAT) Work Breakdown Structure |
| 6 | LAT-MD-00068 | Gamma-ray Large Area Space Telescope (GLAST) Large Area Telescope (LAT) Configuration Management Plan |
| 7 | LAT-MD-00091 | Gamma-ray Large Area Space Telescope (GLAST) Large Area Telescope (LAT) Quality Manual |
| 8 | LAT-SS-00019 | GLAST LAT – T&DF Level III Subsystem Specification |
| 9 | LAT-SS-00284 | GLAST LAT – Trigger Level IV Subsystem Specification |
| 10 | LAT-SS-00285 | GLAST LAT – Dataflow Level IV Subsystem Specification |
| 11 | LAT-SS-00286 | GLAST LAT – Conceptual Design of the Global Trigger |
| 12 | LAT-SS-00287 | GLAST LAT – Conceptual Design of the TKR-CAL Tower Electronics Module |
| 13 | LAT-SS-00289 | GLAST LAT – Conceptual Design of the ACD Electronics Module |
| 14 | LAT-SS-00290 | GLAST LAT – Conceptual Design of the Space-Craft Interface Unit |
| 15 | LAT-SS-00399 | LAT Flight Software Specification – Level III |
| 16 | LAT-TD-01806 | Primary Boot Code |
| 17 | LAT-TD-02150 | Secondary Boot Code |
| 18 | FSW Traveler Document | SBC Tools User Manual |
| 19 |  | Telecommand and Telemetry Formats Handbook (URL: ) |
| 20 | LAT-SS-01378 | LAT Operations Plan |
| 21 | BAE Systems, 234A524 | RAD750 Board Hardware Specification |
| 22 | GSFC 433-SPEC-0001 | Mission System Specification |
| 23 | LAT-TD-00035 | LAT Coordinate System |
| 24 | FSW Traveler Document | FILE Package User Manual |
| 25 | LAT-SS-01539 | Storage Interface Board – Specification and ICD |
| 28 | 1196 EI-Y46311-000C | GLAST LAT Spacecraft to LAT Interface Control Document (SC-LAT ICD), Version C |
| 29 | 433-ICD-0001 (GLAST Project CCB) | LAT-GBM Interface Control Document (ICD) |
| 30 | 492-MOC-009 | Operations Data Products ICD |
| 31 | TBD | I&T Online System Science Data Format http://www-glast.slac.stanford.edu/IntegrationTest/ONLINE/docs/Online%20System%20Science%20Data%20Format.doc |
| 32 | FSW Traveler Document | LHK Manual |
| 33 | FSW Traveler Document | LATC User’s Guide |
| 34 | LAT-MD-04443 | ISOC Management and Development Plan |

# Acronyms

| Acronym | Defintion |
| --- | --- |
| ACD | Anticoincidence Detector |
| ADC | Analog to Digital Converter |
| AEM | ACD Electronics Module |
| AGN | Active Galactic Nuclei |
| BEA | Base Electronics Assembly |
| BOL | Beginning of Life |
| CAL | Calorimeter |
| CFC | Carbon Fiber Composite |
| CG | Center of Gravity |
| CNO | Carbon Nitrogen Oxide |
| CTE | Coefficient of Thermal Expansion |
| DC | Direct Current |
| DFS | Data Flow System |
| EMI | Electromagnetic Interference |
| EOL | End of Life |
| FREE | Front -End Electronics |
| GAFE | GLAST Analog Front End |
| GARC | GLAST Analog Readout Controller |
| GLAST | Gamma-ray Large Area Space Telescope |
| GLT | GLAST Analog Readout Controller |
| GRB | Gamma Ray Burst |
| GSE | Ground Support Equipment |
| GSFC | Goddard Space Flight Center |
| HLD | High Level Discriminator |
| HVBS | High Voltage Bias Supply |
| ICD | Interface Control Document |
| IRD | Interface Requirements Document |
| LAT | Large Area Telescope |
| LLD | Low Level Discriminator |
| LVDS | Low Voltage Differential Signal |
| MGSE | Mechanical Ground Support Equipment |
| MIP | Minimum Ionizing Particle |
| MLI | Multi Layer Insulation |
| MPLS | Multi Purpose Lifting Sling |
| MSB | Most Significant Bit |
| N | Newtons |
| PMT | Photo Multiplier Tube |
| RMS | Root Mean Square |
| SRD | Science Requirements Document |
| TACK | Science Requirements Document |
| TBR | To Be Resolved |
| TBD | To Be Determined |
| T&DF | Trigger and Dataflow System |
| TEM | Tower Electronics Module |
| TKR | Tracker |
| TRG | Trigger |
| TSA | Tile Shell Assembly |

# Overview of the Subsystems Exchanging Data

This section of the ICD briefly describes the roles and functions of the major subsystems exchanging the data described in this document.

## Flight Software

Currently a part of the DAQ, Electronics, and FSW Organization, the LAT FSW Team uses a set of custom-built and standard tools (GCC compiler, CMX/FMX code management tools, Jira issue tracking tool) to develop the LAT FSW according to requirements specified in [15]. The FSW design has passed its Preliminary Design and Critical Design Reviews. FSW will deliver all source code, the compiled operational FSW load, a command and telemetry data dictionary, and CDRLs to the Integration and Test Group on successful conclusion of Acceptance Testing.

FSW running on one of the two redundant spacecraft interface units (SIUs) provides the command, control and configuration functions for the instrument and handles instrument health monitoring. The SIU is responsible for all LAT external communications via the 1553 interface. All LAT commands (other than SIU power on and reset commands) are routed through the SIU. All LAT 1553 telemetry is managed through the SIU, which collects housekeeping and low rate science data from the other LAT subsystems and responds to requests for it from the spacecraft. The SIU manages the LAT operational modes and detailed configuration based on ground commands, automatic control logic and stored, pre-defined configurations. The SIU maintains LAT pointing knowledge based on information provided by the SC via the 1553. The SIU monitors the health of other LAT components and can perform autonomous shutdown in response to a failure detection or load shedding command from the SC. Functionally, the SIU performs the transient monitoring and handling tasks, including processing and responding to transient alerts from the ground and GBM.

Flight software running on 2 of 3 event processor unit(s) (EPUs, the third EPU is a backup) is responsible for filtering the data produced by the T&DF electronics system, rejecting the high flux of cosmic background but keeping the photon interaction events that are the basis of the science data. The EPUs will then perform a preliminary (LAT relative) reconstruction of the photon events. Identical FSW will run on each of the EPUs. The EPU configuration is managed by the SIU via a CPU-to-CPU message protocol. Event data is placed directly in the EPU memory by the Event Builder over the LATp communications fabric.

## Instrument Science Operations Center

The LAT Instrument Science Operations Center (ISOC) is responsible for LAT instrument operations, science analysis, and data processing. It consists of several functional elements

As discussed in [34], the LAT ISOC consists of several functional elements:

- The Command, Health and Safety team supports mission planning, acquires LAT telemetry, monitors LAT health & safety, maintains LAT flight software and configuration control, generates LAT command uploads, interfaces with the GLAST MOC, and supports the rapid alert capability.

- The Flight Software team maintains and validates the flight software and the instrument Testbed.  This team updates the flight software, maintains configuration control for the on-orbit software, and performs verification (including regressive analyses) to validate any changes to the flight software before any uploads. This team maintains the database that tracks the state of the instrument and its data products.

- The Performance Verification and Optimization team provides ongoing assessment of the performance of the LAT as a detector, generates the high-level LAT data products, including the instrument response functions, and manages the data, including distribution to LAT mirror analysis sites and to the SSC. Large-scale Monte Carlo simulations of the instrument will be performed by this team.

- The Science Data Products team uses SAS provided software to process LAT data to generate level 1 and 2 data products, generates the point source catalog, monitors for transient sources, and interfaces with and distributes data to the LAT science team and the GLAST SSC.

- The Science Analysis Software team maintains the code generated by the SAS subsystem and generates new code as needed, supplying these tools as needed to the collaboration and to the GSSC.

## Other Subsystems Associated with the Interface

The ISOC does not exchange files and data directly with the LAT FSW. Exchange is mediated by the GSSC and the MOC. These organizations are briefly described in this section.

### Mission Operations Center

The MOC performs all observatory commanding, monitoring, and level 0 data processing and delivery to the IOCs and GSSC.  The MOC provides rapid response for the follow-up of Target of Opportunities (ToOs) requested by the science team or science community.  The MOC incorporates automation of spacecraft operations and data processing to permit a small operations team and "lights-out" operation, and to speed data processing and response to ToOs.  The MOC is staffed by a Flight Operations Team (FOT) on an eight-hour per day, five-day per week basis.  MOC automation software will also identify potential anomalies and notify personnel if necessary.  The MOC shall generate Pass-oriented Level-0 (L0) telemetry data, and provide the data to the GSSC and IOCs.  The Pass-oriented L0 data will be retained online for 7 days at the MOC.  A subset of the housekeeping telemetry is maintained online for 30 days, and trend data is accumulated over the life of the mission.  In addition, the raw telemetry files as received from TDRSS (or the ground station), command logs, orbit data, the as-flown timelines, and MOC processing statistics and status are archived for the life of mission.

The MOC is based on the Integrated Test and Operations System (ITOS) command and telemetry system, government-off-the-shelf (GOTS) software products, and commercial-off-the-shelf (COTS) hardware and software tailored for GLAST mission support.  ITOS provides all command and telemetry functions, such as front-end processing, command and telemetry processing, real-time monitoring, and archiving. Computer security, with use of firewalls and other techniques, prevents intrusion and disruption of operations.

### GLAST Science Support Center

The GLAST Science Support Center receives level 0 data products from the MOC and sends the observing plan, target of opportunity orders, and the as-flow timeline to the MOC. The GSSC receives Level 1 data and other data products (including LAT and GBM command loads) from the two IOCs (the ISOC and the GLAST Burst Monitor’s Instrument Operations Center (IOC)); the GSSC will have a backup capability for performing Level 1 processing.  The GSSC and the IOCs have joint responsibility for the definition of the relevant science analysis tools and for the representation of the instrument response functions; GSSC scientists participate in the development of the science tools. The GSSC is responsible for supporting the astronomical community’s use of GLAST data by running the guest investigator (GI) program, providing analysis software and expertise, and disseminating GLAST data and results.  The GSSC will be responsible for the mission’s timeline.  Finally, the GSSC will archive the mission’s data.

# Conventions

The following conventions apply to the information in this ICD.

## File Types and File Layouts

The data described in this ICD are packaged in three formats.

Telecommands (file management and memory write commands) and telemetry (science data, contents of file dumps, and contents of memory reads) are formatted as CCSDS packets.

Telemetry packets are collected and subsequently bundled into level 0 Data Products by the MOC.

Source code and configuration files are binary files formatted in a LAT onboard file format defined by the FSW Team.

### Level 0 Data Products

The MOC bundles all CCSDS packets into level 0 data products and transmits these products to the ISOC for processing and analysis. The layout and detailed structure of the level 0 products are discussed in [30].

### CCSDS Packets

For context, the general CCSDS telemetry packet format is shown in Figure 2 below.

Figure 2: LAT CCSDS Telemetry Packet Layout

#### CCSDS Header Format

The LAT CCSDS telemetry packets have the standard 6 byte primary header, followed by a 8 byte secondary header specific to the LAT.  The LAT CCSDS telemetry header layout is shown in Figure 3 below.

| Figure 3: CCSDS Packet Header Layout |
| --- |
| 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| Packet Version=0 | T=0 | SH=1 | APID |
| SF | Sequence Count |
| Packet Length |
| Timestamp Seconds MSW () |
| Timestamp Seconds LSW (sample) |
| Timestamp Sub-Seconds MSW (sample) |
| Timestamp Sub-Seconds LSW (sample) |

Packet Version – The CCSDS packet version identifier.  Always = ‘0’ to indicate a Version 1 packet.

T – The CCSDS packet type identifier. Always = ‘0’ to indicate a telemetry packet.

SH – The CCSDS packet secondary header flag.  Always = ‘1’ to indicate that all GLAST telemetry packets have a secondary header.

APID – The CCSDS packet application identifier.

SF – The CCSDS packet sequence flags.  ‘00’ = continuation packet in the middle of a sequence.  ’01’ = first packet in a sequence.  ‘10’ = last packet in a sequence.  ‘11’ = standalone packet which is not part of a sequence.

Sequence Count – The CCSDS packet sequence count. This running counter increments for each packet generated for a given application type (indicated by the “APID” member).

Packet Length – The CCSDS packet length.  Indicates the length of application data plus the 2 bytes of secondary header minus ‘1’.

Timestamp Seconds – The seconds counter of the local timer. See Section ‎5.2 on page 3.

Timestamp Sub-Seconds – The sub-seconds counter of the local timer. Each tick of the counter represents 1 microsecond from the value presented in the Timestamp Seconds counter. See Section ‎5.2 on page 3.

### LAT Onboard Files

The general layout of files stored in EEPROM is shown in Figure 4 below. This format applies to both binary and text files.

For additional details, refer to [24].

Figure 4: LAT Onboard File General Format

LAT File Header File Data

All files are expected to be prefixed with a LAT File Header. The File Data contents are application-specific.

#### LAT File Header Format

The contents of the LAT File Header are defined in Figure 5 below.

| Figure 5: LAT Onboard File Header Format |
| --- |
| 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| Header Checksum MSW |
| Header Checksum LSW |
| Version = 2 | Cmp | Spare | Header Length = 28 |
| File Type |
| File Key MSW |
| File Key LSW |
| File Data Checksum MSW |
| File Data Checksum LSW |
| File Data Length MSW |
| File Data Length LSW |
| File Creation Timestamp Seconds MSW |
| File Creation Timestamp Seconds LSW |
| File Name 0 | File Name 1 |
| File Name 2 | File Name 3 |
| File Name 4 | File Name 5 |
| File Name 6 | File Name 7 |

Header Checksum – The checksum of the 32 byte file header.  The checksum is calculated using the ZLIB adler32 algorithm.

Version – The file structure version number. This version of the FILE package only supports version 2 file headers.

Cmp – Indicates if the file data is compressed.  A 0 will indicate the file data is not compressed and a 1 will indicate the file data is compressed.  The compression method will be dependent on the type of data contained in the file.

Header Length - The number of bytes in the header, not including the file header checksum, which is 4 bytes.  Set to 28 bytes.  This makes the total file header size 32 bytes.

File Type – Indicates the file content type.

File Key – A 32-bit number which should uniquely define the file, including versioning, within the lifetime of the mission.  Assigned by the file creator.

File Data Checksum – The checksum of the file data.  The checksum is calculated using the ZLIB adler32 algorithm.

File Data Length - The number of bytes in the data portion of the file.

File Creation Timestamp – Time when the file was created by ground processing.  The number of seconds elapsed since the time epoch.

File Name – Eight-character name of the file.  As assigned by the file creator.  If the file name is less than 8 characters then the name should be filled with the space character (0x20 ASCII).

## Representation of Time

The SIU FSW receives two time signals from the Spacecraft: (1) a 1-PPS (1 Hz) time hack over a discrete line, and (2) 500 msec to 800 msec before the time hack, a 1 Hz GPS timetone message from the Spacecraft over the 1553 interface. The GPS 1553 time message communicates the UTC time corresponding to the discrete line time hack, allowing FSW to synchronize itself to UTC time.

The FSW uses these signals and messages, along with the signal from the 20 MHz inside the LAT’s Global Trigger Electronics (GEM) module, to build time and attitude tables for internal use.

### Timestamps in CCSDS Headers

The CCSDS header preceding every telemetry packet issued by FSW contains a timestamp, in which time is represented as a 64-bit offset from a time epoch. The time epoch for LAT and the spacecraft bus is 00:00:00.0 hours of January 1st, 2001. That is the midnight between December 31st, 2000 and January 1st, 2001.

Timestamp Seconds represents the number of elapsed seconds since the epoch. Timestamp Sub-Seconds represents the number of microseconds elapsed since the last second.

### Timestamps in Science Data

At each occurrence of the 1-PPS signal, FSW inserts into event data a timestamp record, consisting of the Spacecraft timetone message and the value of the GEM 20 MHz clock at the exact time of the 1-PPS signal. The Spacecraft guarantees a timetone message at 1 Hz, though if it loses its lock with GPS, the Spacecraft interpolates the contents of the message. In some circumstances, FSW may also have to interpolate its timestamps. All time records in event data are flagged to indicate whether either the Spacecraft of the FSW timestamps have been manufactured rather than directly sampled. The detailed contents of the time records included in event data are described in Sections ‎7.2.2.1 and ‎7.2.3.2.

[[Timestamps in calibration data TBD]]

[[Timestamps in diagnostic data TBD]]

## Representation of Spacecraft Position and Orientation in Science Data

The SIU FSW receives Spacecraft attitude data packets from the SC, delivered at the 5 Hz SC attitude control loop rate, via the 1553 interface with the Spacecraft. This data is read by FSW into attitude/time lookup tables.

Position in science data will be given in inertial coordinates (in km) with respect to the center of the earth. The x-direction will be the J2000 vernal equinox, RA, Dec (0,0), the z-direction will be (0, +90°), and the y-direction will be consistent with a right-handed coordinate system.

The orientation of the spacecraft will be defined by the directions of the spacecraft z- and x-axes (in J2000 RA, Dec in deg).

# Summary of Data Described in this ICD

This section summarizes the data flows defined in this Interface Control Document. See Section ‎7, Section ‎8, and Section ‎9 for details.

## FSW Download Data Products Summary

The following table summarizes those data flows from the onboard FSW to the ISOC covered in this document: uncompressed and compressed event data, instrument calibration data, instrument diagnostic data, file dumps, and memory reads.

Event data is collected and stored on the SSR when the LAT is commanded to begin observations or when GRB observations are performed.

Instrument calibration data is collected and stored on the SSR when the LAT is commanded to perform charge injection calibration.

Instrument diagnostic data is collected and stored on the SSR when the LAT is commanded to carry out diagnostic procedures.

Memory read/dump data telemetry is transmitted as LMEMSIUDATA telemetry in response to the LMEMDUMPMEM, LMEMDUMPPCI, and LMEMDUMPREG telecommands.

File dump data telemetry is transmitted as TBD telemetry in response to LLFSDUMPCTDB and TBD telecommands.

| Table 1: FSW Download Data Products Summary |
| --- |
| ICD ID | Product | Science Data Tlm APID | Summary Description | Delivered | Size | Deliver to |
| FI-001 | SIU0 event data (streaming, uncompressed) | 0x3B6 | Each telemetry packet with this APID contains multiple time records and event data records in LAT Data Format (LDF), up to the maximum packet size of 64 Kbytes. Each LDF record contains one or more uncompressed event data records in Event Builder Format (EBF). See Section ‎7.2 on page 3. | Per SSR read | Total size per observation is variable. 64Kbytes per CCSDS packet. | SSR to MOC to ISOC |
| FI-002 | SIU1 event data (streaming, uncompressed) | TBD | See FI-001 above. | See above. | See above. | See above |
| FI-003 | EPU0 event data (streaming, uncompressed) | 0x3B7 | See FI-001 above. | See above. | See above. | See above |
| FI-004 | EPU1 event data (streaming, uncompressed) | 0x3B8 | See FI-001 above. | See above. | See above. | See above |
| FI-005 | EPU2 event data (streaming, uncompressed) | 0x3B9 | See FI-001 above. | See above. | See above. | See above |
| FI-006 | SIU0 event data (batched, compressed) | 0x3B6 | Each telemetry packet with this APID contains one event summary table, one timestamp table, one or more embedded compression tables, and multiple event data records in LAT Data Format (LDF), up to the maximum packet size of 64 Kbytes. Each LDF record contains one or more compressed event data records in Event Builder Format (EBF). See Section ‎7.2 on page 3. | Per SSR read | Total size per observation is variable. 64K per CCSDS packet. | SSR to MOC to ISOC |
| FI-007 | SIU1 event data (batched, compressed) | TBD | See FI-006 above. | See above. | See above. | See above. |
| FI-008 | EPU0 event data (batched, compressed) | 0x3B7 | See FI-006 above. | See above. | See above. | See above. |
| FI-009 | EPU1 event data (batched, compressed) | 0x3B8 | See FI-006 above. | See above. | See above. | See above. |
| FI-010 | EPU2 event data (batched, compressed) | 0x3B9 | See FI-006 above. | See above. | See above. | See above. |
| FI-011 | SIU0 calibration data | 0x3C5 | Telemetry contains PHA, TOT, pedestals, and other data resulting from commanded ACD, CAL, and TKR charge injection calibrations. See Section ‎7.3 on page 3. | Per SSR read | For SIU0: CAL total size 4.6 Mbytes TKR total 13 Mbytes ACD 0.3 Mbytes | SSR to MOC to ISOC |
| FI-012 | SIU1 calibration data | TBD | See FI-011 above. | See above. | See above. | See above. |
| FI-013 | EPU0 calibration data | 0x3C6 | See FI-011 above. | See above. | See above. | See above. |
| FI-014 | EPU1 calibration data | 0x3C7 | See FI-011 above. | See above. | See above. | See above. |
| FI-015 | EPU2 calibration data | 0x3C8 | See FI-011 above. | See above. | See above. | See above. |
| FI-016 | SIU0 diagnostic data | 0x3CA | TBD | Per SSR read | TBD | SSR to MOC to ISOC |
| FI-017 | SIU1 diagnostic data | TBD | TBD | Per SSR read | TBD | SSR to MOC to ISOC |
| FI-018 | EPU0 diagnostic data | 0x3CB | TBD | Per SSR read | TBD | SSR to MOC to ISOC |
| FI-019 | EPU1 diagnostic data | 0x3CC | TBD | Per SSR read | TBD | SSR to MOC to ISOC |
| FI-020 | EPU2 diagnostic data | 0x3CD | TBD | Per SSR read | TBD | SSR to MOC to ISOC |
| FI-021 | CPU memory dump | 0x314 | Telemetry contains words of data read from CPU memory. Data can be read from “unstructured” memory for low-level troubleshooting as well as from the “structured” Boot Diagnostics Region. | TBD | TBD | TBD |
| FI-022 | CPU PCI header dump | 0x314 | Telemetry contains PCI configuration header data. | On command | TBD | TBD |
| FI-023 | CPU register dump | 0x314 | Telemetry contains data read from RAD750 CPU registers. | On command | TBD | TBD |
| FI-024 | CPU file dump to 1553 | 0x31B | Telemetry contains contents of selected files stored in EEPROM. See Section ‎9 on page 3. | On command | 3Kbytes per CCSDS packet | MOC to ISOC |
| FI-025 | SIU0 file dump to SSR | 0x3CF | Telemetry contains contents of selected files stored in SIU0 EEPROM. See Section ‎9 on page 3. | Per SSR read | TBD | SSR to MOC to ISOC |
| FI-026 | SIU1 file dump to SSR | TBD | Telemetry contains contents of selected files stored in SIU1 EEPROM. See Section ‎9 on page 3. | Per SSR read | TBD | SSR to MOC to ISOC |
| FI-027 | EPU0 file dump to SSR | 0x3D0 | Telemetry contains contents of selected files stored in EPU0 EEPROM. See Section ‎9 on page 3. | Per SSR read | TBD | SSR to MOC to ISOC |
| FI-028 | EPU1 file dump to SSR | 0x3D1 | Telemetry contains contents of selected files stored in EPU1 EEPROM. See Section ‎9 on page 3. | Per SSR read | TBD | SSR to MOC to ISOC |
| FI-029 | EPU2 file dump to SSR | 0x3D2 | Telemetry contains contents of selected files stored in EPU2 EEPROM. See Section ‎9 on page 3. | Per SSR read | TBD | SSR to MOC to ISOC |

## FSW Upload Data Products Summary

All file uploads are performed using the LFILUPLSTART, LFILUPLDATA, and LFILUPLCOMMIT telecommand sequence, all with APID 0x641.

Memory writes are performed using LMEMLOADMEM (general memory loads), LMEMLOADPCI (PCI header writes), and LMEMLOADREG (CPU register write), APID 0x644.

For more information on these telecommands, refer to [19]

| Table 2: FSW Upload Data Products Summary |
| --- |
| ICD ID | Product | Telecmnd APID | Summary Description | Delivered | Max Size | Deliver to |
| IF-024 | Secondary boot code | 0x641 | File upload commands containing secondary boot code executable. Stored in Boot Objects Region of EEPROM. See Section ‎9.2 on page 3. | On update |  | ISOC to GSSC |
| IF-025 | RTOS image | 0x641 | File upload commands containing VxWorks operating system image. Stored in Boot Objects Region of EEPROM. See Section ‎9.3 on page 3. | On update |  | ISOC to GSSC |
| IF-026 | Secondary boot application database file | 0x641 | File upload commands containing application database used by the secondary boot process to control the load and initialization of FSW applications. Stored in Boot Objects Region of EEPROM. See Section ‎9.4 on page 3. | On update |  | ISOC to GSSC |
| IF-027 | FSW code modules | 0x641 | File upload commands containing FSW code libraries. Stored in File Region of EEPROM. See Section ‎9.5 on page 3. | On update |  | ISOC to GSSC |
| IF-028 | Software configuration files | 0x641 | File upload commands containing low-level software parameter files: individual task resource allocations, taskIDs, task priorities. See Section ‎9.6 on page 3. | On update |  | ISOC to GSSC |
| IF-029 | Application configuration files | 0x641 | File upload commands containing configuration files for individual applications/subsystems: data collection schedules, data conversion tables, and other parameters that vary widely by subsystem in question. See Section ‎9.7 on page 3. | On update |  | ISOC to GSSC |
| IF-030 | Instrument configuration files | 0x641 | File upload commands containing configuration files for the LAT instrument: register settings for front-ends, TEM, GEM, AEM Section ‎9.8 on page 3. | On update |  | ISOC to GSSC |
| IF-031 | Writes to CPU memory | 0x644 | Memory write commands to populate CPU memory addresses. See Section ‎8 on page 3. | On update |  | ISOC to GSSC |
| IF-032 | Writes to PCI headers | 0x644 | Memory write commands to populate fields in the PCI configuration headers in PCI memory space. | On update |  | ISOC to GSSC |
| IF-033 | Writes to CPU registers | 0x644 | Memory write commands to populate RAD750 CPU registers. | On update |  | ISOC to GSSC |

# Science Data

FSW reserves a “science data” APID space from 0x3A0 to 0x3D8 for data written to the Spacecraft’s Solid State Recorder, though not all telemetry in this range contains “actual” science data. Various FSW applications produce and transmit high volumes of data: the configuration manager application (LCM) can generate a lengthy software loaded report for each CPU, and can echo error and information messages passed by the low-level software messaging system at a high level of verbosity; the onboard EEPROM filesystem manager (LSM) can dump the contents of files of any size into telemetry. The resulting data cannot be transmitted to the ground in a single contact and must therefore be stored to the SSR for later retrieval. Thus, science data APIDs are assigned to this information for purposes of routing it to storage.

While the science data interface to the SSR handles a variety of high-volume data, this Interface Control Document describes only the large file and memory dumps and the “actual” science data: event data collected during observations, instrument calibration data, and instrument diagnostic data. The science data APIDs covered in this document are listed in Table 1 (page 3). All other telemetry in the science data APID range is described in the Telecommand and Telemetry Formats Handbook, [19].

## Science Data Delivery Mechanism

### Delivery Route

All science data telemetry packets are stored to the Solid State Recorder on board the Spacecraft. Packets are written to this device in the order in which they are processed on an SIU or EPU and sent via the Event Builder to the SSR.

As described in [30], the White Sands facility initiates dumps from the Solid State Recorder, and bundles the resulting “raw” CCSDS packets. The MOC retrieves this data from the White Sands facility, groups and sorts the raw packets by APID, and bundles the sorted data into level 0 data products, which are transferred to the ISOC for processing and analysis.

### Delivery Schedule

Event data for planned observations is delivered on a commanded schedule. Physics event data for GRBs is delivered on a variable schedule.

Instrument calibration and diagnostic data are delivered on a commanded schedule.

### Interruptions in Science Data Delivery

TBD.

## Event Data

Event data collected during planned physics observations and unplanned GRB observations is transmitted to the SSR as CCSDS packets that wrap multiple records in the LAT Data Format (LDF). The FSW can be commanded to send event data in an uncompressed stream or in compressed batches. All event data packets, whether they contain uncompressed or compressed data, contain the complete set of LDF data for events identified as candidates by the FSW event data filter.

Event data collection, filtering, compression, packaging, and routing to storage are handled by the LAT Physics Acquisition (LPA) application. LPA filters events, eliminating those of low interest through application of trigger discriminator, energy level, and track projection tests. On command from the ground, LPA can adjust the LAT Global Trigger to accommodate different types of planned observations or automatically loosen the Trigger if a GRB is detected. If batched event data is requested, LPA compresses the events, applying a customized compression scheme to the individual TKR, CAL, and ACD contributions to the event data. Filter, trigger, and compression configuration are described in Section ‎9.7.2.1 on page 3.

As indicated in Table 1, each CPU can send event data telemetry to the SSR using an APID allocated to that CPU. Uncompressed and compressed data packets from each CPU are telemetered using the same APIDs (TBD). The structure of the telemetry packet itself indicates whether the data is compressed or uncompressed. The layouts of the uncompressed data and compressed data packets are discussed in Sections ‎7.2.2 and ‎7.2.3.

### LAT Data Format

LDF is defined in [31], but the format is described here for reference. LDF is defined by the I&T Online group.

LDF records contain EBF (Event Builder Format) records, amongst other contributions. These EBF records contain event data in its most basic representation, the form in which it is generated by the LAT’s Event Builder Module. An LDF record has several layers. Moving from the outside in, the layers are:

LATdatagram. A 32 bit Identity field and a 32 bit Length field. Bits 0-20 of the Identity field hold a TypeID (value TBD). The remaining 12 bits of the Identity field hold a number identifying which version of the LDF TypeID scheme is being used (value TBD). The Length field defines the length of the LATdatagram, inclusive of all sub-elements.

LATcontribution. A 32 bit Identity field, 16 bit Opaque field, and 16 bit Length field. This is the payload of the LATdatagram. The Identity word is identical in format to the LATdatagram Identity word described above. The Opaque field contains event data-specific opaque data (TBD). The Length field specifies the LATcontribution’s length.

EBFevent. Variable-length records containing data from each of the LAT’s contributing devices: 16 TEMs, 1 AEM, 1 GEM, as assembled and formatted by the LAT’s Event Builder Module. The contents of the various EBFcontributions are summarized in Table 3 on page 3.

Figure 6 (below) depicts the contents of an LDF record from the LATdatagram down.

| Figure 6: Layout of a LAT Data Format (LDF) Record |
| --- |
| Table 3: Contents of Individual EBFcontributions in Event Data |
| EBFcontribution | Length (bytes) | Contents |
| GEMcontribution | TBD | tkrVector, roiVector, Cal LEVector, Cal HEVector, convector, conditionSummary, tileList, Livetime, Prescaled count, Discarded count, Sent count, triggerTime, onePPSTime, deltaEventTime |
| GLTcontribution | TBD | calStrobe, Tag, TACK, Readout4, zeroSuppress, Marker, Error, eventNumber, trgParityError |
| AEMcontribution | TBD | Hit map, Accept map, phaVector, parityError |
| CALcontribution x 16 | TBD | CAL log accepts, log values and range |
| TKRcontribution x 16 | TBD | TKR accepts, strips data, TOT data |

#### Detailed Layout of GEM Contribution

The field-by-field layout of the GEMcontribution is show in Figure X below. TBD.

#### Detailed Layout of GLT Contribution

The field-by-field layout of the GLTcontribution is show in Figure X below. TBD.

#### Detailed Layout of AEM Contribution

The field-by-field layout of the AEMcontribution is show in Figure X below. TBD.

#### Detailed Layout of CAL Contribution

The field-by-field layout of the CALcontribution is show in Figure X below. TBD.

#### Detailed Layout of TKR Contribution

The field-by-field layout of the TKRcontribution is show in Figure X below. TBD.

### Streaming Uncompressed Event Data

The [[TBD]] command is sent to the LPA application to indicate that event data should be sent in streaming, uncompressed format.

In this format, multiple LATdatagrams are packaged into telemetry, up to a limit of 64 Kbytes worth of datagrams per CCSDS packet. Timestamp records are inserted into the telemetry immediately before the first datagram to use them. The individual EBFcontributions in the datagrams are uncompressed. Headers internal to the datagrams and leading and trailing bytes between contributors are trimmed (TBD). Otherwise, event data is packaged exactly as it is forwarded by the LAT Event Builder Module.

The layout of a streaming, uncompressed event data packet is shown schematically in Figure 7 below.

Figure 7: Layout of Streaming Uncompressed Event Data

#### The Streaming Timestamp Record

The streaming timestamp record is structured as shown below.

| Table 4: Structure of the Timestamp Record Included in Streaming Uncompressed Event Data |
| --- |
| Field | Length | Description |
| Elapsed Time | 32 bits | Seconds since Midnight, January 1, 2001 |
| Spectrum-Astro Time Flags | TBD | [TBD: Records whether GPS was locked by Spacecraft; if not, GPS time tone message was “faked”] |
| FSW Attitude/Time Flags | TBD | [TBD: |
| 1-PPS Message Index | 7 bits |  |
| GEM clock value | 25 bits | Value of the GEM clock at the time of the 1-PPS signal |

### Batch Compressed Event Data

The [[TBD]] command is sent to the LPA application to indicate that event data should be sent in batched, compressed format.

The LPA application uses a combination of on-the-fly algorithmic compression and table-driven compression to reduce the size of LATdatagrams before packet assembly. The latter type of compression is defined by compression tables stored in the LAT onboard EEPROM file system.

Again, as with uncompressed event data, multiple LATdatagrams are packaged into telemetry, up to a limit of 64 Kbytes worth of datagrams per CCSDS packet. Each compressed packet begins with an event summary table and a timestamp record table generated by the LPA application during batch compression and assembly. Each packet also contains embedded compression tables defining any on-the-fly compression performed. Individual EBF contributions are compressed. While science data telemetry APIDs for each CPU are the same for compressed and uncompressed data (TBD), the presence of the event summary table, timestamp record table, and compression tables immediately identifies compressed packets.

The layout of a batched, compressed event data packet is shown schematically in Figure 7 on page 3.

#### Event Summary Table

The Event Summary table describes the time sequenced structure of the events in the packet, indicating where “occurrences” (most notably, a change in the 1-PPS counter) take place among the LATdatagrams in the packet. The table consists of a variable number of fixed 16-bit records structured as shown below (TBD).

| Table 5: Structure of the Records in the Event Summary Table (Batched Compressed Event Data) |
| --- |
| Field | Length | Description |
| Occurrence Description | 7 bits | Describes the type of occurrence: Bit 0: No More Bit 1: Range exceeded Bit 2: NOP. Used with Bit 0 to indicate “end-of-file” Bit 3: Timestamp Occurred Bit 4: Error Event Occurred Bit 5: TBD Bit 6: TBD |
| Delta to Next Occurrence | 9 bits | Indicates location of next occurrence. Bit 1 of Occurrence Description indicates location exceeds the range of this field. In this case, this field should be juxtaposed to the next 16 recorded bits to determine the delta. (TBD) |

Figure 8: Layout of Batched Uncompressed Event Data

#### Timestamp Record Table

The timestamp table consists of a fixed header and 1 record per timestamp. TBD.

| Table 6: Header for Timestamp Table Records (Batched Compressed Event Data) |
| --- |
| Field | Length |
| Beginning Seconds | 32 bits |
| Beginning Index | 7 bits |
| Beginning Time | 25 bits |
| Reserved | 7 bits |
| Beginning Frequency | 25 bits |

| Table 7: Timestamp Records (Batched Compressed Event Data) |
| --- |
| Field | Length |
| Fake Record? | 1 bit |
| Delta Exceeded? | 1 bit |
| Delta Time | 14 bits signed |

#### Data Compression Scheme

[[Separate compression algorithms for ACD, TKR, CAL, other data. TBS.]]

### Other Event Data Telemetry

Housekeeping telemetry contains a summary statistics packet reporting the current settings for the event filter and the number of events discarded from the event data stream on each of the 16 filter “channels” [[exact contents TBD]].

On command, the LPA application will send a diagnostic telemetry packet containing a more detailed set of filter statistics [[APID and contents TBD]].

The filter configuration file is discussed in Section ‎9.7.3.2 on page 3. Also see the Telecommand and Telemetry Formats Handbook [19].

## Instrument Calibration Data

Charge injection calibration generates data used to produce:

DAC to ADC curves for each discriminator in the detector front-ends

Measurements of cross-talk between front-end channels

Time over threshold curves

Failed channel maps

FSW will generate different sets of science data depending on which of several categories or “styles” of calibration is performed

ACD Pulse Height Analysis

ACD CNO

ACD Accepts

ACD Hits

ACD Pedestals

CAL ADCs

CAL Low Energy Trigger

CAL High Energy Trigger

CAL Accepts

CAL Pedestals

TKR Accepts

TKR Time over Threshold

TKR Trigger Scan

The contents of these data sets are summarized in Table 8 below.

| Table 8: Instrument Calibration Data Summary Contents |
| --- |
| Product | Telemetry APID | Type of Calibration Run | Description of Telemetry Contents |
| SIU0 calibration data | 0x3C5 | ACD PHA |  |
|  |  | ACD CNO | TBD |
|  |  | ACD Accepts |  |
|  |  | ACD Hits |  |
|  |  | ACD Pedestals |  |
|  |  | CAL ADCs |  |
|  |  | CAL Low Energy Trigger |  |
|  |  | CAL High Energy Trigger |  |
|  |  | CAL Accepts |  |
|  |  | CAL Pedestals |  |
|  |  | TKR Accepts |  |
|  |  | TKR Time Over Threshold |  |
|  |  | TKR Trigger Scan |  |
| SIU1 calibration data | TBD | TBD | TBD |
| EPU0 calibration data | 0x3C6 | TBD | TBD |
| EPU1 calibration data | 0x3C7 | TBD | TBD |
| EPU2 calibration data | 0c3C8 | TBD | TBD |

### Detailed Contents of Calibration Data

The total volume of calibration data and the time required to collect it, per subsystem, is estimated in Table 9 below.

| Table 9: Volume and Collection Time for Calibration Data |
| --- |
| Subsystem | Projected Time | Uncompressed Volume | Compressed Volume |
| CAL | 10 seconds | 420 Mbits | 150 Mbits |
| TKR | 640 seconds | 8,440 Mbits | 420 Mbits |
| ACD | 10 seconds | 30 Mbits | 10 Mbits |

#### Contents of ACD PHA Data Set (etc)

[[Detailed contents per calibration “style”: TBD]]

### Compression of Calibration Data

[[TBD. Much of the data collected in calibration can be compressed using the compression scheme used to event data]]

### Interruption of Calibration Data Collection

TBD.

## Instrument Diagnostic Data

[[TBD]]

# Memory Writes and Reads

The FSW provides memory write and memory read commands to allow low-level troubleshooting of PCI devices and the RAD750 CPU board, and to allow testing of alternate RTOS and secondary boot code executables in flight. Memory can be read and written when the Primary Boot Code enters the boot shell stage. Memory can also be read and written after boot is complete and FSW applications are up and running.

Detailed information on how the primary and secondary boot processes configure SDRAM, PCI configuration registers, PPCI internal registers, PCI memory space, and SUROM can be found in [16] and [17].

## General Memory Map

The hardware memory map, which is the same during and after the boot process, is shown in Figure 9 below. Briefly:

The RAD750 SDRAM is the execution area for all FSW applications. The most commonly written and read areas in SDRAM are the Boot Diagnostics Region, the RTOS Load Region, and the 2 Second Stage Boot RAM Modules. The LMEMLOADMEM and LMEMDUMPMEM telecommands are used to manipulate SDRAM.

The PCI I/O Space use used for TBD.

PPCI (CPU) internal registers provide access to low-level functionality of the RAD750 CPU board. The LMEMLOADREG and LMEMDUMPREG telecommands are used to manipulate CPU register settings.

PCI Memory Space contains PCI configuration headers to configure operation of CPU components such as the Spacecraft Interface Board and LAT Communications Board on the PCI bus. The LMEMLOADPCI and LMEMDUMPPCI telecommands are provided to manipulate PCI configuration headers.

RAD750 SUROM is used to store the Primary Boot Code. This region is not writeable.

| Figure 9: FSW Hardware Memory Map |
| --- |
| RAD750 SDRAM | 00000000 |
| PCI I/O Space [00000000 – 0FFFFFFF] | 80000000 |
| PPCI Internal Registers | BF800000 |
| PCI Memory Space [00000000 – 0FFFFFFF] | C0000000 |
| RAD750 SUROM | FFF00000 |

### Boot SDRAM Regions

Once the primary boot process has reached the boot shell stage and the boot shell is initialized, SDRAM is organized as shown in Table 10 below.

These areas of SDRAM can be written and read using memory management telecommands defined in the Telecommand and Telemetry Formats Handbook [19].

| Table 10: Boot Shell SDRAM Memory Map |
| --- |
| Region | Start Address | Read/Write | Description |
| Reserved | 00000000 | Read/Write | N/A |
| Boot Shell Reset Vector | 00000100 | Read/Write | N/A |
| Boot Shell Exception Vectors | 00000200 | Read/Write | N/A |
| Boot Code Stack | 00003000 | Read/Write | N/A |
| EMC Parameter Region | 0000FF00 | Read Only | N/A |
| Boot Diagnostics Region | 0000FF80 | Read/Write | Contains pertinent information about the boot state. Read this area to access primary boot flags, secondary boot flags, exceptions, memory test results, and other boot diagnostic results. Can also be used to instruct the primary boot code to load the default RTOS image and start the secondary boot process. Also contains FSW application flags and data (TBD: watchdog circular buffer) |
| Second Stage Boot RAM Module 0 | 00010000 | Read/Write | Stores temporary or trial versions of secondary boot module 0 (secondary boot executable) |
| Second Stage Boot RAM Module 1 | 00070000 | Read/Write | Stores temporary or trial versions of secondary boot module 1 (application database). |
| VxWorks RTOS RAM Load Region | 00080000 | Read/Write | Write a provisional RTOS to this area and test before writing to EEPROM TBD |
| Boot Shell File Upload Buffer | 00140000 | Read/Write | Temporary storage area for upload file data before it is written to EEPROM. |
| LCB Input Ring Buffer | 00200000 | Read/Write | Working area. Directly tied to LCB DMA ops. Supports reception of telecommand packets on event fabric. |
| I/O Output Buffer | 002A0000 | Read/Write | [[Working area: 1553 uses it to construct boot housekeeping, EPU LCB uses it for the command list to send housekeeping packets to SIU]] |
| I/O Input Buffer | 002A1000 | Read/Write | Working area: 1553 uses it to wrangle incoming telecommand packets; LCB uses it to extract incoming |
| Boot Shell Memory Heap | 002A2000 | Read/Write | Working area. ZLIB inflation calls. |
| Boot Code Program Data | 002E8000 | Read/Write | Storage for boot code text and data segments. |
| VxWorks RTOS Image | 00300000 00BFFFFF | Read/Write | [[Storage for RTOS text and data segments when the RTOS image is read from EEPROM and inflated.]] |

### Post-Boot SDRAM Regions

After secondary boot is complete, SDRAM is organized as shown in Table 11 below.

| Table 11: RTOS initialization and Application SDRAM Memory Map |
| --- |
| Region | Start Address | Read/Write | Description |
| RTOS Exception Vector Table | 00000000 | Read/Write | N/A |
| Initialization Stack | 00003000 | Read/Write | N/A |
| RTOS Boot Line | 0000FD00 | Read/Write | N/A |
| RTOS Exception Message | 0000FE00 | Read/Write | N/A |
| EMC Parameter Region | 0000FF00 | Read Only | N/A |
| Boot Diagnostics Region | 0000FF80 | Read Only | Contains pertinent information about the boot state. Read this area to access primary boot flags, secondary boot flags, exceptions, memory test results, and other boot diagnostic results. Can also be used to instruct the primary boot code to load the default RTOS image and start the secondary boot process. Also contains FSW application flags and data (TBD: watchdog circular buffer) |
| Second Stage Boot RAM Module 0 | 00010000 |  |  |
| Second Stage Boot RAM Module 1 | 00070000 |  |  |
| VxWorks RTOS Load Region | 00300000 |  |  |
| RTOS System Memory Pool | _end |  |  |
| FSW Application Region | 00800000 sysMemTop() |  |  |

The Applications region is further divided as shown in Table

| Table 12: Detailed FSW Application SDRAM Memory Map |
| --- |
| Region | Start Address | Read/Write | Description |
| TBD | 00C00000 | TBD | TBD |
| TBD | TBD | TBD | TBD |
| TBD | TBD | TBD | TBD |

### PCI Memory Space

PCI Memory Space contains PCI configuration headers used to configure the operation of CPU components on the CPU’s cPCI bus. The LMEMLOADPCI and LMEMDUMPPCI telecommands are used to interact with these headers.

Figure 10 shows the layout of the PCI configuration space. See [25] for complete details.

Figure 10: cPCI Configuration Registers

### CPU Register Space

Refer to [21] for complete documentation on the CPU register set for the RAD750.

CPU registers fall into the categories identified in Table 13 below.

| Table 13: RAD750 CPU Register Types and Usage |
| --- |
| Register Type | Number | Description | Read/Write | Use in boot shell stage |
| GPR | 32 | General purpose registers acting as source or destination registers for integer instructions. | Read/Write | XX |
| CR | 1 | Condition register (8 4-bit fields), used for testing and branching operations. | Read/Write | XX |
| FPSCR | 1 | Floating point status and control register, containing all floating-point exception signal bits, exception summary bits, exception enable bits, rounding control bits | Read/Write | XX |
| XER | 1 | Integer condition register, indicating overflows and carry conditions for integer operations | Read/Write | XX |
| LR | 1 | Link register, used by PPC branching operations to store links to branch instructions | Read/Write | XX |
| CTR | 1 | Count register, holds a loop count for PPC branching operations | Read/Write | XX |
| TBL | 1 | Time base lower register | Read Only | XX |
| TBU | 1 | Time base upper register | Read Only | XX |
| MSR | 1 | Machine state register, storing the state of the processor | Read/Write | XX |
| IBAT | 8 | Instruction block address translator registers, used to set up PPC physical to virtual address translations | Read/Write | XX |
| DBAT | 8 | Data block address translator registers, used to set up PPC physical to virtual address translations | Read/Write | XX |
| SDR1 | 1 | Page table configuration register, specifying the page table base address used for virtual-to-physical address translation | Read/Write | XX |
| PVR | 1 | Processor version register, identifying the versions(model) and revision level of the PPC processor | Read Only | XX |
| DAR | 1 | Data address register, used to store the effective address of an instruction that has generated a DSI or alignment exception | Read/Write | XX |
| SPRG | 4 | Supervisor global register, general purpose registers reserved for PPC operating system use | Read/Write | XX |
| DSISR | 1 | Data access exception status register, recording the cause of DSI and alignment exceptions | Read/Write | XX |
| SRR | 2 | Machine status save/restore registers, used to save and restore machine status on exceptions | Read/Write | XX |
| DEC | 1 | Decrementer register, a 32-bit decrementing counter that can be used to cause of decrementer exception after a delay | Read/Write | XX |
| DABR | 1 | Data address breakpoint register, provided to control the data address breakpoint facility in debugging DSI exceptions | Read/Write | XX |
| EAR | 1 | External address register, used to control a special-purpose external device (TBD: which for FSW setup) | Read/Write |  |
| SR | 16 | Segment registers, used for memory management | Read/Write |  |
| FPR | 60 | Floating point registers acting as source or destination for floating-point instructions. | Read/Write |  |

[[TBD: zero’d out on reboot and thus have not effect on primary boot on the way back around?; have any effect on regular operations]]

Addressing for CPU registers is defined in Table 14 below.

| Table 14: CPU Register Offsets |
| --- |
| Offset | Register | Offset | Register | Offset | Register | Offset | Register |
| 0x000 | GPR 0 | 0x0a0 | IBAT 0U | 0x140 | SR 11 | 0x1e0 | FPR 17L |
| 0x004 | GPR 1 | 0x0a4 | IBAT 0L | 0x144 | SR 12 | 0x1e4 | FPR 18U |
| 0x008 | GPR 2 | 0x0a8 | IBAT 1U | 0x148 | SR 13 | 0x1e8 | FPR 18L |
| 0x00c | GPR 3 | 0x0ac | IBAT 1L | 0x14c | SR 14 | 0x1ec | FPR 19U |
| 0x010 | GPR 4 | 0x0b0 | IBAT 2U | 0x150 | SR 15 | 0x1f0 | FPR 19L |
| 0x014 | GPR 5 | 0x0b4 | IBAT 2L | 0x154 | FPR 0U | 0x1f4 | FPR 20U |
| 0x018 | GPR 6 | 0x0b8 | IBAT 3U | 0x158 | FPR 0L | 0x1f8 | FPR 20L |
| 0x01c | GPR 7 | 0x0bc | IBAT 3L | 0x15c | FPR 1U | 0x1fc | FPR 21U |
| 0x020 | GPR 8 | 0x0c0 | DBAT 0U | 0x160 | FPR 1L | 0x200 | FPR 21L |
| 0x024 | GPR 9 | 0x0c4 | DBAT 0L | 0x164 | FPR 2U | 0x204 | FPR 22U |
| 0x028 | GPR 10 | 0x0c8 | DBAT 1U | 0x168 | FPR 2L | 0x208 | FPR 22L |
| 0x02c | GPR 11 | 0x0cc | DBAT 1L | 0x16c | FPR 3U | 0x20c | FPR 23U |
| 0x030 | GPR 12 | 0x0d0 | DBAT 2U | 0x170 | FPR 3L | 0x210 | FPR 23L |
| 0x034 | GPR 13 | 0x0d4 | DBAT 2L | 0x174 | FPR 4U | 0x214 | FPR 24U |
| 0x038 | GPR 14 | 0x0d8 | DBAT 3U | 0x178 | FPR 4L | 0x218 | FPR 24L |
| 0x03c | GPR 15 | 0x0dc | DBAT 3L | 0x17c | FPR 5U | 0x21c | FPR 25U |
| 0x040 | GPR 16 | 0x0e0 | SDR1 | 0x180 | FPR 5L | 0x220 | FPR 25L |
| 0x044 | GPR 17 | 0x0e4 | PVR | 0x184 | FPR 6U | 0x224 | FPR 26U |
| 0x048 | GPR 18 | 0x0e8 | DAR | 0x188 | FPR 6L | 0x228 | FPR 26L |
| 0x04c | GPR 19 | 0x0ec | SPRG 0 | 0x18c | FPR 7U | 0x22c | FPR 27U |
| 0x050 | GPR 20 | 0x0f0 | SPRG 1 | 0x190 | FPR 7L | 0x230 | FPR 27L |
| 0x054 | GPR 21 | 0x0f4 | SPRG 2 | 0x194 | FPR 8U | 0x234 | FPR 28U |
| 0x058 | GPR 22 | 0x0f8 | SPRG 3 | 0x198 | FPR 8L | 0x238 | FPR 28L |
| 0x05c | GPR 23 | 0x0fc | DSISR | 0x19c | FPR 9U | 0x23c | FPR 29U |
| 0x060 | GPR 24 | 0x100 | SRR 0 | 0x1a0 | FPR 9L | 0x240 | FPR 29L |
| 0x064 | GPR 25 | 0x104 | SRR 1 | 0x1a4 | FPR 10U | 0x244 | FPR 30U |
| 0x068 | GPR 26 | 0x108 | DEC | 0x1a8 | FPR 10L | 0x248 | FPR 30L |
| 0x06c | GPR 27 | 0x10c | DABR | 0x1ac | FPR 11U | 0x24c | FPR 31U |
| 0x070 | GPR 28 | 0x110 | EAR | 0x1b0 | FPR 11L | 0x250 | FPR 31L |
| 0x074 | GPR 29 | 0x114 | SR 0 | 0x1b4 | FPR 12U |  |  |
| 0x078 | GPR 30 | 0x118 | SR 1 | 0x1b8 | FPR 12L |  |  |
| 0x07c | GPR 31 | 0x11c | SR 2 | 0x1bc | FPR 13U |  |  |
| 0x080 | CR | 0x120 | SR 3 | 0x1c0 | FPR 13L |  |  |
| 0x084 | FPSCR | 0x124 | SR 4 | 0x1c4 | FPR 14U |  |  |
| 0x088 | XER | 0x128 | SR 5 | 0x1c8 | FPR 14L |  |  |
| 0x08c | LR | 0x12c | SR 6 | 0x1cc | FPR 15U |  |  |
| 0x090 | CTR | 0x130 | SR 7 | 0x1d0 | FPR 15L |  |  |
| 0x094 | TBL | 0x134 | SR 8 | 0x1d4 | FPR 16U |  |  |
| 0x098 | TBU | 0x138 | SR 9 | 0x1d8 | FPR 16L |  |  |
| 0x09c | MSR | 0x13c | SR 10 | 0x1dc | FPR 17U |  |  |

## Dumps of the Boot Diagnostics Region

The FSW maintains a “permanent” region of SDRAM, the Boot Diagnostics Area, in which to record errors encountered during the primary and secondary boot processes. [[TBD And Apps scribble anything here?]]. The Boot Diagnostics Area begins at address 0000FF80. The detailed layout of this area is shown in Table 15 below.

At each offset location, bitfields are used to report status information. The layout of these bitfields and the bits used to signal status are defined [16].

| Table 15: Layout of the SDRAM Boot Diagnostics Region |
| --- |
| Offset (bytes) | Mnemonic | Description | Data Source |
| 0x00 | DIAGS_PRIM_BOOT_FLAGS | Primary Boot Flags. | Set by startup diagnostics or reboot request. |
| 0x04 | DIAGS_SEC_BOOT_FLAGS | Secondary Boot Flags. | Set by PBC from parameters specified in the Boot RTOS Execute Telecommand. |
| 0x08 | DIAGS_EXC_COUNT_OFF | Counter of exceptions that have occurred. Reset on cold start. | PBC, SBC or application exception vector. |
| 0x0C | DIAGS_EXC_VEC | Exception Vector | PBC, SBC or application exception handler. |
| 0x10 | DIAGS_EXC_SRR0_REG | Exception SSR0 Register Contents | PBC, SBC or application exception handler. |
| 0X14 | DIAGS_EXC_SRR1_REG | Exception SSR1 Register Contents | PBC, SBC or application exception handler. |
| 0X18 | DIAGS_EXC_DAR_REG | Exception DAR Register Contents | PBC, SBC or application exception handler. |
| 0X1C | DIAGS_EXC_DSISR_REG | Exception DSISR Register Contents | PBC, SBC or application exception handler. |
| 0x20 | DIAGS_PCI_STATUS2_REG | Exception PCI Status 2 Register Contents | PBC, SBC or application exception handler. |
| 0x24 | DIAGS_MEM_STATUS_REG | Exception Memory Status Register Contents | PBC, SBC or application exception handler. |
| 0x28 | DIAGS_EXC_TASK_ID | Exception task ID. | SBC or application exception handler. |
| 0x2C | DIAGS_MT_RESULTS_1 | First Pass Memory Test Results | Startup diagnostics. |
| 0x30 | DIAGS_MT_ADDR_1 | First Pass Memory Test Failure Address | Startup diagnostics. |
| 0x34 | DIAGS_MT_ACTUAL_1 | First Pass Memory Test Failure Data | Startup diagnostics. |
| 0x38 | DIAGS_MT_RESULTS_2 | Second Pass Memory Test Results | Startup diagnostics. |
| 0x3C | DIAGS_MT_ADDR_2 | Second Pass Memory Test Failure Address | Startup diagnostics. |
| 0x30 | DIAGS_MT_ACTUAL_2 | Second Pass Memory Test Failure Data | Startup diagnostics. |
| 0x44 | DIAGS_SEC_BOOT_FAIL_ERR | Secondary Boot Error Code | Secondary boot. |
| 0x48 | DIAGS_SEC_BOOT_FAIL_IDX | Secondary Boot Error Index | Secondary boot. |
| 0x4C | DIAGS_SEC_BOOT_FAIL_DATA | Secondary Boot Error Data | Secondary boot. |
| 0x50 | DIAGS_BIST_750 | RAD750 BIST Results | Startup diagnostics. |
| 0x54-0x5C | DIAGS_BIST_PPCI | PPCI BIST Results | Startup diagnostics. |
| 0x5C | DIAGS_MT_COUNT | Number of SDRAM bytes tested | Startup diagnostics. |
| 0x60-0x7C | DIAGS_APP_INFO | Application Information | Secondary boot or Application. |

## Dumps of the Watchdog Timer Circular Buffer

[[TBD: Part of the APPS area of Boot Diagnostics Area? Names and last tasks not responding, etc.]]

# Software File Uploads and Dumps

The onboard FSW must be configured for operation and must be maintained as files become corrupted, software defects are identified and corrected, and new functionality is added. Configuration, upgrade, and maintenance are accomplished through addition and replacement of files stored in SIU and EPU EEPROM.

Production, testing, and packaging of these software files for upload is the responsibility of ISOC’s FSW Team. Upload scheduling is the responsibility of ISOC’s Commanding, Health and Safety Team.

FSW files meant for upload fall into the following categories:

Secondary boot code

RTOS images

Secondary boot application databases

FSW code modules

Software configuration files

Application configuration files

Instrument configuration files

The names and sizes, format, production toolset, and linkages for each of these categories of file are described in this section.

## Software File Delivery Mechanism

### Layout of EEPROM

Each CPU provides two banks of EEPROM. The layout of the EEPROM banks is depicted in Figure 11 below (the two banks are identical; only the upper bank is shown in the figure).

Figure 11: Layout of EEPROM (Upper Bank Shown)

The “Boot Objects Region” contains the boot bank header and storage locations for:

- The secondary boot executable (Second Stage Boot Area 0)

- The secondary boot application database (Second Stage Boot Area 1)

- The VxWorks executable image file (RTOS)

The bank header defines the offsets and sizes of these three file areas.

The “File Region” provides space for the TFFS file system, where all configuration files and all FSW source code libraries are stored.

### Delivery Route

Before launch, software files from each of the categories listed above are stored in SIU and EPU EEPROM as the initial mission software load. Thereafter, new software files are uploaded only as files become corrupted or updates are required.

All software files are uploaded using the same mechanism. FSW provides a set of upload telecommands for uploading files to the SIU, committing them to EEPROM, copying them from the SIU to the EPUs, and generally managing the onboard EEPROM filesystem. Refer to [19] for the latest list of FSW telecommands.

Once ISOC determines that files must be added or replaced, the ISOC FSW Team generates the files, segments them with TBD tool, and constructs and validates the telecommand sequence needed to accomplish the upload. The ISOC Commanding, Health and Safety Team schedules and coordinates the upload with the GSSC, and the MOC ultimately issues the telecommands to the Spacecraft.

Once the files have been stored to EEPROM, the subsequent steps required to use these files to configure or modify FSW operation depend on the category of file.

## Secondary Boot Code

FSW uses a two-stage boot process. During primary boot, the RAD750 CPU board is initialized and a primary boot shell is provided to allow operators to issue a limited set of telecommands, review the outcome of the primary boot in boot housekeeping telemetry, and configure the upcoming secondary boot process. During secondary boot, the VxWorks RTOS is initialized and FSW application modules are loaded and initialized.

Primary boot code files stored in RAD750 SUROM cannot be modified.

Secondary boot code files, the subject of this section, are stored in the Boot Objects Region of SIB EEPROM and can be modified.

The secondary boot code is fully described in [17].

### File List and Parameter Set

The secondary boot code file set is defined in Table 16 below.

| Table 16: Secondary Boot Code File Set |
| --- |
| Filename | FSW Package Name | Maximum size (Kbytes) | Parameters Specified |
| sbc_nominal.o | SBC | 4.5 (compressed) | N/A |

### File Format

As delivered by the ISOC FSW Team, a secondary boot code file is an ELF object module file, stripped by FMX of all unnecessary sections and symbols, GZIP compressed, and prefaced with a LAT File Header.

### Toolset

Secondary boot code files are developed and tested by ISOC’s FSW Team using the FSW development toolset: GCC for compilation, LTX for unit testing, SCP for integration testing, CMX for configuration management, and FMX for conversion to final object format, assignment of file identifier, and addition of LAT File Header.

### Related Files

The secondary boot code file set is independent of other FSW files. Should the secondary boot code be modified and uploaded, no other FSW files need be modified.

## RTOS Image Files

The RTOS image file set contains the VxWorks operating system library, which provides the core VxWorks functionality plus all FSW-specific board support functionality added by the FSW Team.

### File List and Parameter Set

The RTOS image file set is defined in Table 17 below.

| Table 17: RTOS Image File Set |
| --- |
| Filename | FSW Package Name | Maximum size (bytes) | Parameters Specified |
| vxw_flight.o | VXW | 220 | N/A |

### File Format

As delivered by the ISOC FSW Team, an RTOS image file is first built as an ELF object, then striped down to an absolute binary image to facilitate loading by the Primary Boot Code; after stripping, the file is GZIP compressed, and prefaced with a LAT File Header.

### Toolset

RTOS image files are developed and tested by ISOC’s FSW Team using the FSW development toolset: GCC for compilation, LTX for unit testing, SCP for integration testing, CMX for configuration management, and FMX for conversion to final object format, assignment of file identifier, and addition of LAT File Header.

### Related Files

The RTOS image file is independent of other FSW files.

## Secondary Boot Application Database Files

The secondary boot code is responsible for loading and initializing FSW application modules once the RTOS is operational. In order to do so, the secondary boot code for each flight SIU and EPU refers to an application database file, parsing this database file to identify which application object modules to initialize and run. Generally speaking, this application database consists of (1) a list of software object modules to load from the on-board EEPROM file systems and (2) a list of application initialization functions to call and the parameters that should be passed to them.

This application database file is uploaded to the Boot Objects region using file upload commands described in the Telecommand and Telemetry Formats Handbook [19].

### File List and Parameter Set

The secondary boot application database file set is defined in Table 18 below.

| Table 18: Secondary Boot Application Database File Set |
| --- |
| Filename | FSW Package Name | Maximum size (Kbytes) | Parameters Specified |
| TBD | SBC | TBD (small, ~ 5) | See Section ‎9.4.3 below. |

### File Format

As delivered by the ISOC FSW Team, a secondary boot application database file is an ELF object module file, stripped by FMX of all unnecessary sections and symbols, GZIP compressed, and prefaced with a LAT File Header.

### Toolset

The secondary boot application database is generated using a special-purpose tool from the SBC package: sbx. This tool reads an XML file specifying the contents of the application database and produces the ELF object binary file listed in Table 18 above.

The XML specification file and the resulting binary object are version controlled using CMX. The new application database binary object is integration tested using SCP.

The DTD for the XML document is version controlled in CMX. A detailed description of the DTD and an example file are presented in [17]. The parameters specified in this file are listed in Table 19 below.

| Table 19: Parameters Defined in the Secondary Boot Application XML Specification |
| --- |
| Field/Tag | Description | Parameters Specified |
| Modules | For each FSW application object module, defines which binary file to load. | FMX-(TBD) assigned master key CMX package name (e.g., “CCSDS”) CMX constituent name (e.g., “ccsds_pkt”) CMX package version (e.g., “V2-0-8”) EEPROM device location (e.g., ee0) EEPROM directory location (e.g., d00012) EEPROM file identifier (e.g., “05cc044”) |
| Functions | List of application initialization functions to call | Symbol name of function to call Parameters for the function call (0 to 4) |

### Related Files

Changes to the secondary boot application database must be coordinated with changes to the set of FSW code modules described in Section ‎9.5 on page 3.

## FSW Code Modules

The bulk of the FSW codebase is contained in the FSW code module file set, which contains all executable code except for the primary and secondary boot code. FSW code modules are stored in the File Region of EEPROM.

Some of these code modules are loaded and initialized by the secondary boot code once secondary boot is complete.

### File List and Parameter Set

The FSW code module file set for the initial mission software load is defined in Table 20 below. The “App Dbase?” column identifies the library modules that are listed in the secondary boot code application database and are thus loaded and initialized by the secondary boot code. Changes to these code modules in particular may necessitate changes in the secondary boot application database.

| Table 20: FSW Code Module File Set |
| --- |
| Filename | FSW Package Name | Description | Destination CPU | Size (bytes) | App Dbase? |
| libpbs.o | PBS | Processor Basic Services | SIU, EPU | TBD | No |
| liblhk.o | LHK | Housekeeping main system module | SIU | TBD | Yes |
| liblhk_slv | LHK | Housekeeping slave module | SIU, EPU | TBD | TBD |
| liblhk_cfg.o | LHK | Housekeeping config module | SIU, EPU | TBD | TBD |
| librad750_reboot.o | RAD750 |  | SIU, EPU | TBD | No |
| libcmx_asBuilt.o | CMX | Code versioning | SIU, EPU | TBD | No |
| libcmx_asBuiltSpy.o | CMX | Code versioning | SIU, EPU | TBD | No |
| libmsg_mt.o | MSG | Error messaging system | SIU, EPU | TBD | Yes |
| [[TBD: Full list available when Flight Unit candidate released for testing]] | TBD | TBD | TBD | TBD | TBD |

### File Format

As delivered by the ISOC FSW Team, each file in the FSW code module file set is an ELF object module file, stripped by FMX of all unnecessary sections and symbols, GZIP compressed, and prefaced with a LAT File Header.

### Toolset

FSW code modules are developed and tested by ISOC’s FSW Team using the FSW development toolset: GCC for compilation, LTX for unit testing, SCP for integration testing, CMX for configuration management, and FMX for conversion to final object format, assignment of file identifier, and addition of LAT File Header.

### Related Files

If a code module is loaded and initialized by the secondary boot code, changes to it may require corresponding changes to the secondary boot application database file (see Section ‎9.4 on page 3).

In addition, changes to code modules may necessitate changes in the corresponding software configuration file (see Section ‎9.6 on page 3).

## Software Configuration Files

Every FSW code module that, when loaded into memory, spawns an active task has a corresponding software configuration file that defines the taskID, task priority in VxWorks, and the memory resources dedicated to that task.

### File List and Parameter Set

The software configuration file set is defined in Table 21 below.

| Table 21: Software Configuration File Set |
| --- |
| Filename | FSW Package Name | Max size (Kbytes) | Parameters Specified |
| TBD [[soft. config for Houskeeping]] | LHK | TBD (~1) | Task ID, Task Priority, Allocated Memory |
| TBD [[soft. config for Thermal Control]] | LTC | TBD (~1) | Task ID, Task Priority, Allocated Memory |
| TBD: [[Full list available when Flight Unit candidate released for testing]] | TBD | TBD (~1) | Task ID, Task Priority, Allocated Memory |

### File Format

As delivered by the ISOC FSW Team, each file in the software configuration file set is an ELF object module file, stripped by FMX of all unnecessary sections and symbols, GZIP compressed, and prefaced with a LAT File Header.

### Toolset

Secondary configuration files are developed and tested by ISOC’s FSW Team using the FSW development toolset: GCC for compilation, LTX for unit testing, SCP for integration testing, CMX for configuration management, and FMX for conversion to final object format, addition of onboard file headers, and assignment of file identifiers.

### Related Files

If the FSW is upgraded and new FSW application code modules are developed, new software configuration files may be generated.

## Application Configuration Files

The operation of five FSW subsystems can be adjusted using special-purpose application configuration files. These subsystems are:

Housekeeping

Thermal Control

Instrument Physics

Charge Injection Calibration

Diagnostics Framework

### Housekeeping System Configuration Files

The LAT Housekeeping tasks are configured to collect and respond to health and status data based on a set application configuration files stored on the LAT file system.  The configuration files contain the acquisition enabling, packet delivery and acquisition schedule, limit check enabling, and limit value tables. The files can be interchanged via 1553  telecommmands.

Housekeeping configuration is discussed in detail in [32].

#### File List and Parameter Set

The Housekeeping configuration file set is defined in Table 22 below.

| Table 22: Housekeeping Configuration File Set |
| --- |
| Filename | FSW Package Name | Max size (bytes) | Parameters Specified |
| TBD [[acquisition schedule enabling config file]] | LHK | TBD | Mask values describing which values to collect. See Section ‎9.7.1.3 below. |
| TBD [[acquisition enable config file]] | LHK | TBD | Acquisition opcode and apid sequences and the acquisition schedule period. See Section ‎9.7.1.3 below. |
| TBD [[limit table values config file]] | LHK | TBD | Contains threshold values for limit checking. See Section ‎9.7.1.3 below. |
| TBD [[limit table enabling config file]] | LHK | TBD | Contains mask values describing which value to limit check. See Section ‎9.7.1.3 below. |

#### File Format

As delivered by the ISOC FSW Team, each file in the Housekeeping application configuration file set is an ELF object module file, stripped by FMX of all unnecessary sections and symbols, GZIP compressed, and prefaced with a LAT File Header.

#### Toolset

The contents of each housekeeping configuration file are defined in an XML file. These XML files are validated and converted to the ELF format described above by the Python-based lhk_config tool.

The XML specification files and the resulting binary objects are version controlled using CMX. The new application database binary object is integration tested using SCP. LAT File Headers are added by FMX.

The DTD for the XML document is version controlled in CMX. A detailed description of the DTD and an example file are presented in [32]. The parameters specified in this file are listed in Table 32 below.

| Table 23: Parameters Defined in the Housekeeping Configuration XML Specification |
| --- |
| File | Field/Tag | Sub-Field/Tag | Parameter(s) Specified |
| Acquisition and packet delivery schedule file | <sched_cfg> | <pkt_sched> | Housekeeping packet delivery sequence, by APID |
|  |  | <acq_sched> | * Collection schedule period (from 32 to 100 milliseconds) * Opcode defining the order in which Housekeeping data is collected |
| Acquisition schedule enabling file | <sch_enab_cfg> | <tem_adc_enab id=’0’> | This tag specifies a 16 bit mask describing which TEMs are enabled for acquisition of environmental data for a given mux channel. A value of 0xffff signifies enabling of all 16 TEMs. 5 tem_adc_enab tags are required to describe each mux channel. Each tag requires an id attribute to specify the mux channel id. |
|  |  | <tem_adc_enab id=’1’> | See above. |
|  |  | <tem_adc_enab id=’2’> | See above. |
|  |  | <tem_adc_enab id=’3’> | See above. |
|  |  | <tem_adc_enab id=’4’> | See above. |
|  |  | <tem_lrs_enab> | This tag specifies a 16 bit mask describing which tems are enabled for acquisition of low-rate science data. A value of 0xffff signifies enabling of all 16 TEMs. |
|  |  | <aem_adc_enab> | This tag specifies a 13 bit mask describing which AEM FREE boards are enabled for acquisition of environmental data. A value of 0x1fff signifies enabling of all free boards. |
|  |  | <pdu_adc_enab> | This tag specifies a 16 bit mask describing which of the 8 PDU environmental groups are enabled for both PDU0 and PDU1. The top 8 bits are for pdu1 and the lower 8 bits are PDU0. |
|  |  | <pdu_reg_enab> | This tag specifies a 2 bit mask describing which of the two PDUs are enabled for acquisition of the power status registers. |
|  |  | <gem_lrs_enab> | This tag specifies a 4 bit mask signifying the enable status of each of the GEM low-rate science counters. bit 0 – Livetime, bit 1 – Prescaled, bit 2 – Discarded, bit 3 - Sent |
|  |  | <comm_stat_enab> | This tag specifies a one bit enable status of the communication statistics read from ITC. |
|  |  | <file_stat_enab> | This tag specifies a 4 bit mask signifying the enable status of the file statistics for each CPU. bit 0 – SIU, bit 1 - EPU0, bit 2 - EPU1, bit 3 - EPU2 |
| Limit table values file | See [32] | See [32] | See [32] |
| Limit table enabling file | See [32] | See [32] | See [32] |

### Thermal Control System Configuration Files

[[Summary]]

#### File List and Parameter Set

The Thermal Control System configuration file set is defined in Table 22 above.

| Table 24: Thermal Control System Configuration File Set |
| --- |
| Filename | FSW Package Name | Max size (bytes) | Parameters Specified |
| TCSScript.txt | LTC | TBD | TCS master configuration file. Identifies pathname for all sub-files used in the configuration. |
| TCSSnsrs.o | LTC | TBD | [[TBD: Sensor to ADC mapping, set of sensors to read, set of sensors to use in thermal control algorithm]] |
| TCSCfg.o | LTC | TBD | [[TBD: Heat pipe control data]] |
| RTCNVxx.o | LTC | TBD | [[TBD: RIT count-to-temp conversion table]] |
| RSCNVxx.o | LTC | TBD | [[TBD: RSVR count-to-temp conversion table]] |
| RTFLTxx.o | LTC | TBD | [[TBD: RIT smoothing filter definition]] |
| RSFLTxx.o | LTC | TBD | [[TBD: RSVR smoothing filter definition]] |

#### File Format

As delivered by the ISOC FSW Team, other than the TCSScript.txt file, each file in the Thermal Control System configuration file set is an ELF object module file, stripped by FMX of all unnecessary sections and symbols, GZIP compressed, and prefaced with a LAT File Header. The sole text file in the set, TCSScript.txt, is also prepended with a LAT File Header.

#### Toolset

Thermal control system files are developed and tested by ISOC’s FSW Team using the FSW development toolset: GCC for compilation, LTX for unit testing, SCP for integration testing, CMX for configuration management, and FMX for conversion to final object format, addition of onboard file headers, and assignment of file identifiers.

### Instrument Physics Configuration Files

The LAT Physics Acquisition application is a highly configurable subsystem. Filter algorithms, filter settings, and GRB detection criteria are all modifiable, though modifications are likely to be rare. Trigger settings, determined by the contents of instrument configuration files (see Section ‎9.8 on page 3), also affect LPA operations.

#### Filter Algorithm File

The filter algorithm file defines the trigger discriminator, energy level, and track projection tests used to filter event data. The filter algorithm file set is defined in Table 25 below.

| Table 25: Instrument Physics Filter Algorithm File Set |
| --- |
| Filename | FSW Package Name | Max size (bytes) | Parameters Specified |
| TBD | LPA | TBD | N/A |

The following 16 filter tests are currently encoded in the filter algorithm file.

TEST1: Veto tile response; no CAL LO (trigger discriminator test).

TEST2: ACD splash veto, pass 0 (trigger discriminator test).

TEST3: Veto tile response; CAL energy < 350 MeV (energy level test).

TEST4: Any ACD tile response; CAL energy < 10 MeV (energy level test).

TEST 5: ACD Splash Veto (pass 1) (energy level test).

TEST 6: TKR tower match with ACD top tile (energy level test).

TEST 7: TKR tower match with ACD side tile (energy level test).

TEST 8: No connection between CAL energy and TKR (pass 0) (energy level test)

TEST 9: CAL layer 0 energy < 1 percent of total (energy level test).

TEST 10: CAL layer 0 energy > 90 percent of total (energy level test).

TEST 11: CAL crystal ratio (energy level test).

TEST 12: No projections (track projection test).

TEST 13: TKR/ACD matching (track projection test)

TEST 14: Track(s) project into skirt (track projection test)

TEST 15: CAL energy < 350 MeV; fewer than two tracks (track projection test)

TEST 16: Albedo Gamma-ray rejection (track projection test)

As delivered by the ISOC FSW Team, the filter algorithm file is an ELF object module file, stripped by FMX of all unnecessary sections and symbols, GZIP compressed, and prefaced with a LAT File Header.

The filter algorithm file is developed and tested by ISOC’s FSW Team using the FSW development toolset: GCC for compilation, LTX for unit testing, SCP for integration testing, CMX for configuration management, and FMX for conversion to final object format, addition of onboard file headers, and assignment of file identifiers.

If filter algorithms are added to or removed from the compiled filter algorithm file, corresponding changes to filter configuration file will be required.

#### Filter Configuration Files

Each filter configuration file uses a 32-bit mask to define which of the 16 filter tests (trigger discriminator, energy level, and track projection) are currently used to filter event data. These 16 tests can be considered 16 filter “channels”. In normal operations, not all events failing a particular test are discarded; a low-rate sample of rejected events is included in the event data telemetry.

The 32 bits of the bitmask are broken into 16 pairs. The first bit of each pair specifies whether the filter channel is closed or open. The second bit defines the rate at which the filter channel allows events which would normally be discarded due to application of that test to be included into the event data stream. The structure of the 32 bit object is shown in

Figure 12: Structure of the 32bit Event Filter Configuration Mask (TBD)

The filter algorithm file set for the initial mission load is defined in Table 25 above.

| Table 26: Instrument Physics Filter Algorithm File Set |
| --- |
| Filename | FSW Package Name | Max size (bytes) | Parameters Specified |
| File#1 TBD | LPA | [32 bits + header] | [specify which tests |

As delivered by the ISOC FSW Team, each filter configuration file is an ELF object module file, stripped by FMX of all unnecessary sections and symbols, GZIP compressed, and prefaced with a LAT File Header.

The filter configuration files are developed and tested by ISOC’s FSW Team using the FSW development toolset: GCC for compilation, LTX for unit testing, SCP for integration testing, CMX for configuration management, and FMX for conversion to final object format, addition of onboard file headers, and assignment of file identifiers.

If filter algorithms are added to or removed from the compiled filter algorithm file, corresponding changes to filter configuration files will be required.

#### GRB Detection Criteria Files

[TBD]

#### Data Compression Table Files

Event data can be batch compressed, as discussed in Section ‎7.2.3 on page 3. Compression tables used to define the encoding for the TKR, CAL, and ACD data are stored in EEPROM. The file set used to store this data is defined in Table 27 below.

| Table 27: Instrument Physics Data Compression Table File Set |
| --- |
| Filename | FSW Package Name | Max size (bytes) | Parameters Specified |
| TBD [[TKR data compression table]] | LPA | TBD | [TBD] |
| TBD [[CAL data compression table]] | LPA | TBD | [TBD] |
| TBD [[ACD data compression table]] | LPA | TBD | [TBD] |
| TBD [[misc. event data compression table]] | LPA | TBD | [TBD] |

As delivered by the ISOC FSW Team, each data compression table file is an ELF object module file, stripped by FMX of all unnecessary sections and symbols, GZIP compressed, and prefaced with a LAT File Header.

The data compression table file is developed and tested by ISOC’s FSW Team using the FSW development toolset: GCC for compilation, LTX for unit testing, SCP for integration testing, CMX for configuration management, and FMX for conversion to final object format, addition of onboard file headers, and assignment of file identifiers.

#### Filter Geometry File

The filter geometry file defines the tower geometry parameters used by the LPA filter (TBD). The filter geometry file set is defined in Table 25 above.

| Table 28: Instrument Physics Filter Geometry File Set |
| --- |
| Filename | FSW Package Name | Max size (bytes) | Parameters Specified |
| TBD | LPA | TBD | [TBD] |

As delivered by the ISOC FSW Team, the filter geometry file is an ELF object module file, stripped by FMX of all unnecessary sections and symbols, GZIP compressed, and prefaced with a LAT File Header.

The filter geometry file is developed and tested by ISOC’s FSW Team using the FSW development toolset: GCC for compilation, LTX for unit testing, SCP for integration testing, CMX for configuration management, and FMX for conversion to final object format, addition of onboard file headers, and assignment of file identifiers.

Changes to the geometry file may necessitate changes to the filter algorithm file.

#### ACD, TKR, and CAL Constants File (Pedestals and Gains)

[[TBD. 3 files containing pedestals and gains for the ACD, TKR, can CAL hardware. Updated as calibrations are performed and pedestals and gain settings must be adjusted]]

### Calibration Configuration Files

#### File List and Parameter Set

[[2 types of files required: (1) instrument configuration file(s) to set up based configuration of AEM (common controller, GARC, and GAFE registers), TEM (GCFE, GTIC, GTFE registers), and GEM; (2) calibration configuration file to define number of major/minor cycles, pulse levels, thresholds, etc.]]

The calibration configuration file set is defined in Table 29 below.

| Table 29: Calibration Configuration File Set |
| --- |
| Filename | FSW Package Name | Maximum size (bytes) | Parameters Specified |
| TBD (ACD Calibration configuration file) | LCI | TBD | Threshold-related register reconfigurations for each calibration loop |
| TBD (CAL Calibration configuration file) | LCI | TBD | TBD |
| TBD (TKR Calibration config file) | LCI | TBD | TKR Trigger Check: (1) 1 channel per GTRC to loop through, (2) Pulse to inject, threshold |
| TBD (TKR TOT parameter file:) | LCI | TBD | Parameters: 1) # of pulse points, 2) # of samples to collect for each data point |
| TBD (TKR Threshold Scan parameter file) | LCI | TBD | Parameters: 1) # of threshold points, 2) their threshold values, 3) # of samples collected per threshold point, 4) calibration DAC for each GTFE |

#### File Format

[[TBD: Likely binary ELF object]]

#### Toolset

TBD.

#### Related Files

TBD.

### Diagnostics Framework Configuration Files

#### File List and Parameter Set

[[TBD]]

The diagnostics “plug-in” file set is defined in Table 18 above.

| Table 30: LAT Diagnostics Framework Configuration File Set |
| --- |
| Filename | FSW Package Name | Maximum size (bytes) | Parameters Specified |
| TBD | LDF | TBD | TBD |
| TDB | LDF | TBD | TBD |

#### File Format

[[TBD]]

#### Toolset

[[TBD]]

#### Related Files

[[TBD]]

## Instrument Configuration Files

FSW provides a package, LATC, to define the configuration of the entire LAT instrument. LATC represents the instrument configuration using a set of XML files, converted into binary format by LATC tools on the ground, stored in EEPROM (or uploaded during the mission as new configurations are identified), unpacked by LATC on orbit, and used to set the actual hardware registers on the LAT. The opposite pathway is also available: onboard, LATC reads the instrument configuration, then packages the configuration data as a binary file, which can be downloaded for analysis.

The number of LAT registers is, to say the least, large. These registers are grouped into different subsystems by functionality. LATC’s XML-based instrument configuration files are likewise grouped by subsystem. LATC allows instrument configurations to be mixed and matched: a master file identifies the filepath to the particular subsystem configuration files of interest.

As discussed in [33], LAT registers can be divided into four categories

1.	Read-only. There are various statistics registers or ADC interface registers of the LAT that are read-only. These registers cannot be set by LATC  and their state is not recorded by LATC.

2.	One-time write (or static). There are several registers of the LAT that have one, and only one, correct setting. For example, the various timeouts and delays of the TEM, EBM, TCC and CCC. These registers are configured by FSW during start-up and are not modified or recorded by LATC.

3.	Process driven (or contextual). Some registers are implicitly set when a command is issued to the LAT. For example, the CRU registers, the PDU registers and the address registers of the various LATp nodes are set when a command is sent to the LAT instructing it to power a node and add it to the LAT command and response fabric. Other registers in this category might be the charge injection DACs that are used during calibration. These registers are not modified or recorded by LATC.

4.	Everything else (dynamic). The remaining registers can be used to enable and disable portions of the detector, or configure the trigger.

LATC is concerned only with the last group of registers.

Before launch, a large set of configuration files will be preloaded into EEPROM. The configurations defined in these files will be chosen based on the experience gained with the LAT and with the FSW during the integration and test process.

### File List and Parameter Set

The instrument configuration file set is defined in Table 31 below.

| Table 31: Instrument Configuration File Set |
| --- |
| Filename | FSW Package Name | Maximum size (bytes) | Parameters Specified |
| TBD (master file) | LATC | TBD | [[TBD: |
| TBD (file for GEM) | LATC | TBD | See ‎9.8.3 below. |
| TBD (file for AEM) | LATC | TBD | See ‎9.8.3 below. |
| TBD (file for TEMs) | LATC | TBD | See ‎9.8.3 below. |
| TBD (files for additional subsystems) | LATC | TBD | See ‎9.8.3 below. |

### File Format

As delivered by the ISOC FSW Team, aside than the configuration master files, instrument configuration files are ELF object module files, stripped by FMX of all unnecessary sections, GZIP compressed, and prefaced with a LAT File Header. Instrument configuration master files are text files.

### Toolset

Instrument configuration files are generated using a special-purpose command-line tool from the LATC package: lat_parser. This tool reads an XML file specifying the register settings that define a particular configuration and produces the ELF object binary file listed above.

Master files are produced by hand (TBD).

The XML instrument configuration file and the resulting binary object are version controlled using CMX. The new instrument configurations are tested on the FSW Testbed. FMX is used to prepend the LAT File Header to each file in the set.

The DTD for the instrument configuration XML file is version controlled in CMX. A complete description of the DTD and example XML files are presented in [33]. Valid settings for the registers defined in the instrument configuration files are defined in [[hardware ICDs]].

The tag hierarchy used in the XML file are shown in Table 32 below.

| Table 32: Parameters Defined in the Instrument Configuration XML Specification |
| --- |
| Tag | Sub-tag | Parameters Specified |
| GEM | TAM (Trigger Accept Message) | engine0-15 (prescale, inhibit, calstrobe, tack, four_range, zero_suppress, marker, destination) |
|  | ROI (Region of Interest) | rxxx_yyy |
|  | TIE (Trigger Input Enable) | towers x 4 groups (register) acd_cno((register) tiles x 12 groups (register) tower_busy (register) |
|  | SCH (Scheduler) | conditions x 16 (register) |
|  | WIN (Window) | win_width (register, width) |
| AEM | pha_enable_0 | register |
|  | pha_enable_1 | register, enable |
|  | veto_enable_0 | register |
|  | veto_enable_1 | register, enable |
|  | veto_delay | register, delay |
|  | HVBS | register, hv |
|  | HVSAA | register, hv |
|  | hold_delay | register, delay |
|  | veto_width | register, width |
|  | hitmap_width | register, width |
|  | hitmap_deadtime | register, deadtime |
|  | hitmap_delay | register, delay |
|  | pha_threshold_0-17 | register |
|  | ACDTACQ | register, adc |
|  | AFE (many) | afe_configuration (register, HLD_discriminator, veto_descriminator, range_select, PHA_range) |
| TEM (per TEM) | data_masks | register, cal_mask, tkr_mask |
|  | cal_trgseq | register, cal_cal_strobe, cal_TACK |
|  | tkr_trgseq | register, tkr_cal_strobe, tkr_TACK |
|  | TIC (many) | cal_input_mask (register, low_energy, high_energy) , tkr_layer_0 (register, layer) ,tkr_layer_1 (register, layer), tkr_output_mask (register, output_mask) |
|  | CCC (many) | layer_mask_0 (register, pos_log_mask, pos_le_mask, pos_he_mask, neg_log_mask, neg_le_mask, neg_he_mask) layer_mask_1(register, pos_log_mask, pos_le_mask, pos_he_mask, neg_log_mask, neg_le_mask, neg_he_mask) ccc_configuration (register, data_fifo, error_fifo, sum_diag_fifo) ccc_trg_align (register, prim_align, shape_time) event_timeouts(register, range_delay) CRC (many) |
|  | TCC (many) | tcc_input_mask (register, trigger_mask, mask) tcc_configuration(register, cable_length, summary_full, error_full, data_full) tcc_trg_align (register, shape_time, prim_align) TRC (many) |
|  | SPT (many) | low high TFE* |

### Related Files

Instrument configuration files are used by the LAT Calibration, LAT Physics Acquisition, and LAT Diagnostics Framework applications, along with other configuration files specific to those applications.

# Appendix A: LAT Register List

The following table lists all LAT hardware registers, indicating which are D=Dynamic (process-driven), S=Static (write-once), RO=Read-Only, and C=Contextual from the point of view of the FSW LATC application.

| Table 33: LAT Register List |
| --- |
| Component | Register | N | Bits | Comment | Type | XML |
| GAEM | CONFIGURATION | 1 | 1 | Even Parity (internal commands) | C |  |
| GAEM | CONFIGURATION | 1 | 1 | Even Parity (response) | C |  |
| GAEM | CONFIGURATION | 1 | 1 | Event Parity (event) | C |  |
| GAEM | CONFIGURATION | 1 | 12 | Data Masking | D |  |
| GAEM | CONFIGURATION | 1 | 8 | Version | RO |  |
| GAEM | COMMON_STATUS | 1 | 1 | Trigger Message Parity Error | RO |  |
| GAEM | COMMON_STATUS | 1 | 1 | Command Parity Error | RO |  |
| GAEM | COMMON_STATUS | 1 | 1 | Command Prefix Parity Error | RO |  |
| GAEM | COMMON_STATUS | 1 | 16 | Event Statistics | RO |  |
| GAEM | CABLE_STATUS | 1 | 2 | FREE 0 | RO |  |
| GAEM | CABLE_STATUS | 1 | 2 | FREE 1 | RO |  |
| GAEM | CABLE_STATUS | 1 | 2 | FREE 2 | RO |  |
| GAEM | CABLE_STATUS | 1 | 2 | FREE 3 | RO |  |
| GAEM | CABLE_STATUS | 1 | 2 | FREE 4 | RO |  |
| GAEM | CABLE_STATUS | 1 | 2 | FREE 5 | RO |  |
| GAEM | CABLE_STATUS | 1 | 2 | FREE 6 | RO |  |
| GAEM | CABLE_STATUS | 1 | 2 | FREE 7 | RO |  |
| GAEM | CABLE_STATUS | 1 | 2 | FREE 8 | RO |  |
| GAEM | CABLE_STATUS | 1 | 2 | FREE 9 | RO |  |
| GAEM | CABLE_STATUS | 1 | 2 | FREE 10 | RO |  |
| GAEM | CABLE_STATUS | 1 | 2 | FREE 11 | RO |  |
| GAEM | COMMAND_RESPONSE | 1 | 16 | Command Statistics | RO |  |
| GAEM | COMMAND_RESPONSE | 1 | 16 | Response Statistics | RO |  |
| GAEM | TRGSEQ | 1 | 8 | TACK Delay | S |  |
| GAEM | TRGSEQ | 1 | 4 | CALSTROBE Delay | S |  |
| GAEM | POWER_MANAGEMENT | 1 | 1 | FREE 0 | C |  |
| GAEM | POWER_MANAGEMENT | 1 | 1 | FREE 1 | C |  |
| GAEM | POWER_MANAGEMENT | 1 | 1 | FREE 2 | C |  |
| GAEM | POWER_MANAGEMENT | 1 | 1 | FREE 3 | C |  |
| GAEM | POWER_MANAGEMENT | 1 | 1 | FREE 4 | C |  |
| GAEM | POWER_MANAGEMENT | 1 | 1 | FREE 5 | C |  |
| GAEM | POWER_MANAGEMENT | 1 | 1 | FREE 6 | C |  |
| GAEM | POWER_MANAGEMENT | 1 | 1 | FREE 7 | C |  |
| GAEM | POWER_MANAGEMENT | 1 | 1 | FREE 8 | C |  |
| GAEM | POWER_MANAGEMENT | 1 | 1 | FREE 9 | C |  |
| GAEM | POWER_MANAGEMENT | 1 | 1 | FREE 10 | C |  |
| GAEM | POWER_MANAGEMENT | 1 | 1 | FREE 11 | C |  |
| GAEM | ADDRESS | 1 | 5 | Address | C |  |
| GAEM | TIMEOUT | 1 | 16 | EVT Timeout | S |  |

| Component | Register | N | Bits | Comment | Type | XML |
| --- | --- | --- | --- | --- | --- | --- |
| GARC | VETO_DELAY | 12 | 5 | Veto Delay | S |  |
| GARC | RQST_HVBS | 12 | 12 | HVBS | S |  |
| GARC | RQST_SAA | 12 | 12 | SAA | S |  |
| GARC | HVBS | 12 | 12 |  | RO |  |
| GARC | HVSAA | 12 | 12 |  | RO |  |
| GARC | HOLD_DELAY | 12 | 7 | Hold delay | S |  |
| GARC | VETO_WIDTH | 12 | 3 | Veto width | S |  |
| GARC | HITMAP_WIDTH | 12 | 4 | Hit-map width | S |  |
| GARC | HITMAP_DEADTIME | 12 | 3 | Hit-map dead-time | S |  |
| GARC | LOOK_AT_ME | 12 | 1 | Interface A/B enable | C |  |
| GARC | HITMAP_DELAY | 12 | 5 | Hit-map delay | S |  |
| GARC | PHA_EN0 | 12 | 16 | PHA Readout Enable | D |  |
| GARC | VETO_EN0 | 12 | 16 | VETO Enable | D |  |
| GARC | PHA_EN1 | 12 | 2 | PHA Readout Enable | D |  |
| GARC | VETO_EN1 | 12 | 2 | VETO Enable | D |  |
| GARC | MAX_PHA | 12 | 5 | Max PHA to send | D |  |
| GARC | MODE | 12 | 1 | Return Data Parity | C |  |
| GARC | MODE | 12 | 3 | HVBS A Enable | C |  |
| GARC | MODE | 12 | 3 | HVBS B Enable | C |  |
| GARC | MODE | 12 | 1 | Parity for GAFE | C |  |
| GARC | MODE | 12 | 1 | AEM A Veto Outputs | C |  |
| GARC | MODE | 12 | 1 | AEM B Veto Outputs | C |  |
| GARC | MODE | 12 | 1 | Test pin mux | C |  |
| GARC | MODE | 12 | 1 | Return Data Edge | C |  |
| GARC | STATUS | 12 | 6 | Status bits | RO |  |
| GARC | LAST_CMD | 12 | 16 | Cmd/data from last cmd error | RO |  |
| GARC | DIAGNOSTIC | 12 | 16 | Diagnostic information | RO |  |
| GARC | CMD_REJECT | 12 | 8 | Number of rejected cmds | RO |  |
| GARC | FREE_ID | 12 | 8 | Hardwired board serial number | RO |  |
| GARC | GARC_VERSION | 12 | 3 | Version of GARC chip | RO |  |
| GARC | PHA_THRESHOLD_0…17 | 12 | 12 | PHA must exceed all thresholds | S |  |
| GARC | ADC_TACQ | 12 | 6 | Additional time from Hold to ADC | D |  |

| Component | Register | N | Bits | Comment | Type | XML |
| --- | --- | --- | --- | --- | --- | --- |
| GAFE | CONFIGURATION | 216 | 1 | TCI Regular Gain | C |  |
| GAFE | CONFIGURATION | 216 | 1 | PHA Range Mode | D |  |
| GAFE | CONFIGURATION | 216 | 1 | Range Select | D |  |
| GAFE | CONFIGURATION | 216 | 1 | Veto Disc Enable | D |  |
| GAFE | CONFIGURATION | 216 | 1 | HLD Disc Enable | D |  |
| GAFE | CONFIGURATION | 216 | 1 | TCI High Gain | C |  |
| GAFE | VETO_DAC | 216 | 6 | Veto DAC | D |  |
| GAFE | HLD_DAC | 216 | 6 | HLD DAC | D |  |
| GAFE | LLD_DAC | 216 | 6 | LLD DAC | D |  |
| GAFE | BIAS_DAC | 216 | 6 | Bias DAC | D |  |
| GAFE | TCI_DAC | 216 | 6 | Test Charge Inj Level | C |  |
| GAFE | VERS_ADDRESS | 216 | ND | Version Number | RO |  |
| GAFE | WRITE_CTR | 216 | ND | Number of write cmds | RO |  |
| GAFE | REJECT_CTR | 216 | ND | Number of rejected cmds | RO |  |
| GAFE | LOOP_CTR | 216 | ND | Number of cmds | RO |  |
| GAFE | CHIP_ADDR | 216 | ND | GAFE chip address | RO |  |

| Component | Register | N | Bits | Comment | Type | XML |
| --- | --- | --- | --- | --- | --- | --- |
| GTIC | POWER_SUPPLY | 1 | 1 | Tracker | C |  |
| GTIC | POWER_SUPPLY | 1 | 1 | Calorimeter | C |  |
| GTIC | STATUS | 1 | 1 | Command Parity Error | RO |  |
| GTIC | CAL_IN_MASK | 1 | 8 | Low Energy Mask | D |  |
| GTIC | CAL_IN_MASK | 1 | 8 | High Energy Mask | D |  |
| GTIC | CAL_LRS_MASK | 1 | 8 | Low Energy Mask (counter 0) | C |  |
| GTIC | CAL_LRS_MASK | 1 | 8 | High Energy Mask (counter 0) | C |  |
| GTIC | CAL_LRS_MASK | 1 | 8 | Low Energy Mask (counter 1) | C |  |
| GTIC | CAL_LRS_MASK | 1 | 8 | High Energy Mask (counter 1) | C |  |
| GTIC | CAL_LRS_COUNTERS | 1 | 16 | Counter 0 | RO |  |
| GTIC | CAL_LRS_COUNTERS | 1 | 16 | Counter 1 | RO |  |
| GTIC | TKR_LAYER_ENABLE_0 | 1 | 18 | Layer Enable 0 | D |  |
| GTIC | TKR_LAYER_ENABLE_1 | 1 | 18 | Layer Enable 1 | D |  |
| GTIC | TKR_OUT_MASK | 1 | 16 | 3-in-a-row output mask | D |  |
| GTIC | TKR_OUT_LRS_MASK | 1 | 16 | Counter Mask | C |  |
| GTIC | TRK_LRS_COUNTER_0 | 1 | 16 | Lower Counter | RO |  |
| GTIC | TRK_LRS_COUNTER_0 | 1 | 16 | Upper Counter | RO |  |
| GTIC | TRK_LRS_COUNTER_1 | 1 | 16 | Lower Counter | RO |  |
| GTIC | TRK_LRS_COUNTER_1 | 1 | 16 | Upper Counter | RO |  |
| GTIC | BUSY_LRS_MASK | 1 | 1 | Tracker | C |  |
| GTIC | BUSY_LRS_MASK | 1 | 1 | Calorimeter | C |  |
| GTIC | BUSY_LRS_MASK | 1 | 1 | Total | C |  |
| GTIC | BUSY_LRS_COUNTER | 1 | 24 | Counter | RO |  |
| GTIC | MUX_CONFIG | 1 | 3 | Channel | C |  |
| GTIC | TKR_BIASDAC | 1 | 16 | Input Register | S |  |
| GTIC | TKR_BIASDAC | 1 | 1 | Valid | RO |  |
| GTIC | CAL_BIASDAC | 1 | 16 | Input Register | S |  |
| GTIC | CAL_BIASDAC | 1 | 1 | Valid | RO |  |

| Component | Register | N | Bits | Comment | Type | XML |
| --- | --- | --- | --- | --- | --- | --- |
| GTEM | CONFIGURATION | 1 | 1 | Use Redundant GEM | D |  |
| GTEM | CONFIGURATION | 1 | 1 | Use Redundant EBM | D |  |
| GTEM | CONFIGURATION | 1 | 1 | Parity Select (TKR TACK) | C |  |
| GTEM | CONFIGURATION | 1 | 1 | Parity Select (CAL Internal) | C |  |
| GTEM | CONFIGURATION | 1 | 1 | Parity Select (TKR Internal) | C |  |
| GTEM | CONFIGURATION | 1 | 1 | Parity Select (response) | C |  |
| GTEM | CONFIGURATION | 1 | 1 | Parity Select (event) | C |  |
| GTEM | CONFIGURATION | 1 | 1 | Parity Select (token) | C |  |
| GTEM | CONFIGURATION | 1 | 1 | Buffer Model Select | C |  |
| GTEM | CONFIGURATION | 1 | 1 | Trigger Buffer Select | C |  |
| GTEM | CONFIGURATION | 1 | 16 | Cable Controller Timeout | S |  |
| GTEM | DATA_MASKS | 1 | 1 | Diagnostic | C |  |
| GTEM | DATA_MASKS | 1 | 4 | Calorimeter | D |  |
| GTEM | DATA_MASKS | 1 | 8 | Tracker | D |  |
| GTEM | STATUS | 1 | 1 | Event Error | RO |  |
| GTEM | STATUS | 1 | 1 | Trigger Message Parity Error | RO |  |
| GTEM | STATUS | 1 | 1 | Tag Error | RO |  |
| GTEM | STATUS | 1 | 1 | Cable Error | RO |  |
| GTEM | STATUS | 1 | 1 | Timeout Error | RO |  |
| GTEM | STATUS | 1 | 1 | Command Parity Error | RO |  |
| GTEM | STATUS | 1 | 1 | Command Prefix Parity Error | RO |  |
| GTEM | STATUS | 1 | 1 | Parity Error "A" | RO |  |
| GTEM | STATUS | 1 | 1 | Parity Error "B" | RO |  |
| GTEM | STATUS | 1 | 1 | "B" Selected | RO |  |
| GTEM | STATUS | 1 | 6 | Version | RO |  |
| GTEM | STATUS | 1 | 16 | events (packets) sent | RO |  |
| GTEM | COMMAND_RESPONSE | 1 | 16 | Response Statistics | RO |  |
| GTEM | COMMAND_RESPONSE | 1 | 16 | Command Statistics | RO |  |
| GTEM | TKR_TRGSEQ | 1 | 4 | CAL_STROBE Delay | S |  |
| GTEM | TKR_TRGSEQ | 1 | 8 | TACK Delay | S |  |
| GTEM | CAL_TRGSEQ | 1 | 4 | CAL_STROBE Delay | S |  |
| GTEM | CAL_TRGSEQ | 1 | 8 | TACK Delay | S |  |
| GTEM | ADDRESS | 1 | 5 | Address | RO |  |

| Component | Register | N | Bits | Comment | Type | XML |
| --- | --- | --- | --- | --- | --- | --- |
| GCCC | CONFIGURATION | 4 | 1 | Controller output enable | C |  |
| GCCC | CONFIGURATION | 4 | 4 | Listen MSB | C |  |
| GCCC | CONFIGURATION | 4 | 6 | FIFO full cond. (summary/diagnostic) | S |  |
| GCCC | CONFIGURATION | 4 | 6 | FIFO full cond. (error) | S |  |
| GCCC | CONFIGURATION | 4 | 7 | FIFO full cond. (data) | S |  |
| GCCC | TRG_ALIGNMENT | 1 | 4 | Shaping Time | S |  |
| GCCC | TRG_ALIGNMENT | 1 | 4 | Primitive Alignment | S |  |
| GCCC | LAYER_MASK_0,1 | 4 | 56 | Layer Mask | D |  |
| GCCC | EVENT_TIMEOUTS | 4 | 10 | Timeout | S |  |
| GCCC | EVENT_TIMEOUTS | 4 | 10 | Range Delay | S |  |

| Component | Register | N | Bits | Comment | Type | XML |
| --- | --- | --- | --- | --- | --- | --- |
| GCRC | CSR | 16 | 4 | Status | RO |  |
| GCRC | LATC_CMD | 16 | 16 | Last Command | RO |  |
| GCRC | DELAY_1 | 16 | 6 | Time Delay Hold to RNG Decision | S |  |
| GCRC | DELAY_2 | 16 | 6 | Time Delay RNG Decision to Sample | S |  |
| GCRC | DELAY_3 | 16 | 8 | Time Delay ADC Conversion time | S |  |
| GCRC | DAC | 16 | 16 | DAC Setting | D |  |
| GCRC | CONFIGURATION | 16 | 16 | Configuration? | D |  |

| Component | Register | N | Bits | Comment | Type | XML |
| --- | --- | --- | --- | --- | --- | --- |
| GCFE | CONFIG_0 | 192 | 1 | Low energy gain select 0 | D |  |
| GCFE | CONFIG_0 | 192 | 1 | Low energy gain select 1 | D |  |
| GCFE | CONFIG_0 | 192 | 1 | Low energy gain select 2 | D |  |
| GCFE | CONFIG_0 | 192 | 1 | High energy gain select 0 | D |  |
| GCFE | CONFIG_0 | 192 | 1 | High energy gain select 1 | D |  |
| GCFE | CONFIG_0 | 192 | 1 | High energy gain select 2 | D |  |
| GCFE | CONFIG_0 | 192 | 1 | High energy gain select 3 | D |  |
| GCFE | CONFIG_0 | 192 | 1 | Low energy range enable | D |  |
| GCFE | CONFIG_0 | 192 | 1 | High energy range enable | D |  |
| GCFE | CONFIG_0 | 192 | 1 | Use first range | D |  |
| GCFE | CONFIG_0 | 192 | 1 | First range 0 | D |  |
| GCFE | CONFIG_0 | 192 | 1 | First range 1 | D |  |
| GCFE | CONFIG_0 | 192 | 1 | Overwrite | D |  |
| GCFE | CONFIG_1 | 192 | 1 | Log accept enable | D |  |
| GCFE | CONFIG_1 | 192 | 1 | Low Energy trigger enable | D |  |
| GCFE | CONFIG_1 | 192 | 1 | High Energy trigger enable | D |  |
| GCFE | CONFIG_1 | 192 | 1 | Calibration Gain | D |  |
| GCFE | CONFIG_1 | 192 | 1 | Calibration Low Energy Enable | D |  |
| GCFE | CONFIG_1 | 192 | 1 | Calibration High Energy Enable | D |  |
| GCFE | FLE_DAC | 192 | 7 | Low Energy TRG Disc | D |  |
| GCFE | FHE_DAC | 192 | 7 | High Energy TRG Disc | D |  |
| GCFE | LOG_ACPT | 192 | 7 | Log Accept Disc | D |  |
| GCFE | RNG_ULD_DAC | 192 | 7 | Range Select Disc | D |  |
| GCFE | REF_DAC | 192 | 7 | DAC for DC Reference | D |  |

| Component | Register | N | Bits | Comment | Type | XML |
| --- | --- | --- | --- | --- | --- | --- |
| GTCC | CONFIGURATION | 8 | 1 | Controller output enable | C |  |
| GTCC | CONFIGURATION | 8 | 4 | Cable Length | S |  |
| GTCC | CONFIGURATION | 8 | 6 | FIFO full cond. (summary/diagnostic) | S |  |
| GTCC | CONFIGURATION | 8 | 6 | FIFO full cond. (error) | S |  |
| GTCC | CONFIGURATION | 8 | 7 | FIFO full cond. (data) | S |  |
| GTCC | TRG_ALIGNMENT | 8 | 4 | Shaping Time | S |  |
| GTCC | TRG_ALIGNMENT | 8 | 4 | Alignment Delay | S |  |
| GTCC | INPUT_MASK | 8 | 1 | Disable Parity Check | C |  |
| GTCC | INPUT_MASK7 | 8 | 1 | Mask | D |  |
| GTCC | INPUT_MASK | 8 | 9 | Trigger Masks | D |  |
| GTCC | FIFO_STATUS | 8 | 3 | Diagnostic FIFO Signals | RO |  |
| GTCC | FIFO_STATUS | 8 | 3 | Error FIFO Signals | RO |  |
| GTCC | FIFO_STATUS | 8 | 3 | TOT FIFO Signals | RO |  |
| GTCC | FIFO_STATUS | 8 | 3 | Data FIFO Signals | RO |  |
| GTCC | FIFO_STATUS | 8 | 3 | Summary FIFO Signals | RO |  |
| GTCC | LATCHED_STATUS | 8 | 1 | Data Parity Error | RO |  |
| GTCC | LATCHED_STATUS | 8 | 1 | GTRC Summary Error | RO |  |
| GTCC | LATCHED_STATUS | 8 | 1 | Word Count Parity Error | RO |  |
| GTCC | LATCHED_STATUS | 8 | 1 | Header Parity Error | RO |  |
| GTCC | LATCHED_STATUS | 8 | 1 | Timeout Error | RO |  |
| GTCC | LATCHED_STATUS | 8 | 1 | FULL Error | RO |  |
| GTCC | LATCHED_STATUS | 8 | 1 | GTFE Tag Error | RO |  |
| GTCC | LATCHED_STATUS | 8 | 1 | GTRC Tag Error | RO |  |
| GTCC | LATCHED_STATUS | 8 | 1 | Command Parity Error | RO |  |
| GTCC | LATCHED_STATUS | 8 | 3 | Diagnostic FIFO Signals | RO |  |
| GTCC | LATCHED_STATUS | 8 | 3 | Error FIFO Signals | RO |  |
| GTCC | LATCHED_STATUS | 8 | 3 | TOT FIFO Signals | RO |  |
| GTCC | LATCHED_STATUS | 8 | 3 | Data FIFO Signals | RO |  |
| GTCC | LATCHED_STATUS | 8 | 3 | Summary FIFO Signals | RO |  |
| GTCC | EVENT_TIMEOUTS | 8 | 14 | EVT Timeout | S |  |

| Component | Register | N | Bits | Comment | Type | XML |
| --- | --- | --- | --- | --- | --- | --- |
| GTRC | CSR | 36 | 33 | CSR Register (status) | RO |  |
| GTRC | SYNCH | 36 | 5 | Synch Register | RO |  |

| Component | Register | N | Bits | Comment | Type | XML |
| --- | --- | --- | --- | --- | --- | --- |
| GTFE | DAC | 1728 | 7 | DAC | D |  |
| GTFE | DATA_MASK | 1728 | 64 | Data Mask | D |  |
| GTFE | TRIG_MASK | 1728 | 64 | Trigger Mask | D |  |
| GTFE | CALIB_MASK | 1728 | 64 | Calibration Mask | C |  |
| GTFE | MODE | 1728 | 2 | Mode | D |  |
| DAQ |  | 192 | 128 | Gain | D |  |

# Footnotes

Assumes pulsing at 10 kHz, 1 channel per TFE and 12 TFE per TRC; auto-range readout; no cross-talk measurement.

Assumes pulsing at 10 kHz, 1 channel per TFE and 12 TFE per TRC; no cross-talk measurement.

Assumes pulsing at 10 kHz

# Text boxes

Packet Telemetry Data

Test 1

Telemetry Packet

Header