Minutes of the LAT Operations Scenario Meeting with CAL

Held 7/14/04 at 11:00 PDT

Attendees:

Ernest Canevari, John Teter, Jim Martin, Jeff Fisher, Bill Craig, Lori Bator, Steve Culp, Mike DeKlotz, Eduardo do Couto e Silva, Neil Johnson, Eric Grove, Byron Leas

Operations Phases

- Suggested that we add a “Spectrum” phase to the I&T phases.

- No difference for CAL between the pointing and survey modes

LAT Commanding

- Testbed won’t be useful to verify CAL sensor commands because there aren’t detectors

  - Need a way to verify parsing of commands

  - Jeff Fisher action to see what response there is to FSW when commands are sent to CAL

Subsystem Operations

- L&EO

  - Functional tests to verify nothing broke or changed after launch

  - Exercise commands by running calibration activities and executing pre-loaded scripts

  - Comprehensive test

    - All 16 modules tested at turn-on stage

    - Each module test takes approximately 3 hours

  - Upload changes to tables – expect there to be some

  - Want to collect science as soon as possible to gather data

    - Look at spectra, occupancy etc with the full LAT operational and running

    - Individual module tests performed as needed

    - Make adjustments to baseline set of pedestals and thresholds

- Survey Mode/Pointed Observation Operations

  - Gather data, verify linearity

  - Calibration approximately a couple times a year

  - Nominal (baseline) set of pedestals and thresholds

    - I&T

    - CAL-triggered

    - Nominal science

    - Other LAT orbital modes

Scope of Commanding

- No daily or routine commanding

- Not a lot of commands sent from ground

  - Execute scripts from FSW to do commanding

    - Jeff Fisher action: need better coordination with JJ on the implementation of these scripts

    - CI for linearity, noise,

    - Threshold calibration

  - Every module has approx 1000 registers

  - File uploads to change tables may be needed

Special Requirements

- Can’t command CAL and collect science at same time

  - Triggers disabled – must be in quiescent mode to command

- Reconfiguration of entire system would take ~ 3500 commands

  - Unknown how large the file would be

- No dangerous or critical issues for CAL

- Need to define mode for CAL during SAA

  - Disable trigger during SAA

Possible Anomalies

- Degradation – change gain

- Thermal excursion – no thermal risk and no immediate response needed if temp changes

- Power failure – polyfuses are like thermostats and could chatter open/closed

- Noisy channel – file upload within a day or two

- Noisy trigger primitive – disable primitive or adjust threshold

Monitoring

- FSW monitors 28 volts and current to TEM

  - If FSW sees dropt in current to TEM, powers off CAL

  - Mike DeKlotz action to verify FSW monitoring requirement and action taken

- MOC only needs to monitor HK parameters (power, temp, some scalars)

  - Notify ISOC of limit violations and alerts

- Diagnostic data

  - Monitored by ISOC (beyond scope of MOC)

  - Implementation of diagnostic data depends on FSW

  - Some diagnostic data can be determined on the ground (not sure what this meant. Nneeds further detailed definition if ISOC is doing this)